## Slide 1
Custom Memory Cube
Yu Zou, Vinayak Deshpande, Herman Lam, Alan George
F3
MOTIVATION & GOAL
Goal: Create flexible research platform for design space exploration of CMC apps & arch. before existence of CMC
Motivation
Memory bottleneck – critical for memory-intensive Big Data apps
Promise of CMC for computational ram & processor-in-memory processing
DRAM
Layers
Logic Layer
CPU
HMC
Processor
Custom
Logic Layer
CPU
CMC
DRAM
Layers
PLANS FOR 2017
PHASE 2: Case Study
  Selected notional CMC model from published work
  Identified hardware parameters required by performance model
  Mapped measurement points to model parameters as required
  Task 2: Case studies to explore
    Notional CMC architectures
    CMC apps: DRE, Sorting, Bloom filter
    Characteristics of CMC-amenable apps
  Task 1: Platform development
    Develop library for customization of notional CMC architecture under study
    Explore CMC apps using HT
  Members e.g.,
APPROACH
  Phase 1: Prototype Platform
    Create CMC emulation platform using Convey’s FPGA-HMC platform (Merlin board)
  Phase 2: Case Study
    Select model of CMC
    Develop mapping from measured parameters to model parameters
    Perform design space exploration of CMC arch & CMC operations/apps
PHASE2: Initial Results
PHASE1: Initial Results
PHASE 1: Prototype Platform
  Observability
    Instrument Merlin infrastructure with hardware performance monitors (C’, D’, M1, M2, M3, M4, M5, and E’)
  Usability & Flexibility
    Implemented & measured kernels and apps using HT (Convey’s tool & language)
      Vector Addition (emulates DRE* fill operation)
      DRE app: SpMV
      *
Oper. | A’ (µs) | C’ | D’ | M1 | M2 | M3 | M4 | M5 | E’
Read | 1095.6 | 1.03 | 1.006 | 0.923 | 0.725 | 0.519 | - | - | -
Write | 1104.0 | 1.071 | 1.011 | 0.991 | 0.793 | 0.577 | - | - | -
A’ (ms) | C’ | D’ | M1 | M2 | M3 | M4 | M5 | E’
282.55 | 281.72 | 278.72 | 258.96 | 199.68 | 151.31 | - | - | -
A’ (s) | C’ | D’ | M1 | M2 | M3 | M4 | M5 | E’
1658.67 | 1580.14 | 1559.65 | 1460.57 | 1122.42 | 839.84 | - | - | -
Measured performance: Vector Addition in ms (100,000 iterations of 2 reads & 1 write)
Measured performance: SpMV – DRE app in seconds (224 X 224 matrix)
Measured performance: simple read/write (µs)
(Averaged over 100,000 iterations)
Merlin board
Case study: model of a notional CMC
CMC platform on Merlin board
Model of notional CMC
CMC platform on Merlin board
Model of notional CMC
CMC platform on Merlin board
*DRE: Data Reordering/Rearrangement Engine from LLNL