## Slide 1
Custom Memory Cube
S. Gundecha, R. J. Xavier, G. Wang, A. Lawande, H. Lam, A. George
PHASE 2: CMC PROTOTYPE
PHASE 1: MEMORY-MAPPED HMC
APPROACH
F3
MOTIVATION & GOAL
Goal: Explore new forms of parallel processing and memory architectures
  Exploit performance and power advantages of :
    Custom logic/memory stacks (e.g., HMC and variants)
    Computational memory (C-RAM) and processor in memory (PIM)
  Fully utilize HMC memory bandwidth and data locality
Motivation
Increasing need for faster and low-power parallel processing
Communication involved with data-intensive apps. consumes considerable time and power
DRAM
Layers
Logic Layer
CPU
HMC
Processor
Custom
Logic Layer
CPU
CMC
DRAM
Layers
RISC-V simulator (+HMC-Sim):
GC64 – Goblin core based on RISC-V ISA
HMC-Sim framework can be integrated into GC64
Supports HMC v.1.0, 2.0 in dev
SST: Support for gem5 simulator integration
VaultSimC simulator supports HMC
Framework supports wide variety of processors, memory simulators
gem5:
Supports SST integration
Supports x86, ARM64 (up to 8 cores)
Features detailed event-driven memory system
PLANS FOR 2016
  PHASE 1: Memory-mapped HMC
    HMC accessible as regular memory by host
    Enable access from host to HMC on FPGA/HMC board – hide PCIe, FPGA processing delays
    Measure & report HMC access time to host
  PHASE 2: CMC Prototype
    Explore processing capabilities on FPGA:
    Wide-shallow processors for data, simplified RISCV/ARM64 for control
    Evaluate CMC prototype via key apps
FPGA/HMC boards
  Convey Merlin board (MA-100)
  PICO EX500 board with AC510 modules
Processor testbeds
  ARM64: JUNO ARM development platform
  RISC-V: Rocket Core on Zedboard
Software simulators
  gem5
  Goblin core64
  SST
HMC/CMC TESTBEDS
  Task B: CMC prototyping
    Design-space exploration using software simulation and Task-A testbeds
    Develop CMC prototypes on FPGA & evaluate different designs based on key application requirements
  Task A: Memory-mapped HMC
    Enable HMC access from host
    Measure & report HMC access time
  Method 1: “Direct” HMC access from host via HIX* core on FPGA
    Use same virtual addresses for memory locations
    Independent of user app on FPGA
    Provided by Convey for Merlin board
  Method #2: Access HMC via user-built FPGA app from host
    Need to develop FPGA app
    Flexible functionality
    Higher performance
 | Convey Merlin | PICO AC-510
FPGA | Altera Arria 10 GX1150 | Xilinx Kintex Ultrascale 060
Logic Cells | 1150 K | 725 K
BRAM | 67 Mb | 38 Mb
Transceivers | 17.4 Gb/s (96) | 16.3 Gb/s (32)
DSPs | 3036 | 2760
HMC Links, Lanes per Link | 2, 16 | 2, 8
Bandwidth per Lane** | 10 Gb/s | 15 Gb/s
Bandwidth** | 40 GB/s | 30 GB/s
Capacity | 4 GB | 4 GB
PCI Gen | 3 | 3
Lanes | 8 | 8
Bandwidth** | 7.88 GB/s | 7.88 GB/s
Prog. Tools | HDLs & Convey HT* | HDLs & OpenCL
Date of avail. | Oct. 13, 2015 | Before end of 2015
  Custom memory cube with in-memory processing capability
  Ground work involves
  Choosing software simulators for design-space exploration
  Processor benchmarking with focus on memory bandwidth and power
  ARM64: Juno ADP – 6 core big.LITTLE architecture: 2 low-power consuming Cortex A53 cores, 4 high-performance Cortex A57 cores; 1.1GHz max. operating frequency
Chart: Average GUPS for 1 OpenMP vs 6 OpenMP threads
| 2^7 | 2^8 | 2^9 | 2^10 | 2^11 | 2^12 | 2^13 | 2^14 | 2^15 | 2^16 | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23 | 2^24 | 2^25 | 2^26 | 2^27 | 2^28
1OMP | 0.011228 | 0.014713 | 0.019468 | 0.022605 | 0.024066 | 0.023352 | 0.022383 | 0.024048 | 0.024441 | 0.024565 | 0.02438 | 0.024512 | 0.025358 | 0.025869 | 0.025917 | 0.025758 | 0.025955 | 0.025942 | 0.025945 | 0.025951 | 0.025938 | 0.025947
6OMP | 4.5e-05 | 8.9e-05 | 0.000179 | 0.000355 | 0.000706 | 0.001409 | 0.002585 | 0.005223 | 0.006032 | 0.008107 | 0.008758 | 0.009047 | 0.009057 | 0.009085 | 0.011089 | 0.0128 | 0.01475 | 0.015286 | 0.02097 | 0.030428 | 0.037424 | 0.038069
  RISC-V: Rocket Core – Emulated on Xilinx Zynq-7020 FPGA SoC Operating at 25MHz
  5 stage, in-order execution pipeline
Chart: GUPS : RISC-V vs ARM64 (varying field size)
| 2^10 | 2^11 | 2^12 | 2^13 | 2^14 | 2^15 | 2^16 | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23
RISCV | 0.028578 | 0.030341 | 0.031228 | 0.031188 | 0.032052 | 0.031788 | 0.016968 | 0.013643 | 0.012404 | 0.011881 | 0.011617 | 0.011493 | 0.011195 | 0.010566
ARM64 | 0.1201 | 0.10457 | 0.16547 | 0.11018 | 0.15073 | 0.11026 | 0.066458 | 0.047384 | 0.033473 | 0.027807 | 0.037411 | 0.028692 | 0.020929 | 0.01038
Chart: STREAM : RISC-V vs ARM Cortex A57 (Avg Rate MB/s)
| Copy | Scale | Add | Triad | Fill
RISCV | 1116.2 | 679.3 | 788.8 | 747.6 | 1543
ARM | 4665.5 | 4621.4 | 3921.2 | 3694.9 | 3794.7
CMC Prototype
  Processor Benchmarking
GUPS
- Host code taken from HPCC suite
- Modified host code to test both methods
Parameters
- Table/Field size : 216 – 229, 8-byte words
- Number of updates : 4 x table size
Power
- Measured for entire board Idle : ~54 Watts Busy : ~59 Watts
Log Scale graph
Initial Results
  Members e.g.,
Chart: Power Consumption for GUPS (mw)
| 1 | 2 | 4 | 6 | 8 | 12 | 16
A53 Aff | 118 | 163 | 190 | 182 | 191 | 191 | 192
A57 Aff | 587 | 686 | 692 | 687 | 685 | 713 | 674
No Aff | 575 | 691 | 683 | 715 | 707 | 730 | 731
Chart: Power Consumption for STREAM (mw)
| 1 | 2 | 4 | 6 | 8 | 10 | 12
A57 Aff. | 841 | 1146 | 1148 | 1138 | 1129 | 1109 | 1116
No Aff. | 832 | 1098 | 612 | 714 | 1055 | 1017 | 1016
Aff. A53 | 171 | 296 | 504 | 327 | 401 | 441 | 471
Chart: STREAM Multithreaded Execution – Avg Rate (MB/s)
| w/o OpenMP | 1 | 2 | 4 | 6 | 8 | 10 | 12
Dot(Read) | 8793.4 | 8786.8 | 11859.7 | 12865.5 | 12255.4 | 13885.1 | 12282.3 | 15610.3
Fill(Write) | 4396.8 | 4395.5 | 4574.1 | 5604.7 | 5070.8 | 5085.3 | 4983.8 | 5504.9
Add | 3785.5 | 3779.1 | 4105.5 | 4203.5 | 4552.1 | 4330.6 | 3942.1 | 3834.4
Triad | 3760.4 | 3837.5 | 4126.7 | 3939.2 | 4194.4 | 4832.5 | 4125.1 | 3729.4
Copy | 4765.9 | 4341.4 | 4785.6 | 5223 | 4530.3 | 5411.6 | 5174.5 | 5137.3
Scale | 4611.4 | 4298.4 | 4757.6 | 4388.3 | 4507.7 | 4753 | 4241.4 | 4205.2