## Slide 1
Custom Memory Cube
Gongyu Wang, Yu Zou, Herman Lam, Alan George
F3
MOTIVATION & GOAL
Goal: Create research platform to explore potential of custom logic layer for HMC
  Exploit performance advantage of :
    Custom logic/memory stacks (e.g., HMC and variants)
    Computational memory (C-RAM) and processor in memory (PIM)
  Fully utilize HMC memory bandwidth and data locality
Motivation
Communication involved with data-intensive apps. consumes considerable time
HMC has higher B/W than current memories
Lack of fully functional CMC research platform
DRAM
Layers
Logic Layer
CPU
HMC
Processor
Custom
Logic Layer
CPU
CMC
DRAM
Layers
PLANS FOR CAW16
TASK 2: Measurement on HMC
  Two measurement methods
    CPU measurement from view of host application
    FPGA measurement using PERFMON logic of Convey PDK
  Two running modes
    Host only
      CPU code directly accessing HMC
    CMC
      CMC computation on FPGA accessing HMC in highly parallel fashion
  Task 2: Measurement on HMC
    Enable performance monitor for DRE applications and validate results
    Enable power measurement of HMC device
  Task 1: CMC Prototype
    Explore DRE designs w/ memory-mapped view buffer in FPGA
    Continue study of DRE on Merlin and LPS-suggested CMC apps
  Members e.g.,
APPROACH
  Task 1: CMC Prototype
    Create initial prototype of CMC architecture using data reorder/rearrangement engine (DRE) of LLNL
    Study elaborate CMC designs using select apps
  Task 2: Measurement on HMC
    Develop test apps on FPGA-HMC platform (e.g., Merlin board)
    Enable perf. measurement on FPGA & study HMC w/ test apps
Developed and enabled multi-level performance measurement methods
Evaluated HMC bandwidth using GUPS and STREAM benchmarks
Initial Results
Testbed
Convey Merlin board (MA-100)
Benchmarks
GUPS
STREAM
Parameters
Table size: 216 ~ 229 , 8-byte words
Test app – PageRank
Parameters
Test size: 216 ~ 224 , 8-byte words
Performance
Performance with DRE is better than without
Design optionA shows better performance than design optionB
Initial Results
TASK 1: CMC Prototypes
  Design optionA: view buffer in host memory
    DRE’s view buffer is located in host memory
    Read/write to DRE through HT’s host data interfaces
  Design optionB: view buffer in HMC
    Allocate DRE’s view buffer in HMC
    Read/write to DRE’s view buffer through HIX directly
GUPS Performance
CMC shows speedup if host-only is baseline
PERFMON outputs average latencies
STREAM Performance
PERFMON outputs average latencies
Nearly constant difference between Pers & MC PERFMON measurements