## Slide 1: F3-16: FPGA & HMC Tools & Architectures for RSC
Number of supporting memberships = #
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida
Dr. Alan George
Professor of ECE
University of Florida
Kenneth Hill
Nikhil Ghanathe
Shefali Gundecha
Abhijeet Lawande
Gongyu Wang
Riju John Xavier
Yu Zou
Research Students

## Slide 2: Project Goals, Motivations, & Challenges
Explore and advance key technologies for RSC
HLS tool studies for reconfigurable computing
Role of Custom Memory Cube (CMC) for RSC
Multi-device architecture and tool studies
Achieve performance gain while maintaining productivity
Study CMC before existence of CMC
Again, achieve performance gain while maintaining productivity
Breakout year for reconfigurable supercomputing (RSC)
Derek Chiou, Microsoft (not Microsoft Research), “Catapult”
Mike Paolini, IBM, “Acceleration is the New Norm, Now Get to Work!”
Mike Strickland, Altera, “2015 is the Year of the FPGA!”
  Intel to purchase Altera for $16.7B cash
BOF*
*BOF: Birds-of-a-Feather event
Goal
Motivation
Challenges

## Slide 3: F3-16: Approach
P3: Custom Memory Cube (CMC)
Build foundation of CMC research by studying HMC
Create research vehicle and study benefits of CMC
P2: Reconfigurable Interconnects for Novo-G#
Novo-G#: reconfigurable interconnect, w/ OpenCL integration
Evaluate performance & productivity tradeoffs
P1: Multi-device Acceleration on POWER Arch.
Evaluate HLS tools on POWER architecture (e.g., OpenCL+CAPI*) for impactful RSC applications
  Explore interconnect topologies for CAPI-enabled accelerators
P4: CMS** Endcap L-1 Muon Trigger
Explore HLS tools for CMS firmware development at Large Hadron Collider in CERN
Evaluate optimization & productivity issues using HLS
**CMS- Compact Muon Solenoid
*CAPI: Coherent Accelerator Processor Interface

## Slide 4: F3-16: Highlights
P3: Custom Memory Cube (CMC)
STREAM shows ~10x B/W than GUPS on HMC
  Initial prototype of CMC (DRE) shows >2x speedup
P2: Reconfigurable Interconnects for Novo-G#
Fast, efficient, and flexible protocol stack for inter-FPGA comm.
  Multi-FPGA HLS development with Altera OpenCL
P1: Multi-device Acceleration on POWER Arch.
Highlight 1
  Highlight 2
P4: CMS Endcap L-1 Muon Trigger
Highlight 1
  Highlight 2
*DRE: Data reordering engine

## Slide 5: P1: Multi-device Acceleration on POWER Arch.
Task 2: Direct accelerator network w/ OpenCL+CAPI
Improve application scalability for multi-FPGA designs
Goal
F3-16
Explore interconnect topologies and scalability for CAPI-enabled accelerators
  Via system simulation studies
Experiment via POWER8 testbed
Leverage OpenCL for user productivity
F3-15
Leverage from Novo-G# technology
  Three-layer protocol stack for inter-FPGA networking
  Multi-FPGA OpenCL
Four-node POWER8 cluster

## Slide 6: P2: Reconfigurable Interconnects for Novo-G#
Improve performance & usability of multi-FPGA systems
  through HLS integration & flexible interconnect strategies
  Explore reconfigurable aspects of Novo-G# interconnect
  DSE* through simulation of Novo-G# VisualSim model
  Rapid prototyping via multi-FPGA OpenCL
Goal
Novo-G#
HDL
VisualSim
(DSE)
Reconfigure
Design Entry
Prototype
*DSE: design-space exploration
Approach
Motivation
Acceleration of large-scale RSC apps on Novo-G# with:
  Perf. estimation model for rapid DSE
  HLS integration to reduce barrier-to-entry
  Framework to support reconfigurable networks

## Slide 7: P2: Reconfigurable Interconnects for Novo-G#
Novo-G# protocol stack now supports multiple link-layer prototcols
  Interlaken, Custom, and Low-latency PHYs supported
OpenCL support for productive multi-FPGA development
  OpenCL BSP w/ channels + basic kernels
  Lessons learned for efficient inter-FPGA channel usage in OpenCL
Reconfigurable Network Aspects
Network topology
Network behavior
Point-to-point protocol
Achievements
Inter-FPGA channel
ProceV board
ProceV board
CAW16 Plans
Explore & evaluate reconfigurable aspects of network topology and network behavior
  Through simulation and prototyping

## Slide 8: P3: Custom Memory Cube (CMC)
Design-space exploration using software simulation & Task-A testbeds
Develop CMC prototypes & explore CMC processing capabilities
Explore potential of custom logic layer for HMC
    C-RAM* & PIM** (e.g., control & SIMD in logic layer)
Goal
*C-RAM: Computational RAM
**PIM: Processor in Memory
Motivation
Memory accesses of data-intensive applications consumes considerable amount of time and energy
HMC has higher B/W & lower power than current memories
Lack of fully functional CMC research platform
Approach
Develop test apps on FPGA-HMC platform (e.g., Merlin board)
Enable perf. measurement on FPGA & study HMC w/ test apps
HMC has higher B/W & lower power than current memories
Lack of fully functional CMC research platform
Phase 1
Phase 2

## Slide 9: P3: Custom Memory Cube (CMC)
*C-RAM: Computational RAM
**PIM: Processor in Memory
Memory accesses of data-intensive applications consumes considerable amount of time and energy
HMC has higher B/W & lower power than current memories
Lack of fully functional CMC research platform
Develop test apps on FPGA-HMC platform (e.g., Merlin board)
Enable perf. measurement on FPGA & study HMC w/ test apps
HMC has higher B/W & lower power than current memories
Lack of fully functional CMC research platform
Achievements
CAW16 Plans
Enable support of tunable parameters of HMC (e.g., packet size, tag size)
Study LPS-suggested CMC apps to define set of amenable operations in the logic layer
Phase 1
Phase 2

## Slide 10: P4: CMS Endcap L-1 Muon Trigger
Explore High-level Synthesis languages & tools for next-generation CMS code for
Parallel development of firmware & C++ model
Increase Flexibility, reduce development time
Enable consistent high-level (C++) verification
Motivation
Code development time
Verilog Implementation took several years and >4000 lines of code
Development and Maintenance
Code and development complexity rapidly increasing
Verification for Physicists
Increasingly difficult to obtain consistency between C++ & RTL model
Goal

## Slide 11: P4: CMS Endcap L-1 Muon Trigger
Achievements
Translated and verified 8 out of 9 modules of CSC Track-finder using HLS
Marked improvement in productivity
Performance constraints met for all modules
RTL optimizations using high-level constructs
Resource usage comparable
Observed to be better than Verilog impl. for majority of cases
Consistency between C++ & RTL achieved
HLS code compatible with g++ compiler enabling reliable high-level verification
  Design tool: Vivado HLS FPGA: Xilinx Virtex-7 XC7VX690T

## Slide 12: P4: CMS Endcap L-1 Muon Trigger
F3-15
Converted 4 out of 9 modules of Track-finder algorithm
Promising outcomes
  Improved productivity using Vivado HLS
  Lessons learned for h/w optimization via Vivado HLS
  HLS (C++) code used automatically for verification
Further exploration of HLS languages & tools
for next-gen CMS code
Goal
F3-16
Complete & optimize sub-modules in Track Finder Module
Integrate submodules
  Study integration issues in Vivado HLS
Integrate HLS code into CMSSW**
**CMSSW- CMS software

## Slide 13: F3-16: Conclusions
Summary & Conclusions
Developed a BSP & methodology for Multi-FPGA OpenCL
Explored reconfigurability through link protocols, more in CAW16
Summary & Conclusions
P1: Multi-device Acceleration on POWER Arch.
P2: Reconfigurable Interconnects for Novo-G#
P3: Custom Memory Cube (CMC)
P4: CMS Endcap L-1 Muon Trigger
Summary & Conclusions

## Slide 14: Questions, Posters, & Demos
Posters & Demos
  Altera OpenCL for FPGAs
  HLS for CMS Level-1 Endcap Muon Trigger
  Behavioral Emulation of Future-gen Devices & Systems
  Custom Memory Cube
  A Reconfigurable 3D Interconnect for Novo-G
Publications
  A. Lawande, A. George, and H. Lam, “Novo-G#: A multidimensional Torus-based Reconfigurable Cluster for Molecular Dynamics,” Concurrency & Computation: Practice & Experience, 2015, doi:10.1002/cpe.3565
  K. Hill, S. Craciun, A. George, and H. Lam, “Comparative Analysis of OpenCL vs. HDL with Image-Processing Kernels on Stratix-V FPGA,” 2015 IEEE Application-Specific Systems, Architectures and Processors (ASAP’15), Toronto, Canada, 27-29 July 2015
  G. Wang, H. Lam, A. George, and G. Edwards, “Performance and Productivity Evaluation of Hybrid-Threading HLS versus HDLs,” IEEE High Performance Extreme Computing Conference (HPEC’15), Waltham, MA, 15-17 Sept. 2015
  N. Kumar, M. Sringarpure, T. Banerjee, J. Hackl, S. Balachandar, H. Lam, A. George, and S. Ranka, "CMT-bone: A mini-app for Compressible Multiphase Turbulence Simulation Software,“ Cluster Computing (CLUSTER), IEEE International Conference on , vol., no., pp.785-792, 8-11 Sept. 2015, doi: 10.1109/CLUSTER.2015.134
Placeholder
Placeholder

## Slide 15: Outline
Note: each project presentation is allocated 10 minutes, plus 5 minutes of Q&A, for a total of 15 minutes
Goals, Motivations, & Challenges (1 slide)
  Refresh IAB on where we have been going with this project and why
Approach (1 slide)
  Refresh IAB on how we are getting there (methods, tasks)
Results & Analysis (5-7 slides)
  Start with single attention-grabber slide on major progress & achievements
  Then, for each major task, highlight key developments, experiments, results, analyses, and insight (“elevator pitch” style) – avoid overly dense
  Reminder: details should be saved for posters & appendix
Conclusions (1-2 slides)
  Brief summary of work, progress, achievement, and benefit
  Listing of any publications from project
  Listing of poster & demo titles
Appendix: Additional Materials (≤ 5 slides) – optional
  For off-line study by IAB, but NOT presented at workshop

## Slide 16: REMINDER
Faculty, please send final draft of presentation (both .pptx and .pdf files, please) to Alan & Darlene by 5pm ET on Monday, May 30th for posting and IAB preview
Please remember to include poster titles and demo titles in your closing slide, so we can make a list and send it to the IAB as well