## Slide 1: P3: Custom Memory Cube (CMC)
Explore potential of custom logic layer for HMC
    C-RAM* & PIM** (e.g., control & SIMD in logic layer)
Goal
*C-RAM: Computational RAM
**PIM: Processor in Memory
†DRE: Data reordering engine
Motivation
Memory accesses of data-intensive applications consumes considerable amount of time and energy
HMC has higher B/W & lower power than current memories
Lack of fully functional CMC research platform
Approach
Develop test apps on FPGA-HMC platform (e.g., Merlin board)
Enable perf. measurement on FPGA & study HMC w/ test apps
Create initial prototype of CMC arch. using DRE† of LLNL
Validate and evaluate DRE designs using select apps
Phase 1
Phase 2

## Slide 2: P3: Custom Memory Cube (CMC)
*DRE: Data reordering engine
Developed STREAM memory benchmark & bucket sort test application on Merlin board
Developed and enabled multi-level performance measurement methods
Evaluated HMC bandwidth using GUPS and STREAM benchmarks
  Up to 0.164 GUPS
Discussed five potential design options for developing DRE on Merlin
Developed DRE with view buffer in HMC upon LPS’s feedback
  Tested DRE on Merlin using page rank app. showing >2x speedup
Developed and tested DRE on Merlin with view buffer in host memory
Achievements
CAW16 Plans
Enable support of tunable parameters of HMC (e.g., packet size, tag size)
Continue study of CMC using DRE
Study LPS-suggested CMC apps
Phase 1
Phase 2
PLACEHOLDER FOR MINI GRAPHS WHICH SERVE AS CLIPARTS
PLACEHOLDER FOR MINI GRAPHS WHICH SERVE AS CLIPARTS
More results on poster