## Slide 1
App & Architecture Studies
In Reconfigurable Supercomputing (RSC)
Behavioral Emulation
Manage emulation complexity via Behavioral Emulation (BE)
  Coarse-grained, multi-scale simulation approach to balance accuracy, speed, & scalability
Approach
How to study future notional devices, nodes, & systems, up to Exascale without an existing Exascale system?
Goal & Motivation
  Novo-G# Reconfigurable Supercomputer
  52+1 Linux servers
  448 FPGAs (+ 64 coming soon)
    192 Altera Stratix-III E260 FPGAs
    192 Altera Stratix-IV E530 FPGAs
    64 Altera Stratix-V D8 FPGAs
  Reconfigurable interconnect
  3D (4x4x4) Torus or 6D Hypercube
    64 Altera Stratix-V D8 FPGAs (coming soon)
SST*-based BE Platform
NGEE** BE Platform
FPGAs
Scale of Sim
Simultaneous Sim
Original Project Target: One large, Exascale simulation distributed over many FPGAs
NGEEv1** Progress: One small, microscale simulation limited to a single FPGA
NGEEv1 Enhancements: Ongoing improve-ments to allow for simulations at larger scale
NGEEv1 Parameter Sweeps: Multi-FPGA DSE+ limited to a single simulation per device
Pipelined Design-Space Exploration: Simultaneous simulations pipelined in 1 FPGA
Up to eight orders-of-magnitude faster DSE/UQ than software simulator
Potential Target: Multiple Exascale simulations simultaneously distributed over many FPGAs
**NGEE: Novo-G Exascale Emulation
+DSE: Design-Space Exploration
++UQ: Uncertainty Quantification
Experimental Testbed will:
Support algorithmic design-space exploration
Provide behavioral emulation within SST* ecosystem
Reconfigurable Interconnects
Goal: Low-power, high-connectivity RC platform
    Targeted towards large-scale, communication-intensive problems like MD* & CFD**
Novo-G#
64 GiDEL ProceV (Stratix V D8)
4x4x4 3D torus
6 Rx-Tx links/FPGA
4x10 Gbps per link
*MD = Molecular Dynamics **CFD = Computational Fluid Dynamics
Approach:
Novo-G# network design to support multi-FPGA apps efficiently
Reconfigurable networking to adapt protocol & topology to needs of target application
OpenCL support to improve productivity & usability
Outcomes:
Flexible 3-layer protocol stack for Novo-G#
  Supports multiple protocols from light-weight to feature-rich
Novo-G# provides high-speed, reliable connectivity
  Bit error rate < 10-13 for each 10 Gbps link
Support for Altera OpenCL on multiple FPGAs
  Inter-FPGA links abstracted to inter-kernel (I/O) channels
Reconfigurable network support to fit architecture to app
  End-to-end AOCL-based design flow with DSE emphasized
ProceV Board
Node Architecture
Goal
Approach
Outcomes
App kernel
App kernel
FPGA
OpenCL channels
Inter-FPGA links
P
H
Y
X
C
V
R
ctrl logic
X
C
V
R
P
H
Y
P
H
Y
X
C
V
R
P
H
Y
X
C
V
R
P
H
Y
X
C
V
R
P
H
Y
X
C
V
R
X
C
V
R
P
H
Y
X
C
V
R
P
H
Y
X
C
V
R
P
H
Y
X
C
V
R
P
H
Y
Inter-FPGA links
OpenCL
Router
Bypass kernel
…
…
App kernel
CMC Research Platform
Develop custom architectures for distributed SpGEMM
Scale to multiple FPGAs leveraging Novo-G# interconnect
1 SpGEMM – Sparse Generalized Matrix/Matrix Multiplication; SuiteSparse/CombBLAS baseline on Xeon E5260 @ 2.40 GHz
Developed graph-processor architecture on Stratix-IV E530
  >200x performance-per-watt improvement over CPU for SpGEMM1
  Exploring amenable graph kernels & apps on our architecture
Develop scalable architecture to accelerate graph processing in the language of linear algebra
Goal
Motivation
Traditional architectures poorly suited for sparsity of graph datasets
Sparse-Matrix Processor for Graph Apps
Approach
Outcomes
RSC for Big Data & Extreme Computing
*SST: Structural Simulation Toolkit, Sandia National Lab
Large-scale, heterogeneous systems
A necessity for big data & extreme-scale computing (toward Exascale)
Motivation
  Develop Framework = Architecture + Tools
  for FPGA accelerators
  that is scalable and productive
Goal
Approach
  Architecture
Directly interconnected FPGAs
  Provides performance & scalability through OpenCL pipes
Memory coherency
  AFU uses CAPI to directly access host process memory
  Tools
    Hybrid programming model
  Use high-level OpenCL language to increase designer productivity
  Leverage optimized RTL cores (libraries)
    DSE of large-scale heterog. systems
  using system simulation tools (e.g., PSL Simulation Engine)
AFU: Accelerator Functional Unit
CAPI: Coherent Accelerator Processor Interface from IBM
CAPP: Coherent Accelerator Processor Proxy
PSL: POWER Service Layer
DSE: design space exploration
Explore performance measurement methods for CMC platform
Research performance modelling for notional CMC architecture
Initial case study CMC app: DRE*** of LLNL
Memory-intensive Big Data apps: memory bottleneck & high energy consumption
HMC: higher B/W & lower power than conventional memories
  Potential for C-RAM* & PIM** processing (CMC)
Create research platform for design space exploration of CMC apps & arch before existence of CMC
Motivation
Goal
Approach
Progress
Explore performance measure. methods for CMC platform
  Add hardware monitors to Merlin board infrastructure code
(hardware monitors)
Research performance modelling for notional CMC architecture
Model of notional CMC*
Merlin Board**
* Nair, R., et al. "Active Memory Cube: A processing-in-memory architecture for exascale systems.“ IBM Journal of Research and Development 59.2/3 (2015): 17-1.
** Merlin board from Convey Computer, Inc. (now a part of Micron)
Initial prototype of CMC research platform on Convey Merlin* board (FPGA + HMC)