## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Vinayak Deshpande
Peter Harduvel
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida

## Slide 2: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Performance mapping of DRE operations
  Case study result of random access app.
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 3: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Performance mapping of DRE operations
  Case study result of random access app.
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 4: Notional CMC Architecture*
Simplified view: an HMC with a user-programmable logic layer
* Nair, R., et al. "Active Memory Cube: A processing-in-memory architecture for exascale systems.“ IBM Journal of Res. & Development 59.2/3 (2015): 17-1.

## Slide 5: DRE* Prototype on CMC Architecture
View buffer (VB) can be set up on host (design option 1), inside the HMC (design option 2) or inside CMC logic (design option 3)
VB2
VB1
VB3
VB3
* DRE: Data Reordering/Rearrangement Engine Lawrence Livermore Nat. Labs

## Slide 6: Performance Measurement on Merlin Board
F3
CMC platform on Merlin board
M3 M4 M5
E’
**
Instrumented Merlin infrastructure with hardware performance monitors
  (A’, B’, C’, D’, M1, M2, M3, M4, M5, and E’ )
Progress: Able to measure all listed parameters except:
  M4, M5: Exploring with help from Convey
  E’: Exploring with help with Micron under NDA

## Slide 7: Mapping Notional CMC onto Merlin Board

## Slide 8: Model of CMC-to-Merlin Mapping
      Latency A = latency C +ctrl signal transfer time B
      Ctrl signal transfer time B : time to transfer control signal between host and CMC
      Latency C = latency C’ – delay D’minusE’ + delay TSV*
      Delay D’minusE’ = latency D’ – latency E’
      Latency E’ = latency M5 – delay TX** (currently we cannot determine E’)
      Data transfer time B: time for host access to view buffer to get result data
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
M3 M4 M5
E’
**

## Slide 9: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Performance mapping of DRE operations
  Case study result of random access app.
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 10: Review of DRE setup, fill, drain
void drain() {
for (size_t i = 0; i < scratchpad.length(); i++) {
ref_base[idx_base[i]] = scratchpad[i];
}
}
void setup(value_pointer refp, index_pointer indexp, value_pointer sp)
{
ref_base = refp;
idx_base = indexp;
scratchpad = sp;
}
void fill() {
for (size_t i = 0; i < scratchpad.length(); i++) {
scratchpad[i] = ref_base[idx_base[i]];
}
}

## Slide 11: Non-overlapping Memory Access
Consistent with expectation: M1 > M2 > M3 (> M4 > M5 > E’)
Oper. | A’ (µs) | C’ | D’ | M1 | M2 | M3
Read | 1095.6 | 1.03 | 1.006 | 0.923 | 0.725 | 0.519
Write | 1104.0 | 1.071 | 1.011 | 0.991 | 0.793 | 0.577
A’ (ms) | C’ | D’ | M1 | M2 | M3
282.55 | 281.72 | 278.72 | 258.96 | 199.68 | 151.31
A’ (s) | C’ | D’ | M1 | M2 | M3
1658.67 | 1580.14 | 1559.65 | 1460.57 | 1122.42 | 839.84
Measured performance: Vector Addition in ms (100,000 iterations of 2 reads & 1 write)
Measured performance: SpMV – DRE app in seconds (224 X 224 matrix)
Measured performance: simple read/write (µs)
(Averaged over 100,000 iterations)

## Slide 12: Overlapping Memory Access: read/write ops
Observation: M1, M2, M3, (M4, M5, E’) have no significant difference
Chart: Overlapping Mem. Read Total Time of M1,2,3 (ms) vs. # Mem Ops.
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0014671 | 0.0057844 | 0.048994 | 0.097222 | 0.14531 | 0.19344 | 0.24155 | 0.28973 | 0.33797 | 0.38602 | 0.43406 | 0.48229 | 0.53029 | 0.57918 | 0.62651 | 0.6753 | 0.72247 | 0.77092 | 0.8192 | 0.86733 | 0.91493 | 0.96356 | 1.0117 | 1.0604 | 1.1073 | 1.156 | 1.2043 | 1.2535 | 1.3017 | 1.348 | 1.3966 | 1.445
M2 (ms) | 0.0012695 | 0.0055868 | 0.048796 | 0.097024 | 0.14511 | 0.19325 | 0.24135 | 0.28953 | 0.33777 | 0.38583 | 0.43386 | 0.48209 | 0.5301 | 0.57898 | 0.62631 | 0.6751 | 0.72228 | 0.77072 | 0.819 | 0.86714 | 0.91474 | 0.96337 | 1.0115 | 1.0602 | 1.1071 | 1.1558 | 1.2041 | 1.2533 | 1.3015 | 1.3478 | 1.3964 | 1.4448
M3 (ms) | 0.0010539 | 0.0053892 | 0.048575 | 0.096796 | 0.1449 | 0.19302 | 0.24116 | 0.28931 | 0.33756 | 0.3856 | 0.43367 | 0.48186 | 0.52988 | 0.57877 | 0.62609 | 0.67489 | 0.72205 | 0.7705 | 0.8188 | 0.8669 | 0.9145 | 0.96316 | 1.0113 | 1.06 | 1.1069 | 1.1555 | 1.2038 | 1.2531 | 1.3013 | 1.3476 | 1.3962 | 1.4446
Chart: Overlapping Mem. Write Total Time of M1,2,3 (ms) vs. # Mem Ops
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0020479 | 0.0060838 | 0.049233 | 0.097605 | 0.14559 | 0.19401 | 0.2419 | 0.2902 | 0.33817 | 0.38655 | 0.43444 | 0.48291 | 0.53079 | 0.58008 | 0.62741 | 0.67531 | 0.72349 | 0.77162 | 0.82021 | 0.86833 | 0.91622 | 0.9641 | 1.0138 | 1.0604 | 1.1111 | 1.1591 | 1.2054 | 1.2531 | 1.302 | 1.3494 | 1.3978 | 1.4458
M2 (ms) | 0.0018503 | 0.0058862 | 0.049036 | 0.097407 | 0.14539 | 0.19381 | 0.24171 | 0.29001 | 0.33797 | 0.38635 | 0.43424 | 0.48271 | 0.53059 | 0.57988 | 0.62721 | 0.67511 | 0.72329 | 0.77142 | 0.82001 | 0.86813 | 0.91602 | 0.96399 | 1.0136 | 1.0602 | 1.1109 | 1.1589 | 1.2052 | 1.2529 | 1.3018 | 1.3492 | 1.3976 | 1.4455
M3 (ms) | 0.0016407 | 0.0056587 | 0.04882 | 0.097168 | 0.14518 | 0.1936 | 0.24148 | 0.28978 | 0.33777 | 0.38613 | 0.43401 | 0.48249 | 0.53036 | 0.57966 | 0.62698 | 0.67488 | 0.72307 | 0.77119 | 0.81981 | 0.8679 | 0.91583 | 0.96367 | 1.0134 | 1.06 | 1.1106 | 1.1587 | 1.205 | 1.2527 | 1.3015 | 1.349 | 1.3973 | 1.4453

## Slide 13: Overlapping Memory Access: DRE ops
M1, M2, M3, (M4, M5, E’) have no significant difference
  For overlapping memory access, discrepancy between M1, M2, M3, M4, M5, E’ is hidden by pipeline
Chart: Random Access App. Fill Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.15226 | 0.30119 | 0.59834 | 1.955 | 2.3873 | 4.7748 | 9.5416 | 19.0795 | 38.1606 | 76.1869 | 152.3098 | 304.7398 | 609.6542 | 1219.0793 | 2441.405
M2 (ms) | 0.15206 | 0.3008 | 0.59755 | 1.9392 | 2.3841 | 4.7685 | 9.5289 | 19.0542 | 38.11 | 76.0857 | 152.1075 | 304.3351 | 608.8448 | 1217.4607 | 2438.167
M3 (ms) | 0.14832 | 0.29685 | 0.5932 | 1.1883 | 2.3747 | 4.745 | 9.5028 | 18.9907 | 37.9955 | 75.9464 | 151.8868 | 303.8764 | 607.8186 | 1215.2063 | 2430.8469
Chart: Random Access App. Drain Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.1486 | 0.29793 | 0.59473 | 1.1907 | 2.3817 | 4.7562 | 9.5399 | 19.0358 | 38.1075 | 76.1439 | 152.2908 | 304.761 | 609.4099 | 1219.5077 | 2440.3599
M2 (ms) | 0.14841 | 0.29754 | 0.59394 | 1.1892 | 2.3785 | 4.7498 | 9.5272 | 19.0104 | 38.0569 | 76.0426 | 152.0884 | 304.3563 | 608.6005 | 1217.8883 | 2437.1223
M3 (ms) | 0.14822 | 0.29714 | 0.59315 | 1.1876 | 2.3751 | 4.7434 | 9.502 | 18.9808 | 37.9742 | 75.9328 | 151.8523 | 303.8206 | 607.6246 | 1215.151 | 2430.2197

## Slide 14: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Performance mapping of DRE operations
  Case study result of random access app.
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 15: Simplified Notional CMC Modeling
For pipelined overlapping memory operations, estimate:
  M1 = M2 = M3 = M4 = M5 = E’
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
M3 M4 M5
E’
**
      Latency A = latency C +ctrl signal transfer time B
      Ctrl signal transfer time B : time to transfer control signal between host and CMC
      Latency C = latency C’ – delay D’minusE’ + delay TSV*
      Delay D’minusE’ = latency D’ – latency E’
      Latency E’ = latency M5 – delay TX** (currently we cannot determine E’)
      Data transfer time B: time for host access to view buffer to get result data

## Slide 16: Simplified Notional CMC Modeling
For pipelined overlapping memory operations, estimate:
  M1 = M2 = M3 = M4 = M5 = E’
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
M3 M4 M5
E’
**
      Latency A = latency C +ctrl signal transfer time B
      Ctrl signal transfer time B : time to transfer control signal between host and CMC
      Latency C = latency C’ + delay TSV*
      Data transfer time B: time for host access to view buffer to get result data
      * delay TSV = time to transfer request + time to transfer response

## Slide 17: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Application of simplified mapping to DRE design option 3
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 18: Scope
Current scope: 1 link, 1 CMC core architecture
  Scale and parameterized in the future (n links, m core)
link
CMCcore

## Slide 19: Parameters of CMC architecture
  Link parameters:
    BWlink: Effective bandwidth of Host-CMC interface:
    Bit width of Host-CMC message (request + response): Whost-logic
      Data: Whost-logic(data) Ctrl: Whost-logic(ctrl)
  TSV
    Effective bandwidth of CMC logic – vault controller connection: BWlogic-vc
    Bit width of logic-vault message (request + response): Wlogic-vc
BWlogic-vc
Wlogic-vc
link

## Slide 20: Best-case Performance (DS3, 1 link, 1 core)
Model of notional CMC
CMC platform on Merlin board
M3 M4 M5
E’
**

## Slide 21: Worst-case performance
Model of notional CMC
CMC platform on Merlin board
M3 M4 M5
E’
**
  Not clear to me the purpose of the next 3 slides. The outline says “Case study result of random access app.”

## Slide 22: Case Study Result for Random Access App.
Placeholder
  Will update performance results here

## Slide 23: Going Forward
Creating user-friendly CMC API
Share code and lessons with LPS
  Visit LPS at some time
Continue researching on CMC modelling for multiple links multiple CMC cores
Study sorting and bloom filter on CMC