## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Vinayak Deshpande
Peter Harduvel
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida

## Slide 2: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Application of simplified mapping to DRE option 2
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 3: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Application of simplified mapping to DRE option 2
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 4: Notional CMC Architecture*
Based on Nair et al.* : an HMC with a user-programmable logic layer
A, B, C, D, and : performance-measurement points of interest
* Nair, R., et al. "Active Memory Cube: A processing-in-memory architecture for exascale systems.“ IBM Journal of Res. & Development 59.2/3 (2015): 17-1.
I thought we decided to delete the Delay boxes on the link? If so, do so all slides.
Why is there a VB in this general CMC arch?
Notes: You need to address my two comments in yellow boxes.
I modified the bullets to emphasize the 2 take-away points for this slide

## Slide 5: DRE* Prototype on CMC Architecture
View buffer (VB) can be set up on host (design option 1), inside the HMC (design option 2) or inside CMC logic (design option 3)
VB2
VB1
VB3
VB3
* DRE: Data Reordering/Rearrangement Engine Lawrence Livermore Nat. Labs
I thought we decided to delete the Delay boxes on the link? If so, do so all slides.
Notes: Same comment about “Delay boxes” in the links.
I modified the animation to be consistent with the ordering of 1, 2, and 3.

## Slide 6: Performance Measurement on Merlin Board
CMC platform on Merlin board
M3 M4 M5
E’
**
Instrumented Merlin infrastructure with hardware performance monitors
  A’, B’, C’, D’, M1, M2, M3, M4, M5, and E’
Progress: Able to measure all listed parameters except:
  M4, M5: Exploring with help from Convey
  E’: Exploring with help with Micron under NDA
Notes: Removed F3 on top of slide;
I changed the colors to make the bullets and figure consistent. Please make sure you do the same when creating slides in the future.

## Slide 7: Mapping Notional CMC onto Merlin Board
Merlin board
Case study: model of a notional CMC
Simplifying assumption:
For this model, this part of CMC is assumed to have an HMC architecture
I thought we decided to delete the Delay boxes on the link? If so, do so all slides.
Notes: I tried to make the take-away point more obvious:
Add yellow boxes to draw attention to them
State take-away point
This is something you need to learn to do.
Make clear in your mind what is the take-away point of the slide?
Make the take-away point clear IN THE SLIDE (either by a bullet or some graphics)

## Slide 8: Model of CMC-to-Merlin Mapping
      Total = latency A + data transfer time B
      Data transfer time B: time for host access to view buffer to get result data
      Latency A = latency C + ctrl signal transfer time B
      Ctrl signal transfer time B : time to transfer control signal between host and CMC
      Latency C = latency C’ – delay D’minusE’ + delay TSV*
      Delay D’minusE’ = latency D’ – latency E’
      Latency E’ = latency M5 – delay TX** (currently we cannot determine E’)
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
M3 M4 M5
E’
**
Original slide 8: Model of CMC-to-Merlin Mapping; see next slide for my modification

## Slide 9: Model of CMC-to-Merlin Mapping
      Latency A = ctrl signal transfer time B + latency C + result transfer time B
      Ctrl signal transfer time B : time to transfer control signals between host and CMC
      Data transfer time B: time for host access to obtain result (e.g., transfer from view buffer)
      Latency C = latency C’ – delay D’minusE’ + delay TSV*
      Delay D’minusE’ = latency D’ – latency E’
      * delay TSV = between DRE core and switch, time to transfer a request +
      time to transfer response of that request
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
M3 M4 M5
E’
**
I thought we decided to delete the Delay boxes on the link? If so, do so all slides.
Notes: I changed the first few bullet for latency A; hopefully simpler and more clear.
I added “Between DRE core and switch” for the footnote for delay TSV
Added animation
I deleted the following bullets completely. All they do is to cause confusion (see my reasons below)
Latency E’ = latency M5 – delay TX** (currently we cannot determine E’)
* * delay TX = time to transfer a a request to HMC switch logic + time to transfer response back
Reasons for the deletion:
- We don’t need E’ for now.
- Even if we do need E’ later, we assume that we will be able to measure it (with Micron’s help)

## Slide 10: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Application of simplified mapping to DRE option 2
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 11: Review of DRE setup, fill, drain
void setup(value_pointer refp, index_pointer indexp, value_pointer sp)
{
ref_base = refp;
idx_base = indexp;
scratchpad = sp;
}
void fill() {
for (size_t i = 0; i < scratchpad.length(); i++) {
scratchpad[i] = ref_base[idx_base[i]];
}
}
void drain() {
for (size_t i = 0; i < scratchpad.length(); i++) {
ref_base[idx_base[i]] = scratchpad[i];
}
}

## Slide 12: Memory Access on Merlin Board
Non-overlapping memory access
Overlapping memory access
Wait for data return before issuing next memory request
Send next memory request immediately after sending previous one
Barrier synchronization to guarantee all responses are returned before exiting code
Notes: I changed the animation a little bit

## Slide 13: Non-overlapping Memory Access
Observation consistent with expectation: M1 > M2 > M3 (> M4 > M5 > E’)
Oper. | A’ (µs) | C’ | D’ | M1 | M2 | M3
Read | 1095.6 | 1.03 | 1.006 | 0.923 | 0.725 | 0.519
Write | 1104.0 | 1.071 | 1.011 | 0.991 | 0.793 | 0.577
A’ (ms) | C’ | D’ | M1 | M2 | M3
282.55 | 281.72 | 278.72 | 258.96 | 199.68 | 151.31
A’ (s) | C’ | D’ | M1 | M2 | M3
1658.67 | 1580.14 | 1559.65 | 1460.57 | 1122.42 | 839.84
Measured performance: Vector Addition in ms (100,000 iterations of 2 reads & 1 write)
Measured performance: SpMV – DRE app in seconds (224 X 224 matrix)
Measured performance: simple read/write (µs) (Averaged over 100,000 iterations)

## Slide 14: Overlapping Memory Access: read/write ops
Observation: M1, M2, M3, (M4, M5, E’) have no significant difference
Chart: Overlapping Mem. Read Total Time of M1,2,3 (ms) vs. # Mem Ops.
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0014671 | 0.0057844 | 0.048994 | 0.097222 | 0.14531 | 0.19344 | 0.24155 | 0.28973 | 0.33797 | 0.38602 | 0.43406 | 0.48229 | 0.53029 | 0.57918 | 0.62651 | 0.6753 | 0.72247 | 0.77092 | 0.8192 | 0.86733 | 0.91493 | 0.96356 | 1.0117 | 1.0604 | 1.1073 | 1.156 | 1.2043 | 1.2535 | 1.3017 | 1.348 | 1.3966 | 1.445
M2 (ms) | 0.0012695 | 0.0055868 | 0.048796 | 0.097024 | 0.14511 | 0.19325 | 0.24135 | 0.28953 | 0.33777 | 0.38583 | 0.43386 | 0.48209 | 0.5301 | 0.57898 | 0.62631 | 0.6751 | 0.72228 | 0.77072 | 0.819 | 0.86714 | 0.91474 | 0.96337 | 1.0115 | 1.0602 | 1.1071 | 1.1558 | 1.2041 | 1.2533 | 1.3015 | 1.3478 | 1.3964 | 1.4448
M3 (ms) | 0.0010539 | 0.0053892 | 0.048575 | 0.096796 | 0.1449 | 0.19302 | 0.24116 | 0.28931 | 0.33756 | 0.3856 | 0.43367 | 0.48186 | 0.52988 | 0.57877 | 0.62609 | 0.67489 | 0.72205 | 0.7705 | 0.8188 | 0.8669 | 0.9145 | 0.96316 | 1.0113 | 1.06 | 1.1069 | 1.1555 | 1.2038 | 1.2531 | 1.3013 | 1.3476 | 1.3962 | 1.4446
Chart: Overlapping Mem. Write Total Time of M1,2,3 (ms) vs. # Mem Ops
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0020479 | 0.0060838 | 0.049233 | 0.097605 | 0.14559 | 0.19401 | 0.2419 | 0.2902 | 0.33817 | 0.38655 | 0.43444 | 0.48291 | 0.53079 | 0.58008 | 0.62741 | 0.67531 | 0.72349 | 0.77162 | 0.82021 | 0.86833 | 0.91622 | 0.9641 | 1.0138 | 1.0604 | 1.1111 | 1.1591 | 1.2054 | 1.2531 | 1.302 | 1.3494 | 1.3978 | 1.4458
M2 (ms) | 0.0018503 | 0.0058862 | 0.049036 | 0.097407 | 0.14539 | 0.19381 | 0.24171 | 0.29001 | 0.33797 | 0.38635 | 0.43424 | 0.48271 | 0.53059 | 0.57988 | 0.62721 | 0.67511 | 0.72329 | 0.77142 | 0.82001 | 0.86813 | 0.91602 | 0.96399 | 1.0136 | 1.0602 | 1.1109 | 1.1589 | 1.2052 | 1.2529 | 1.3018 | 1.3492 | 1.3976 | 1.4455
M3 (ms) | 0.0016407 | 0.0056587 | 0.04882 | 0.097168 | 0.14518 | 0.1936 | 0.24148 | 0.28978 | 0.33777 | 0.38613 | 0.43401 | 0.48249 | 0.53036 | 0.57966 | 0.62698 | 0.67488 | 0.72307 | 0.77119 | 0.81981 | 0.8679 | 0.91583 | 0.96367 | 1.0134 | 1.06 | 1.1106 | 1.1587 | 1.205 | 1.2527 | 1.3015 | 1.349 | 1.3973 | 1.4453

## Slide 15: Overlapping Memory Access: DRE ops
Observation: M1, M2, M3, (M4, M5, E’) again have no significant difference
Chart: Random Access App. Fill Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.15226 | 0.30119 | 0.59834 | 1.955 | 2.3873 | 4.7748 | 9.5416 | 19.0795 | 38.1606 | 76.1869 | 152.3098 | 304.7398 | 609.6542 | 1219.0793 | 2441.405
M2 (ms) | 0.15206 | 0.3008 | 0.59755 | 1.9392 | 2.3841 | 4.7685 | 9.5289 | 19.0542 | 38.11 | 76.0857 | 152.1075 | 304.3351 | 608.8448 | 1217.4607 | 2438.167
M3 (ms) | 0.14832 | 0.29685 | 0.5932 | 1.1883 | 2.3747 | 4.745 | 9.5028 | 18.9907 | 37.9955 | 75.9464 | 151.8868 | 303.8764 | 607.8186 | 1215.2063 | 2430.8469
Chart: Random Access App. Drain Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.1486 | 0.29793 | 0.59473 | 1.1907 | 2.3817 | 4.7562 | 9.5399 | 19.0358 | 38.1075 | 76.1439 | 152.2908 | 304.761 | 609.4099 | 1219.5077 | 2440.3599
M2 (ms) | 0.14841 | 0.29754 | 0.59394 | 1.1892 | 2.3785 | 4.7498 | 9.5272 | 19.0104 | 38.0569 | 76.0426 | 152.0884 | 304.3563 | 608.6005 | 1217.8883 | 2437.1223
M3 (ms) | 0.14822 | 0.29714 | 0.59315 | 1.1876 | 2.3751 | 4.7434 | 9.502 | 18.9808 | 37.9742 | 75.9328 | 151.8523 | 303.8206 | 607.6246 | 1215.151 | 2430.2197
  For overlapping memory access, discrepancy between M1, M2, M3, (M4, M5, E’) is hidden by “pipeline effect”
  Simplified CMC modeling can be used
Notes: Changed to “pipeline effort” vs. “pipeline”. I’m not sure we can expect perfect pipelining for overlapping memory accesses.
Put in a second take-away point.

## Slide 16: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Application of simplified mapping to DRE option 2
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 17: Simplified Notional CMC Modeling
For pipelined overlapping memory operations, estimate:
  M1 = M2 = M3 = M4 = M5 = E’
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
M3 M4 M5
E’
**
      Total = latency A + data transfer time B
      Data transfer time B: time for host access to view buffer to get result data
      Latency A = latency C +ctrl signal transfer time B
      Ctrl signal transfer time B : time to transfer control signal between host and CMC
      Latency C = latency C’ – delay D’minusE’ + delay TSV*
      Delay D’minusE’ = latency D’ – latency E’
      Latency E’ = latency M5 – delay TX** (currently we cannot determine E’)
I thought we decided to delete the Delay boxes on the link? If so, do so all slides.
If you agree with the new Slide 9 (Model of CMC-to-Merlin Mapping), these equations needs to be changed.

## Slide 18: Simplified Notional CMC Modeling
For pipelined overlapping memory operations, estimate:
  M1 = M2 = M3 = M4 = M5 = E’
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
M3 M4 M5
E’
**
      Total = latency A + data transfer time B
      Data transfer time B: time for host access to view buffer to get result data
      Latency A = latency C +ctrl signal transfer time B
      Ctrl signal transfer time B : time to transfer control signal between host and CMC
      Latency C = latency C’ + delay TSV*
      * delay TSV = time to transfer request + time to transfer response
I thought we decided to delete the Delay boxes on the link? If so, do so all slides.
If you agree with the new Slide 9 (Model of CMC-to-Merlin Mapping), these equations needs to be changed.

## Slide 19: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Experiments & measurements
  Non-overlapping memory access
    Simple read & write ops, DRE ops
  Overlapping memory access
    Simple read & write ops, DRE ops
Simplified CMC-to-Merlin mapping
  Application of simplified mapping to DRE option 2
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 20: Scope and Parameter Definition
Current scope: 1 link, 1 CMC core architecture
  Scale and parameterized in future (n links, m core)
1 link
1 CMC Core
  Link parameters:
    BWlink: Bandwidth of host-CMC interface (bit/s)
    Whost-cmc: Bit width of host-CMC message (request + response) (bit)
      Data: Whost-cmc(data)
      Ctrl: Whost-cmc(ctrl)
  TSV parameters
    BWTSV: Bandwidth of TSV connection (bit/s)
    Wcore-vc: Bit width of core-vault message (request + response) (bit)
I thought we decided to delete the Delay boxes on the link? If so, do so all slides.

## Slide 21: Best-case Performance (Design Op3, 1 link, 1 CMC core)
Model of notional CMC
CMC platform on Merlin board
M3 M4 M5
E’
**
Isn’t this Design Option 2 in Slide 5?
Explain to me in meeting why this is best-case.

## Slide 22: Worst-case performance (Design Op3, 1 link, 1 CMC core)
Model of notional CMC
CMC platform on Merlin board
M3 M4 M5
E’
**
Isn’t this Design Option 2 in Slide 5?
Why is 50% the worst case (may need a better name)
May have several: 75%, 50%, 25%??

## Slide 23: Case Study Result for Random Access App.
Chart: Max Performance of Randa Access App on CMC vs TableSize
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Total (ms) | 0.74295 | 1.4838 | 2.9639 | 5.922 | 11.8502 | 23.6735 | 47.3491 | 94.7597 | 189.6191 | 378.8273 | 757.6678 | 1515.5201 | 3030.8338 | 6061.6937 | 12134.3116
Fill (ms) | 0.14389 | 0.28462 | 0.56602 | 1.128 | 2.2629 | 4.5027 | 9.0052 | 18.0105 | 36.0645 | 71.9819 | 143.9428 | 288.0154 | 575.8178 | 1151.8563 | 2307.2027
Drain (ms) | 0.29752 | 0.59606 | 1.1917 | 2.3817 | 4.7627 | 9.5216 | 19.0455 | 38.1523 | 76.361 | 152.4581 | 304.9505 | 609.9556 | 1219.9178 | 2439.6411 | 4886.7162
Data Transfer (ms) | 0.30154 | 0.60308 | 1.2062 | 2.4123 | 4.8246 | 9.6492 | 19.2984 | 38.5968 | 77.1936 | 154.3873 | 308.7745 | 617.5491 | 1235.0982 | 2470.1963 | 4940.3926
Chart: Worst Performance of Randa Access App on CMC vs TableSize
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Total (ms) | 0.76011 | 1.5181 | 3.0326 | 6.0593 | 12.1248 | 24.2228 | 48.4477 | 96.9569 | 194.0137 | 387.6163 | 775.2459 | 1550.6763 | 3101.1463 | 6202.3187 | 12415.5616
Fill (ms) | 0.15248 | 0.30179 | 0.60035 | 1.1967 | 2.4002 | 4.7773 | 9.5545 | 19.1092 | 38.2618 | 76.3764 | 152.7318 | 305.5935 | 610.9741 | 1222.1688 | 2447.8277
Drain (ms) | 0.3061 | 0.61323 | 1.226 | 2.4503 | 4.9 | 9.7962 | 19.5948 | 39.2509 | 78.5583 | 156.8526 | 313.7396 | 627.5337 | 1255.0741 | 2509.9536 | 5027.3412
Data Transfer (ms) | 0.30154 | 0.60308 | 1.2062 | 2.4123 | 4.8246 | 9.6492 | 19.2984 | 38.5968 | 77.1936 | 154.3873 | 308.7745 | 617.5491 | 1235.0982 | 2470.1963 | 4940.3926
Chart: Max Performance of Randa Access App on CMC vs TableSize
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Total (ms) | 0.74295 | 1.4838 | 2.9639 | 5.922 | 11.8502 | 23.6735 | 47.3491 | 94.7597 | 189.6191 | 378.8273 | 757.6678 | 1515.5201 | 3030.8338 | 6061.6937 | 12134.3116
Fill (ms) | 0.14389 | 0.28462 | 0.56602 | 1.128 | 2.2629 | 4.5027 | 9.0052 | 18.0105 | 36.0645 | 71.9819 | 143.9428 | 288.0154 | 575.8178 | 1151.8563 | 2307.2027
Drain (ms) | 0.29752 | 0.59606 | 1.1917 | 2.3817 | 4.7627 | 9.5216 | 19.0455 | 38.1523 | 76.361 | 152.4581 | 304.9505 | 609.9556 | 1219.9178 | 2439.6411 | 4886.7162
Data Transfer (ms) | 0.30154 | 0.60308 | 1.2062 | 2.4123 | 4.8246 | 9.6492 | 19.2984 | 38.5968 | 77.1936 | 154.3873 | 308.7745 | 617.5491 | 1235.0982 | 2470.1963 | 4940.3926
Chart: Worst Performance of Randa Access App on CMC vs TableSize
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Total (ms) | 0.76011 | 1.5181 | 3.0326 | 6.0593 | 12.1248 | 24.2228 | 48.4477 | 96.9569 | 194.0137 | 387.6163 | 775.2459 | 1550.6763 | 3101.1463 | 6202.3187 | 12415.5616
Fill (ms) | 0.15248 | 0.30179 | 0.60035 | 1.1967 | 2.4002 | 4.7773 | 9.5545 | 19.1092 | 38.2618 | 76.3764 | 152.7318 | 305.5935 | 610.9741 | 1222.1688 | 2447.8277
Drain (ms) | 0.3061 | 0.61323 | 1.226 | 2.4503 | 4.9 | 9.7962 | 19.5948 | 39.2509 | 78.5583 | 156.8526 | 313.7396 | 627.5337 | 1255.0741 | 2509.9536 | 5027.3412
Data Transfer (ms) | 0.30154 | 0.60308 | 1.2062 | 2.4123 | 4.8246 | 9.6492 | 19.2984 | 38.5968 | 77.1936 | 154.3873 | 308.7745 | 617.5491 | 1235.0982 | 2470.1963 | 4940.3926
What is the take-away point(s)?
What is the take-away point(s)?
Important: what are the take-away points for this slide??
Important: what are the take-away points for this slide??
Notes: I changed the animation.
Looking at this slide, I can’t figure out the take-away point(s).

## Slide 24: Going Forward
Creating user-friendly CMC API
Share code and lessons with LPS
  Visit LPS at some time
Continue researching on CMC modelling for multiple links multiple CMC cores
Study sorting and bloom filter on CMC