## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Vinayak Deshpande
Peter Harduvel
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida

## Slide 2: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Simplified CMC-to-Merlin mapping
  Overlapping memory access
    Simple read & write ops, DRE ops
  Validation of Platform
    Validation of PERFMON
    Validation of performance measurement
  Bloom filter and sorting implementations in HT
    Bloom filter demos
    Sorting
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 3: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Simplified CMC-to-Merlin mapping
  Overlapping memory access
    Simple read & write ops, DRE ops
  Validation of Platform
    Validation of PERFMON
    Validation of performance measurement
  Bloom filter and sorting implementations in HT
    Bloom filter demos
    Sorting
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 4: Notional CMC Architecture*
Based on Nair et al.* : an HMC with a user-programmable logic layer
A, B, C, D, and : performance-measurement points of interest
* Nair, R., et al. "Active Memory Cube: A processing-in-memory architecture for exascale systems.“ IBM Journal of Res. & Development 59.2/3 (2015): 17-1.

## Slide 5: DRE* Prototype on CMC Architecture
View buffer (VB) can be set up on host (design option 1), inside the HMC (design option 2) or inside CMC logic (design option 3)
VB2
VB1
VB3
VB3
* DRE: Data Reordering/Rearrangement Engine Lawrence Livermore Nat. Labs

## Slide 6: Performance Measurement on Merlin Board
CMC platform on Merlin board
*
Instrumented Merlin infrastructure with hardware performance monitors
  A’, B’, C’, D’, M1, M2, M3, M4, M5, and E’
Progress: Able to measure all listed parameters except:
  M4, M5: Exploring with help from Convey
  E’: Exploring with help with Micron under NDA
VB*: View Buffer

## Slide 7: Mapping Notional CMC onto Merlin Board
Simplifying assumption:
For this model, this part of CMC is assumed to have an HMC architecture
Merlin board
Case study: model of a notional CMC

## Slide 8: Model of CMC-to-Merlin Mapping
      Latency A = ctrl signal transfer time B + latency C + result transfer time B
      Ctrl signal transfer time B : time to transfer control signals between host and CMC
      Data transfer time B: time for host access to obtain result (e.g., transfer from view buffer)
      Latency C = delay TSV* + latency C’ – delay D’minusE’
      Delay D’minusE’ = latency D’ – latency E’
      * delay TSV= between DRE core and switch, time to transfer a request +
      time to transfer response of that request
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board

## Slide 9: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Simplified CMC-to-Merlin mapping
  Overlapping memory access
    Simple read & write ops, DRE ops
  Validation of Platform
    Validation of PERFMON
    Validation of performance measurement
  Bloom filter and sorting implementations in HT
    Bloom filter demos
    Sorting
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 10: Overlapping Memory Access: read/write ops
Observation: M1, M2, M3, (M4, M5, E’) have no significant difference
Chart: Overlapping Mem. Read Total Time of M1,2,3 (ms) vs. # Mem Ops.
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0014671 | 0.0057844 | 0.048994 | 0.097222 | 0.14531 | 0.19344 | 0.24155 | 0.28973 | 0.33797 | 0.38602 | 0.43406 | 0.48229 | 0.53029 | 0.57918 | 0.62651 | 0.6753 | 0.72247 | 0.77092 | 0.8192 | 0.86733 | 0.91493 | 0.96356 | 1.0117 | 1.0604 | 1.1073 | 1.156 | 1.2043 | 1.2535 | 1.3017 | 1.348 | 1.3966 | 1.445
M2 (ms) | 0.0012695 | 0.0055868 | 0.048796 | 0.097024 | 0.14511 | 0.19325 | 0.24135 | 0.28953 | 0.33777 | 0.38583 | 0.43386 | 0.48209 | 0.5301 | 0.57898 | 0.62631 | 0.6751 | 0.72228 | 0.77072 | 0.819 | 0.86714 | 0.91474 | 0.96337 | 1.0115 | 1.0602 | 1.1071 | 1.1558 | 1.2041 | 1.2533 | 1.3015 | 1.3478 | 1.3964 | 1.4448
M3 (ms) | 0.0010539 | 0.0053892 | 0.048575 | 0.096796 | 0.1449 | 0.19302 | 0.24116 | 0.28931 | 0.33756 | 0.3856 | 0.43367 | 0.48186 | 0.52988 | 0.57877 | 0.62609 | 0.67489 | 0.72205 | 0.7705 | 0.8188 | 0.8669 | 0.9145 | 0.96316 | 1.0113 | 1.06 | 1.1069 | 1.1555 | 1.2038 | 1.2531 | 1.3013 | 1.3476 | 1.3962 | 1.4446
Chart: Overlapping Mem. Write Total Time of M1,2,3 (ms) vs. # Mem Ops
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0020479 | 0.0060838 | 0.049233 | 0.097605 | 0.14559 | 0.19401 | 0.2419 | 0.2902 | 0.33817 | 0.38655 | 0.43444 | 0.48291 | 0.53079 | 0.58008 | 0.62741 | 0.67531 | 0.72349 | 0.77162 | 0.82021 | 0.86833 | 0.91622 | 0.9641 | 1.0138 | 1.0604 | 1.1111 | 1.1591 | 1.2054 | 1.2531 | 1.302 | 1.3494 | 1.3978 | 1.4458
M2 (ms) | 0.0018503 | 0.0058862 | 0.049036 | 0.097407 | 0.14539 | 0.19381 | 0.24171 | 0.29001 | 0.33797 | 0.38635 | 0.43424 | 0.48271 | 0.53059 | 0.57988 | 0.62721 | 0.67511 | 0.72329 | 0.77142 | 0.82001 | 0.86813 | 0.91602 | 0.96399 | 1.0136 | 1.0602 | 1.1109 | 1.1589 | 1.2052 | 1.2529 | 1.3018 | 1.3492 | 1.3976 | 1.4455
M3 (ms) | 0.0016407 | 0.0056587 | 0.04882 | 0.097168 | 0.14518 | 0.1936 | 0.24148 | 0.28978 | 0.33777 | 0.38613 | 0.43401 | 0.48249 | 0.53036 | 0.57966 | 0.62698 | 0.67488 | 0.72307 | 0.77119 | 0.81981 | 0.8679 | 0.91583 | 0.96367 | 1.0134 | 1.06 | 1.1106 | 1.1587 | 1.205 | 1.2527 | 1.3015 | 1.349 | 1.3973 | 1.4453

## Slide 11: Overlapping Memory Access: DRE ops
Observation: M1, M2, M3, (M4, M5, E’) again have no significant difference
Chart: Random Access App. Fill Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.15226 | 0.30119 | 0.59834 | 1.955 | 2.3873 | 4.7748 | 9.5416 | 19.0795 | 38.1606 | 76.1869 | 152.3098 | 304.7398 | 609.6542 | 1219.0793 | 2441.405
M2 (ms) | 0.15206 | 0.3008 | 0.59755 | 1.9392 | 2.3841 | 4.7685 | 9.5289 | 19.0542 | 38.11 | 76.0857 | 152.1075 | 304.3351 | 608.8448 | 1217.4607 | 2438.167
M3 (ms) | 0.14832 | 0.29685 | 0.5932 | 1.1883 | 2.3747 | 4.745 | 9.5028 | 18.9907 | 37.9955 | 75.9464 | 151.8868 | 303.8764 | 607.8186 | 1215.2063 | 2430.8469
Chart: Random Access App. Drain Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.1486 | 0.29793 | 0.59473 | 1.1907 | 2.3817 | 4.7562 | 9.5399 | 19.0358 | 38.1075 | 76.1439 | 152.2908 | 304.761 | 609.4099 | 1219.5077 | 2440.3599
M2 (ms) | 0.14841 | 0.29754 | 0.59394 | 1.1892 | 2.3785 | 4.7498 | 9.5272 | 19.0104 | 38.0569 | 76.0426 | 152.0884 | 304.3563 | 608.6005 | 1217.8883 | 2437.1223
M3 (ms) | 0.14822 | 0.29714 | 0.59315 | 1.1876 | 2.3751 | 4.7434 | 9.502 | 18.9808 | 37.9742 | 75.9328 | 151.8523 | 303.8206 | 607.6246 | 1215.151 | 2430.2197
  For overlapping memory access, discrepancy between M1, M2, M3, (M4, M5, E’) is hidden by “pipeline effect”
  Thus, a simplified CMC mapping can be used

## Slide 12: Simplified Notional CMC Modeling
For pipelined overlapping memory operations, estimate:
  M1 = M2 = M3 = M4 = M5 = E’
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
      Latency A = ctrl signal transfer time B + latency C + result transfer time B
      Ctrl signal transfer time B : time to transfer control signals between host and CMC
      Data transfer time B: time for host access to obtain result (e.g., transfer from view buffer)
      Latency C = latency C’ – delay D’minusE’ + delay TSV*
      Delay D’minusE’ = latency D’ – latency E’

## Slide 13: Simplified Notional CMC Modeling
For pipelined overlapping memory operations, estimate:
  M1 = M2 = M3 = M4 = M5 = E’
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
Model of notional CMC
      Latency A = ctrl signal transfer time B + latency C + result transfer time B
      Ctrl signal transfer time B : time to transfer control signals between host and CMC
      Data transfer time B: time for host access to obtain result (e.g., transfer from view buffer)
      Latency C = latency C’ + delay TSV*

## Slide 14: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Simplified CMC-to-Merlin mapping
  Overlapping memory access
    Simple read & write ops, DRE ops
  Validation of Platform
    Validation of PERFMON
    Validation of performance measurement
  Bloom filter and sorting implementations in HT
    Bloom filter demos
    Sorting
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 15: Validation of PERFMON
M1, M2, M3 are measured in PERFMON
  PERFMON – Hardware(Verilog) monitor designed by Convey, modified by CHREC
M4, M5, E’ are not measured
  By observing M1 = M2 = M3, we hypothesize M1 = M2 = M3 = M4 = M5 = E’
To validate M1, M2, M3 are accurately measured in PERFMON

## Slide 16: Validation of PERFMON
Progress
  Set up a RTL simulation of PERFMON in ModelSim, with help from Convey
  Validating the reported PERFMON values cycle by cycle in ModelSim

## Slide 17: Validation of Measurement
overlapping memory request:
Measured on Merlin board: D’=M1=M2=M3
Hypothesis: M3 = M5 (= E’)
Collect memory trace at D’
Input memory trace to simulator’s host
Expect: M1 = M5 (= E’) = C = E (from HMC simulator)
Measurement on Merlin board
Simulation on HMC Simulator

## Slide 18: Validation of Measurement
Progress

## Slide 19: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Simplified CMC-to-Merlin mapping
  Overlapping memory access
    Simple read & write ops, DRE ops
  Validation of Platform
    Validation of PERFMON
    Validation of performance measurement
  Bloom filter and sorting implementations in HT
    Bloom filter demos
    Sorting
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 20: Bloom Filter HT Demos
Spell checker
  Used a dictionary as database to set bit vector
  When a new word comes, bloom filter searches the existence of word in dictionary
  Report the word is wrongly spelled, if it doesn’t exist in dictionary
  Utilized 1 HT unit

## Slide 21: Bloom Filter HT Demos
Content-based deep packet inspection (longest string match)
  Used a group of different-length sensitive words to set bit vectors
  When a packet comes, bloom filter searches the existence of the longest matching sensitive word
  Report the packet contains sensitive information, if matched
  Utilized 16 HT unit

## Slide 22: Sorting

## Slide 23: Outline
Review & overview
  Notional CMC architecture
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
Simplified CMC-to-Merlin mapping
  Overlapping memory access
    Simple read & write ops, DRE ops
  Validation of Platform
    Validation of PERFMON
    Validation of performance measurement
  Bloom filter and sorting implementations in HT
    Bloom filter demos
    Sorting
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 24: Going Forward
Platform development
Complete validation of CMC platform
Complete development & instrumentation of CMC platform
Develop library for customization of notional CMC architecture under study
  Create user-friendly CMC API
Explore CMC apps using HT
Case studies to explore
Notional CMC architectures
CMC apps, including:
  Data Reordering/Rearrangement Engine, sorting algorithms, bloom filter
Lessons learned, including:
  Characteristics of CMC-amenable apps
  How to re-factor algorithms to become CMC-amenable
Share code and lessons with LPS
Visit LPS
F1