## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Vinayak Deshpande
Peter Harduvel (UG)
JeshalraThakaria (volunteer)
Raviteja Voora (volunteer)
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida
Notes: Add names of the volunteer students

## Slide 2: Outline
Review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter demos
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 3: Outline
Review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter demos
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 4: Notional CMC Architecture*
Based on Nair et al.* : an HMC with a user-programmable logic layer
A, B, C, D, and : performance-measurement points of interest
* Nair, R., et al. "Active Memory Cube: A processing-in-memory architecture for exascale systems.“ IBM Journal of Res. & Development 59.2/3 (2015): 17-1.

## Slide 5: DRE* Prototype on CMC Architecture
View buffer (VB) can be set up on host (design option 1), inside the HMC (design option 2) or inside CMC logic (design option 3)
VB2
VB1
VB3
VB3
* DRE: Data Reordering/Rearrangement Engine Lawrence Livermore Nat. Labs

## Slide 6: Performance Measurement on Merlin Board
CMC platform on Merlin board
*
Instrumented Merlin infrastructure with hardware performance monitors
  A’, B’, C’, D’, M1, M2, M3, M4, M5, and E’
Progress: Able to measure all listed parameters except:
  M4, M5: Exploring with help from Convey
  E’: Exploring with help with Micron under NDA
VB*: View Buffer

## Slide 7: Mapping Notional CMC onto Merlin Board
Simplifying assumption:
For this model, this part of CMC is assumed to have an HMC architecture
Merlin board
Case study: model of a notional CMC

## Slide 8: Model of CMC-to-Merlin Mapping
      Latency A = ctrl signal transfer time B + latency C + result transfer time B
      Ctrl signal transfer time B : time to transfer control signals between host and CMC
      Data transfer time B: time for host access to obtain result (e.g., transfer from view buffer)
      Latency C = delay TSV* + latency C’ – delay D’minusE’
      Delay D’minusE’ = latency D’ – latency E’
      * delay TSV= between DRE core and switch, time to transfer a request +
      time to transfer response of that request
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board

## Slide 9: Outline
Review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter demos
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 10: Overlapping Memory Access: read/write ops
Observation: M1, M2, M3, (M4, M5, E’) have no significant difference
Chart: Overlapping Mem. Read Total Time of M1,2,3 (ms) vs. # Mem Ops.
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0014671 | 0.0057844 | 0.048994 | 0.097222 | 0.14531 | 0.19344 | 0.24155 | 0.28973 | 0.33797 | 0.38602 | 0.43406 | 0.48229 | 0.53029 | 0.57918 | 0.62651 | 0.6753 | 0.72247 | 0.77092 | 0.8192 | 0.86733 | 0.91493 | 0.96356 | 1.0117 | 1.0604 | 1.1073 | 1.156 | 1.2043 | 1.2535 | 1.3017 | 1.348 | 1.3966 | 1.445
M2 (ms) | 0.0012695 | 0.0055868 | 0.048796 | 0.097024 | 0.14511 | 0.19325 | 0.24135 | 0.28953 | 0.33777 | 0.38583 | 0.43386 | 0.48209 | 0.5301 | 0.57898 | 0.62631 | 0.6751 | 0.72228 | 0.77072 | 0.819 | 0.86714 | 0.91474 | 0.96337 | 1.0115 | 1.0602 | 1.1071 | 1.1558 | 1.2041 | 1.2533 | 1.3015 | 1.3478 | 1.3964 | 1.4448
M3 (ms) | 0.0010539 | 0.0053892 | 0.048575 | 0.096796 | 0.1449 | 0.19302 | 0.24116 | 0.28931 | 0.33756 | 0.3856 | 0.43367 | 0.48186 | 0.52988 | 0.57877 | 0.62609 | 0.67489 | 0.72205 | 0.7705 | 0.8188 | 0.8669 | 0.9145 | 0.96316 | 1.0113 | 1.06 | 1.1069 | 1.1555 | 1.2038 | 1.2531 | 1.3013 | 1.3476 | 1.3962 | 1.4446
Chart: Overlapping Mem. Write Total Time of M1,2,3 (ms) vs. # Mem Ops
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0020479 | 0.0060838 | 0.049233 | 0.097605 | 0.14559 | 0.19401 | 0.2419 | 0.2902 | 0.33817 | 0.38655 | 0.43444 | 0.48291 | 0.53079 | 0.58008 | 0.62741 | 0.67531 | 0.72349 | 0.77162 | 0.82021 | 0.86833 | 0.91622 | 0.9641 | 1.0138 | 1.0604 | 1.1111 | 1.1591 | 1.2054 | 1.2531 | 1.302 | 1.3494 | 1.3978 | 1.4458
M2 (ms) | 0.0018503 | 0.0058862 | 0.049036 | 0.097407 | 0.14539 | 0.19381 | 0.24171 | 0.29001 | 0.33797 | 0.38635 | 0.43424 | 0.48271 | 0.53059 | 0.57988 | 0.62721 | 0.67511 | 0.72329 | 0.77142 | 0.82001 | 0.86813 | 0.91602 | 0.96399 | 1.0136 | 1.0602 | 1.1109 | 1.1589 | 1.2052 | 1.2529 | 1.3018 | 1.3492 | 1.3976 | 1.4455
M3 (ms) | 0.0016407 | 0.0056587 | 0.04882 | 0.097168 | 0.14518 | 0.1936 | 0.24148 | 0.28978 | 0.33777 | 0.38613 | 0.43401 | 0.48249 | 0.53036 | 0.57966 | 0.62698 | 0.67488 | 0.72307 | 0.77119 | 0.81981 | 0.8679 | 0.91583 | 0.96367 | 1.0134 | 1.06 | 1.1106 | 1.1587 | 1.205 | 1.2527 | 1.3015 | 1.349 | 1.3973 | 1.4453

## Slide 11: Overlapping Memory Access: DRE ops
Observation: M1, M2, M3, (M4, M5, E’) again have no significant difference
Chart: Random Access App. Fill Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.15226 | 0.30119 | 0.59834 | 1.955 | 2.3873 | 4.7748 | 9.5416 | 19.0795 | 38.1606 | 76.1869 | 152.3098 | 304.7398 | 609.6542 | 1219.0793 | 2441.405
M2 (ms) | 0.15206 | 0.3008 | 0.59755 | 1.9392 | 2.3841 | 4.7685 | 9.5289 | 19.0542 | 38.11 | 76.0857 | 152.1075 | 304.3351 | 608.8448 | 1217.4607 | 2438.167
M3 (ms) | 0.14832 | 0.29685 | 0.5932 | 1.1883 | 2.3747 | 4.745 | 9.5028 | 18.9907 | 37.9955 | 75.9464 | 151.8868 | 303.8764 | 607.8186 | 1215.2063 | 2430.8469
Chart: Random Access App. Drain Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.1486 | 0.29793 | 0.59473 | 1.1907 | 2.3817 | 4.7562 | 9.5399 | 19.0358 | 38.1075 | 76.1439 | 152.2908 | 304.761 | 609.4099 | 1219.5077 | 2440.3599
M2 (ms) | 0.14841 | 0.29754 | 0.59394 | 1.1892 | 2.3785 | 4.7498 | 9.5272 | 19.0104 | 38.0569 | 76.0426 | 152.0884 | 304.3563 | 608.6005 | 1217.8883 | 2437.1223
M3 (ms) | 0.14822 | 0.29714 | 0.59315 | 1.1876 | 2.3751 | 4.7434 | 9.502 | 18.9808 | 37.9742 | 75.9328 | 151.8523 | 303.8206 | 607.6246 | 1215.151 | 2430.2197
  For overlapping memory access, discrepancy between M1, M2, M3, (M4, M5, E’) is hidden by “pipeline effect”
  Thus, a simplified CMC mapping can be used

## Slide 12: Simplified Notional CMC Modeling
For pipelined overlapping memory operations, estimate:
  M1 = M2 = M3 = M4 = M5 = E’
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
      Latency A = ctrl signal transfer time B + latency C + result transfer time B
      Ctrl signal transfer time B : time to transfer control signals between host and CMC
      Data transfer time B: time for host access to obtain result (e.g., transfer from view buffer)
      Latency C = latency C’ – delay D’minusE’ + delay TSV*
      Delay D’minusE’ = latency D’ – latency E’

## Slide 13: Simplified Notional CMC Modeling
For pipelined overlapping memory operations, estimate:
  M1 = M2 = M3 = M4 = M5 = E’
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board
Model of notional CMC
      Latency A = ctrl signal transfer time B + latency C + result transfer time B
      Ctrl signal transfer time B : time to transfer control signals between host and CMC
      Data transfer time B: time for host access to obtain result (e.g., transfer from view buffer)
      Latency C = latency C’ + delay TSV*

## Slide 14: Outline
Review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter demos
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 15: HMC Simulator Selection
CasHMC simulator from Hanyang University
  No information about how the results are validated
Micron RTL HMC simulator
  Compilation issues (still in communication with Micron?)
SystemC HMC simulator from Micron
  Signed NDA with Micron to use the tool
  Accurate for optimal memory traces
  Communicating with Dan Stewart (Micron engineer) to interpret the results

## Slide 16: HMC SytemC Simulator - Architecture
Cycle-accurate simulator developed by Micron
Main modules:
  Synthetic traffic generator
  Host controller
  HMCWrapper
  Monitor
Traffic Generator
  Creates request stream (config.def)
    Read-to-write ratio, request buffer size, etc.
  Uses TLM2.0 interface to send
  read/write requests to host controller
Host Controller
  Map requests to links
  Create formatted packets (places in corresponding request buffer)
Trace file reader
  Parses an input trace file and issues requests to the model
Micron Technology, Inc., HMC SystemC Model
Document Revision 1.0 (SVN R194)
Trace file

## Slide 17: Generated Trace File – For Simulator
Which Vault the request is sent to
Which bank within a vault the request is sent to
Addressing within the DRAM array

## Slide 18: Example Output (1000 memory reads)
The bandwidth and latency calculations are measured on the pins of the HMC (C point in notional CMC architecture)
This value equals point C on the Simulator
Total latency of all request

## Slide 19: Validation Experiments
  Goal: Validate performance measurement on Merlin board
  Approach: Compare
  Merlin board measurement
  HMC SystemC simulator results
Merlin board
SystemC HMC Simulator
Experiments:
  Comparison of average latency of single memory access
  Comparison of average latency of single memory access (alternative method)
  Comparison of total overlapping latency

## Slide 20: Exp. 1: Avg. Latency, Single Memory Access
2. Input memory trace to simulator
Measurement on Merlin board
Simulation on HMC Simulator
1. Collect memory trace of HT
3. Measure latency of each single memory access at M3
4. Calculate average (1000 accesses) latency & compare with avg. latency reported in SystemC simulator

## Slide 21: Unexpected Result
give results
Telecon with Dan (Micron engineer responsible for SystemC simulator)
Need optimal trace for SystemC simulation

## Slide 22: Optimal Memory Trace
Accuracy of simulator depends on input memory trace
Optimal memory trace results in best performance & accuracy (~10% difference)
Optimal: to fully utilize internal parallelism of HMC, rotate vault address first, then bank address, and then byte address
  different vaults could work in parallel
  different bank could work in pipeline

## Slide 23: Example of Optimal Trace File
Which Vault the request is sent to
Which bank within a vault the request is sent to
Addressing within the DRAM array

## Slide 24: Exp. 1: Avg. Latency, Single Memory Access
2. Convert memory trace to HT address
Measurement on Merlin board
Simulation on HMC Simulator
1. Input optimal memory trace into simulator
3. Measure latency of each single memory access at M3
4. Calculate average (1000 accesses) latency & compare with avg. latency reported in SystemC simulator

## Slide 25: Exp. 1: Avg. Latency, Single Memory Access
Avg. Latency measured over 1000 memory read requests
  tM3 Measured at M3 point on Merlin board: 88.1 * 6 ns = 528.6 ns
  tC = Determined from SystemC Simulator: 479.414 ns (equivalent to M5)
Merlin board frequency:167 MHz
Notes: Make clear the point that we are measuring M3 on the Merlin board and
System C is giving result for C, which is equal to M5
Therefore M3 is a little bit larger M5 (consistent with our expectation)

## Slide 26: Exp. 2: Avg. Latency, Single Memory Access (Using overlapping memory requests)
Measurement on Merlin board
overlapping memory request
Measure M3
t1 and t are measured by 2 different PERFMON counters at M3 point
t2 = t – t1
t2 equals latency of single memory request
Execute code 10000 times to calculate Lavg
t2avg should be comparable to tC Avg. Latency reported in SystemC simulator (next slide)

## Slide 27: Experiment 2 Results
Measured results from Merlin board
  Results will be reported when Merlin board comes back online
Conclusions: (expected)
  Measured results are close to simulator results
  Validate modified PERFMON code for this case
SystemC simulator results
  1000 Memory read requests
  Link Avg. Latency = 479.414 ns
Notes: MADE CHANGES

## Slide 28: Experiment 3 Description
Hypothesis
  In overlapping access (already validated by measurement)
    M1 = M2 = M3 = (M4 = M5 = E’)
  In HMC
    M5 = C
    E = E’
Expect: M1 = M5 (= E’) = C = E (from HMC simulator)

## Slide 29: Experiment 3 Setup
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube
2. Convert memory trace to HT address
Expect: M1= M5 (= E’) = C = E (from HMC simulator)
Measurement on Merlin board
Simulation on HMC Simulator
1. Input optimal memory trace into simulator

## Slide 30: Experiment 3 Results
Measured results from Merlin board
  Results will be reported when Merlin board comes back online
Conclusions: (expected)
  Measured results are close to simulator results
SystemC simulator results
  1000 Memory read requests
  Total overlapping latency
    1683.2ns
Notes: MADE CHANGES

## Slide 31: Outline
Review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter demos
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 32: Verification of PERFMON Code Modification
M1, M2, M3 are measured in PERFMON
  PERFMON – Hardware(Verilog) monitor designed by Convey, modified by CHREC
M4, M5, E’ are not measured
  By observing M1 = M2 = M3, we hypothesize M1 = M2 = M3 = M4 = M5 = E’
Goal: to verify M1, M2, M3 are accurately measured in PERFMON

## Slide 33: Verification of PERFMON Code Modification
Progress
  Set up a RTL simulation of PERFMON in ModelSim, with help from Convey
  Verifying reported PERFMON values cycle by cycle in ModelSim

## Slide 34: Outline
Review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Comparison to DRE published data
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter demos
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 35: Bloom Filter HT Demos
Spell checker
  Input
    A dictionary
    Words to check
  Function
    A bloom filter was pre-set using the dictionary
    A new word was compared against bloom filter to check existence in the dictionary
  Output
    A wrong spelling is reported if the new word doesn’t exist in bloom filter
  HT utilization
    1 HT unit

## Slide 36: Bloom Filter HT Demos
Content-based deep packet inspection (longest string match)
  Input
    A group of different-length sensitive words
    Packet to inspect
  Function
    All same-length sensitive words are used to set the same bloom filter
    Multiple bloom filters are pre-set
    A new packet is compared against bloom filters to check existence of sensitive words
  Output
    Report the packet contains sensitive information, if matched
  HT utilization
    16 HT units

## Slide 37: Sorting Algorithms
Sorter Architectures
  Sorting Networks
    Bitonic merge sorter
  FIFO-Based Merge Sorter
  Merge Sorter Trees
  Bucket Sort
Progress

## Slide 38: Bitonic merge sorter
Input
  Unsorted list of numbers
Function
  First convert an unsorted sequence into Bitonic Sequence
  Need (log2N) cycles to sort a bitonic sequence with N keys
Output
  Sorted list of numbers

## Slide 39: FIFO-Based Merge Sorter - Two Input FIFOs
Input
  Two input FIFOs with sorted list of numbers
Function
  Comparator: compares the FIFO entries and produces an output
  Multiplexer: Comparator output is used to select the Large ( or small) number
Output
  Single output FIFO with sorted list of numbers
5 6 8 12 13
1 3 8 11 17
1 3 5 6 8 8 11 12 13 17

## Slide 40: FIFO-Based Merge Sorter - Multiple cascaded FIFOs
Input
  Tow input FIFOs with sorted list of numbers
Function
  Following functions are performed at each stage
  Comparator: compares the FIFO entries and produces an output
  Multiplexer: Comparator output is used to select the Large ( or small) number
Output
  Single output FIFO with sorted list of numbers

## Slide 41: Merge Sorter Trees
Input
  Large number of sorted lists to be merged (usually in external memory)
Function
  At each horizontal level, two FIFOs are compared to produce one sorted list
  Comparator: compares the FIFO entries and produces an output
  Multiplexer: Comparator output is used to select the Large ( or small) number
Output
  Single output FIFO with sorted list of numbers

## Slide 42: Bucket Sort
Input
  List of unsorted numbers
Function
  Buckets with different range of
  values are created
  Based on the specified ranges, each
  number goes into one particular bucket
  Finally each bucket is sorted
Output
  List of sorted numbers

## Slide 43: Sorting Algorithms - Progress
Currently implementing host applications for following
  Bitonic Merge Sorter
  Bucket Sort
These applications are relatively easy to implement in HT language as they do not require lot of on-chip* memory
Exploring FIFO-based merge sorter methods to see if they are efficient as they require more on-chip memory
on-chip* memory : Block RAM on FPGA

## Slide 44: Going Forward
Platform development
Complete validation of CMC platform
Complete development & instrumentation of CMC platform
Develop library for customization of notional CMC architecture under study
  Create user-friendly CMC API
Explore CMC apps using HT
Case studies to explore
Notional CMC architectures
CMC apps, including:
  Data Reordering/Rearrangement Engine, sorting algorithms, bloom filter
Lessons learned, including:
  Characteristics of CMC-amenable apps
  How to re-factor algorithms to become CMC-amenable
Share code and lessons with LPS
Visit LPS
F1