## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Vinayak Deshpande
Peter Harduvel (UG)
JeshalraThakaria (volunteer)
Raviteja Voora (volunteer)
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida

## Slide 2: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter examples
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 3: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter examples
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 4: Performance Measurement on Merlin Board
CMC platform on Merlin board
*
Instrumented Merlin infrastructure with hardware performance monitors
  A’, B’, C’, D’, M1, M2, M3, M4, M5, and E’
Progress: Able to measure all listed parameters except:
  M4, M5: Exploring with help from Convey
  E’: Exploring with help with Micron under NDA
VB*: View Buffer

## Slide 5: Mapping Notional CMC onto Merlin Board
Simplifying assumption:
For this model, this part of CMC is assumed to have an HMC architecture
Merlin board
Case study: model of a notional CMC
Observation:
“Pipelining” effect of overlapping memory access

## Slide 6: Observation: Overlapping Memory Access
For overlapping read/write ops:
Measurements at M1, M2, M3, (M4, M5, E’) have no significant difference
Chart: Overlapping Mem. Read Total Time of M1,2,3 (ms) vs. # Mem Ops.
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0014671 | 0.0057844 | 0.048994 | 0.097222 | 0.14531 | 0.19344 | 0.24155 | 0.28973 | 0.33797 | 0.38602 | 0.43406 | 0.48229 | 0.53029 | 0.57918 | 0.62651 | 0.6753 | 0.72247 | 0.77092 | 0.8192 | 0.86733 | 0.91493 | 0.96356 | 1.0117 | 1.0604 | 1.1073 | 1.156 | 1.2043 | 1.2535 | 1.3017 | 1.348 | 1.3966 | 1.445
M2 (ms) | 0.0012695 | 0.0055868 | 0.048796 | 0.097024 | 0.14511 | 0.19325 | 0.24135 | 0.28953 | 0.33777 | 0.38583 | 0.43386 | 0.48209 | 0.5301 | 0.57898 | 0.62631 | 0.6751 | 0.72228 | 0.77072 | 0.819 | 0.86714 | 0.91474 | 0.96337 | 1.0115 | 1.0602 | 1.1071 | 1.1558 | 1.2041 | 1.2533 | 1.3015 | 1.3478 | 1.3964 | 1.4448
M3 (ms) | 0.0010539 | 0.0053892 | 0.048575 | 0.096796 | 0.1449 | 0.19302 | 0.24116 | 0.28931 | 0.33756 | 0.3856 | 0.43367 | 0.48186 | 0.52988 | 0.57877 | 0.62609 | 0.67489 | 0.72205 | 0.7705 | 0.8188 | 0.8669 | 0.9145 | 0.96316 | 1.0113 | 1.06 | 1.1069 | 1.1555 | 1.2038 | 1.2531 | 1.3013 | 1.3476 | 1.3962 | 1.4446
Chart: Overlapping Mem. Write Total Time of M1,2,3 (ms) vs. # Mem Ops
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0020479 | 0.0060838 | 0.049233 | 0.097605 | 0.14559 | 0.19401 | 0.2419 | 0.2902 | 0.33817 | 0.38655 | 0.43444 | 0.48291 | 0.53079 | 0.58008 | 0.62741 | 0.67531 | 0.72349 | 0.77162 | 0.82021 | 0.86833 | 0.91622 | 0.9641 | 1.0138 | 1.0604 | 1.1111 | 1.1591 | 1.2054 | 1.2531 | 1.302 | 1.3494 | 1.3978 | 1.4458
M2 (ms) | 0.0018503 | 0.0058862 | 0.049036 | 0.097407 | 0.14539 | 0.19381 | 0.24171 | 0.29001 | 0.33797 | 0.38635 | 0.43424 | 0.48271 | 0.53059 | 0.57988 | 0.62721 | 0.67511 | 0.72329 | 0.77142 | 0.82001 | 0.86813 | 0.91602 | 0.96399 | 1.0136 | 1.0602 | 1.1109 | 1.1589 | 1.2052 | 1.2529 | 1.3018 | 1.3492 | 1.3976 | 1.4455
M3 (ms) | 0.0016407 | 0.0056587 | 0.04882 | 0.097168 | 0.14518 | 0.1936 | 0.24148 | 0.28978 | 0.33777 | 0.38613 | 0.43401 | 0.48249 | 0.53036 | 0.57966 | 0.62698 | 0.67488 | 0.72307 | 0.77119 | 0.81981 | 0.8679 | 0.91583 | 0.96367 | 1.0134 | 1.06 | 1.1106 | 1.1587 | 1.205 | 1.2527 | 1.3015 | 1.349 | 1.3973 | 1.4453

## Slide 7: Overlapping Memory Access: DRE ops
Observation: M1, M2, M3, (M4, M5, E’) again have no significant difference
Chart: Random Access App. Fill Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.15226 | 0.30119 | 0.59834 | 1.955 | 2.3873 | 4.7748 | 9.5416 | 19.0795 | 38.1606 | 76.1869 | 152.3098 | 304.7398 | 609.6542 | 1219.0793 | 2441.405
M2 (ms) | 0.15206 | 0.3008 | 0.59755 | 1.9392 | 2.3841 | 4.7685 | 9.5289 | 19.0542 | 38.11 | 76.0857 | 152.1075 | 304.3351 | 608.8448 | 1217.4607 | 2438.167
M3 (ms) | 0.14832 | 0.29685 | 0.5932 | 1.1883 | 2.3747 | 4.745 | 9.5028 | 18.9907 | 37.9955 | 75.9464 | 151.8868 | 303.8764 | 607.8186 | 1215.2063 | 2430.8469
Chart: Random Access App. Drain Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.1486 | 0.29793 | 0.59473 | 1.1907 | 2.3817 | 4.7562 | 9.5399 | 19.0358 | 38.1075 | 76.1439 | 152.2908 | 304.761 | 609.4099 | 1219.5077 | 2440.3599
M2 (ms) | 0.14841 | 0.29754 | 0.59394 | 1.1892 | 2.3785 | 4.7498 | 9.5272 | 19.0104 | 38.0569 | 76.0426 | 152.0884 | 304.3563 | 608.6005 | 1217.8883 | 2437.1223
M3 (ms) | 0.14822 | 0.29714 | 0.59315 | 1.1876 | 2.3751 | 4.7434 | 9.502 | 18.9808 | 37.9742 | 75.9328 | 151.8523 | 303.8206 | 607.6246 | 1215.151 | 2430.2197
  For overlapping memory access, discrepancy between M1, M2, M3, (M4, M5, E’) is hidden by “pipeline effect”
  Thus, for overlapping memory access, we will use measurements at M3 in this presentation.

## Slide 8: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter examples
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 9: HMC Simulator Selection
CasHMC simulator from Hanyang University
  No information about how results are validated
Micron RTL HMC simulator
  Compilation issues (Not enough from help from Micron to solve problem)
Micron SystemC HMC Simulator
  Signed NDA with Micron to use the tool
  Communicating with Dan Stewart (Micron engineer) to interpret the results

## Slide 10: HMC SytemC Simulator - Architecture
Cycle-accurate simulator developed by Micron
Main modules:
  Synthetic Traffic Generator
  HMC Host Controller
  HMCWrapper
  Monitor
Traffic Generator
  Creates request stream (config.def)
    Read-to-write ratio, request buffer size, etc.
  Uses TLM2.0 interface to send
  read/write requests to Host Controller
HMC Host Controller
  Map requests to links
  Create formatted packets (places in corresponding request buffer)
Trace file reader
  Parses an input trace file and issues requests to the model
Micron Technology, Inc., HMC SystemC Model
Document Revision 1.0 (SVN R194)
Trace file

## Slide 11: Example Trace File for Simulator
Which vault to send the request
Which bank within a vault to send the request
Addressing within the DRAM array

## Slide 12: Example Output (1000 memory reads)
The bandwidth and latency calculations are measured on the pins of the HMC (C point in notional CMC architecture)
Total latency of all request
Values measured in simulator at a point equivalent to C

## Slide 13: Validation Experiments
  Goal: Validate performance measurement on Merlin board
  Approach: Compare
  Merlin board measurement vs.
  HMC SystemC Simulator results
Merlin board
SystemC HMC Simulator
Experiments:
  Comparison of average latency of single memory access (Method 1)
  Comparison of average latency of single memory access (Method 2)
  Comparison of total overlapping latency
  Other experiments
(overlapping memory accesses)

## Slide 14: Optimal Memory Trace
Learning to use & interpret results from SystemC Simulator
  Telecons with Dan Steward
?Accuracy of simulator depends on input memory trace??
Optimal memory trace results in best performance & accuracy (~10% difference) ??
Optimal: to fully utilize internal parallelism of HMC, rotate vault address first, then bank address, and then byte address
  different vaults could work in parallel
  different bank could work in pipeline
Need to discuss and finalize this slide to tell a consistent story.

## Slide 15: Example of Optimal Trace File
Rotate the vaults; same bank & dram
Change the bank after a rotation of vaults
Change the dram after a rotation of banks

## Slide 16: Exp. 1: Avg. Latency, Single Memory Access: (Method 1)
2. Convert memory trace to HT address
Measurement on Merlin board
Simulation on HMC Simulator
1. Input optimal memory trace into simulator
3. Measure latency of each single memory access at M3
4. Calculate average (1000 accesses) latency & compare with avg. latency reported in SystemC Simulator

## Slide 17: Exp. 1: Avg. Latency, Single Memory Access: (Method 1)
Avg. Latency measured over 1000 memory read requests
  tC = Determined from SystemC Simulator: 479.414 ns (equivalent to M5)
Results from SystemC Simulator

## Slide 18: Exp. 1: Avg. Latency, Single Memory Access: (Method 1)
Avg. Latency measured over 1000 memory read requests
Merlin board frequency:167 MHz (6 ns)
Measured Avg. Latency = 88.1 * 6 ns = 528.6 ns
Measured on Merlin board at M3

## Slide 19: Exp. 1: Avg. Latency, Single Memory Access: (Method 1)
Summary
Avg. Latency measured over 1000 memory read requests
tC = determined from SystemC Simulator 479.414 ns (equivalent to M5)
tM3 measured at M3 point on Merlin board: 88.1 * 6 ns = 528.6 ns
(528 – 479) / 479 = 10.23%
(528 – 479) / 479 = 9.28%
Merlin board frequency:167 MHz
According to Dan: difference probably comes from HMCCIF - serialization and de-serialization (i.e., result is even better than 10%)

## Slide 20: Exp. 2: Avg. Latency, Single Memory Access (Method 2: Using overlapping memory requests)
T and D can be measured by two different PERFMON counters at M3
T: time between first req. and last resp. (See Experiment 3 later)
D: time between first req. and last req.
L can be calculated
L is latency of last memory request
L = T – D (Method 2, single memory req.)
Measurement on Merlin board
Overlapping memory requests
Measure M3
D
L
T
Executed code 10000 times to calculate Lavg
Lavg should be comparable to tC (Avg. Latency 479.414 ns) reported in SystemC Simulator

## Slide 21: Experiment 2 Results
Measured results from Merlin board
  (Not yet available) Results will be reported when Merlin board comes back online
Conclusions: (expected)
  Measured results are close to simulator results
  2nd method of validation of single memory access
SystemC Simulator results
  1000 Memory read requests
  Link Avg. Latency = 479.414 ns (just as before)

## Slide 22: Experiment 3 Description
Hypothesis
  In overlapping access (already validated by measurement)
    M1 = M2 = M3 = (M4 = M5 = E’)
  In HMC
    M5 = C
    E = E’
Expect: M1 = M5 (= E’) = C = E (from HMC simulator)
D
L
T
Measure T (total latency) at M1
This is the original slide.
Question: why need to be so complicated? Why can’t we not just measure at M3, like the rest of the experiments? (See modified slide on next page)

## Slide 23: Experiment 3 Description
Recall
  In overlapping access
    M1 = M2 = M3 = (M4 = M5 = E’)
  For HMC
    M5 = C (from simulator
    E = E’ (from simulator
Expect: M1 = M5 (= E’) = C = E (from HMC simulator)
D
L
T
Measure T (total latency) at M3

## Slide 24: Experiment 3 Setup
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube
2. Convert memory trace to HT address
Expect: M1= M5 (= E’) = C = E (from HMC simulator)
Measurement on Merlin board
Simulation on HMC Simulator
1. Input optimal memory trace into simulator

## Slide 25: Experiment 3 Results
SystemC Simulator results
  1000 Memory read requests
  Total overlapping latency
    1683.2ns
Measured results from Merlin board
  (Not yet available) Results will be reported when Merlin board comes back online
Conclusions: (expected)
  Measured results will be close to simulator results

## Slide 26: Other Verification Experiments
Increasing the request count to ~10k
  Simulator produces more accurate results
Implement NOP (No-Operation) on hardware
  Nop means sending Null FLITs on the Link
  Read request takes one FLIT but a read response needs two FLITs, so higher Response Utilization
  Nop helps reduce the response traffic at the expense of slightly reduced bandwidth
Multiplexing Read and Write requests
  Produces better results
  Write takes one Req. and one Res. FLIT
Let’s discuss this slide (unnecessarily complicated)
Results from non-optimal input traces
DRE access patterns
Access patterns of other apps of interests (e.g., bloom filter)
Compared with published data

## Slide 27: SystemC Simulator : 10k Rd. Requests (NOP)
Add 17 NOPs after every 16 Read requests
Let’s discuss this slide Necessary for this meeting?

## Slide 28: SystemC Simulator : 10k Rd. and Wr. Requests
Let’s discuss this slide Necessary for this meeting?

## Slide 29: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter examples
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 30: Verification of PERFMON Code Modification
M1, M2, M3 are measured in PERFMON
  PERFMON – Hardware(Verilog) monitor designed by Convey, modified by CHREC
M4, M5, E’ are not measured
  By observing M1 = M2 = M3, we hypothesize M1 = M2 = M3 = M4 = M5 = E’
Goal: to verify M1, M2, M3 are accurately measured in PERFMON

## Slide 31: Verification of PERFMON Code Modification
Progress
  Set up a RTL simulation of PERFMON in ModelSim, with help from Convey
  Verifying reported PERFMON values cycle by cycle in ModelSim

## Slide 32: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Simulator selection (simulators studied)
      System C HMC simulator from Micron
      System C HMC simulator results
    Comparison to DRE published data
    Validation of PERFMON code modification (Convey testbench)
  Application exploration using HT
    Bloom filter examples
    Sorting algorithms
  Going forward
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 33: Bloom Filter HT Demos
Spell checker
  Input
    A dictionary
    Words to check
  Function
    A bloom filter was pre-set using the dictionary
    A new word was compared against bloom filter to check existence in the dictionary
  Output
    A wrong spelling is reported if the new word doesn’t exist in bloom filter
  HT utilization
    1 HT unit
Let’s discuss this slide

## Slide 34: Bloom Filter HT Demos
Content-based deep packet inspection (longest string match)
  Input
    A group of different-length sensitive words
    Packet to inspect
  Function
    All same-length sensitive words are used to set the same bloom filter
    Multiple bloom filters are pre-set
    A new packet is compared against bloom filters to check existence of sensitive words
  Output
    Report the packet contains sensitive information, if matched
  HT utilization
    16 HT units
Let’s discuss this slide

## Slide 35: Sorting Algorithms
Sorting algorithms being studied
  Bitonic merge sort
  FIFO-Based merge sorter
  Merge-sort trees
  Bucket sort
Details of progress in appendix

## Slide 36: Going Forward
Platform development
Complete validation of CMC platform
Complete development & instrumentation of CMC platform
Develop library for customization of notional CMC architecture under study
  Create user-friendly CMC API
Explore CMC apps using HT
Case studies to explore
Notional CMC architectures
CMC apps, including:
  Data Reordering/Rearrangement Engine, sorting algorithms, bloom filter
Lessons learned, including:
  Characteristics of CMC-amenable apps
  How to re-factor algorithms to become CMC-amenable
Share code and lessons with LPS
Internship for student(s) at LPS?
F1

## Slide 37: Appendix

## Slide 38: Bitonic merge sorter
Input
  Unsorted list of numbers
Function
  First convert an unsorted sequence into Bitonic Sequence
  Need (log2N) cycles to sort a bitonic sequence with N keys
Output
  Sorted list of numbers

## Slide 39: FIFO-Based Merge Sorter - Two Input FIFOs
Input
  Two input FIFOs with sorted list of numbers
Function
  Comparator: compares the FIFO entries and produces an output
  Multiplexer: Comparator output is used to select the Large ( or small) number
Output
  Single output FIFO with sorted list of numbers
5 6 8 12 13
1 3 8 11 17
1 3 5 6 8 8 11 12 13 17

## Slide 40: FIFO-Based Merge Sorter - Multiple cascaded FIFOs
Input
  Tow input FIFOs with sorted list of numbers
Function
  Following functions are performed at each stage
  Comparator: compares the FIFO entries and produces an output
  Multiplexer: Comparator output is used to select the Large ( or small) number
Output
  Single output FIFO with sorted list of numbers

## Slide 41: Merge Sorter Trees
Input
  Large number of sorted lists to be merged (usually in external memory)
Function
  At each horizontal level, two FIFOs are compared to produce one sorted list
  Comparator: compares the FIFO entries and produces an output
  Multiplexer: Comparator output is used to select the Large ( or small) number
Output
  Single output FIFO with sorted list of numbers

## Slide 42: Bucket Sort
Input
  List of unsorted numbers
Function
  Buckets with different range of
  values are created
  Based on the specified ranges, each
  number goes into one particular bucket
  Finally each bucket is sorted
Output
  List of sorted numbers

## Slide 43: Sorting Algorithms - Progress
Currently implementing host applications for following
  Bitonic Merge Sorter
  Bucket Sort
These applications are relatively easy to implement in HT language as they do not require lot of on-chip* memory
Exploring FIFO-based merge sorter methods to see if they are efficient as they require more on-chip memory
on-chip* memory : Block RAM on FPGA