## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Vinayak Deshpande
Jeshalraj Thakaria
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida

## Slide 2: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Experiment 1
      Experiment 2
  Application exploration using HT
    Bloom filter examples
    Bucket sorting examples
  Going forward

## Slide 3: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Experiment 1
      Experiment 2
  Application exploration using HT
    Bloom filter examples
    Bucket sorting examples
  Going forward

## Slide 4: Performance Measurement on Merlin Board
CMC platform on Merlin board
Instrumented Merlin infrastructure with hardware performance monitors
  A’, B’, C’, D’, M1, M2, M3, M4, and M5.
Progress: Able to measure all listed parameters except:
  M4, M5: Cannot measure currently; if necessary will seek help from Convey

## Slide 5: Mapping Notional CMC onto Merlin Board
Simplifying assumption:
For this model, this part of CMC is assumed to have an HMC architecture
Merlin board
Case study: model of a notional CMC*
Observation:
“Pipelining” effect of overlapping memory access
* Nair, R., et al. "Active Memory Cube: A processing-in-memory architecture for exascale systems.“ IBM Journal of Res. & Development 59.2/3 (2015): 17-1.

## Slide 6: Observation: Overlapping Memory Access
For overlapping read/write ops:
Measurements at M1, M2, M3, (M4, M5, E’) have no significant difference
Chart: Overlapping Mem. Read Total Time of M1,2,3 (ms) vs. # Mem Ops.
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0014671 | 0.0057844 | 0.048994 | 0.097222 | 0.14531 | 0.19344 | 0.24155 | 0.28973 | 0.33797 | 0.38602 | 0.43406 | 0.48229 | 0.53029 | 0.57918 | 0.62651 | 0.6753 | 0.72247 | 0.77092 | 0.8192 | 0.86733 | 0.91493 | 0.96356 | 1.0117 | 1.0604 | 1.1073 | 1.156 | 1.2043 | 1.2535 | 1.3017 | 1.348 | 1.3966 | 1.445
M2 (ms) | 0.0012695 | 0.0055868 | 0.048796 | 0.097024 | 0.14511 | 0.19325 | 0.24135 | 0.28953 | 0.33777 | 0.38583 | 0.43386 | 0.48209 | 0.5301 | 0.57898 | 0.62631 | 0.6751 | 0.72228 | 0.77072 | 0.819 | 0.86714 | 0.91474 | 0.96337 | 1.0115 | 1.0602 | 1.1071 | 1.1558 | 1.2041 | 1.2533 | 1.3015 | 1.3478 | 1.3964 | 1.4448
M3 (ms) | 0.0010539 | 0.0053892 | 0.048575 | 0.096796 | 0.1449 | 0.19302 | 0.24116 | 0.28931 | 0.33756 | 0.3856 | 0.43367 | 0.48186 | 0.52988 | 0.57877 | 0.62609 | 0.67489 | 0.72205 | 0.7705 | 0.8188 | 0.8669 | 0.9145 | 0.96316 | 1.0113 | 1.06 | 1.1069 | 1.1555 | 1.2038 | 1.2531 | 1.3013 | 1.3476 | 1.3962 | 1.4446
Chart: Overlapping Mem. Write Total Time of M1,2,3 (ms) vs. # Mem Ops
| 10 | 100 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000 | 21000 | 22000 | 23000 | 24000 | 25000 | 26000 | 27000 | 28000 | 29000 | 30000
M1 (ms) | 0.0020479 | 0.0060838 | 0.049233 | 0.097605 | 0.14559 | 0.19401 | 0.2419 | 0.2902 | 0.33817 | 0.38655 | 0.43444 | 0.48291 | 0.53079 | 0.58008 | 0.62741 | 0.67531 | 0.72349 | 0.77162 | 0.82021 | 0.86833 | 0.91622 | 0.9641 | 1.0138 | 1.0604 | 1.1111 | 1.1591 | 1.2054 | 1.2531 | 1.302 | 1.3494 | 1.3978 | 1.4458
M2 (ms) | 0.0018503 | 0.0058862 | 0.049036 | 0.097407 | 0.14539 | 0.19381 | 0.24171 | 0.29001 | 0.33797 | 0.38635 | 0.43424 | 0.48271 | 0.53059 | 0.57988 | 0.62721 | 0.67511 | 0.72329 | 0.77142 | 0.82001 | 0.86813 | 0.91602 | 0.96399 | 1.0136 | 1.0602 | 1.1109 | 1.1589 | 1.2052 | 1.2529 | 1.3018 | 1.3492 | 1.3976 | 1.4455
M3 (ms) | 0.0016407 | 0.0056587 | 0.04882 | 0.097168 | 0.14518 | 0.1936 | 0.24148 | 0.28978 | 0.33777 | 0.38613 | 0.43401 | 0.48249 | 0.53036 | 0.57966 | 0.62698 | 0.67488 | 0.72307 | 0.77119 | 0.81981 | 0.8679 | 0.91583 | 0.96367 | 1.0134 | 1.06 | 1.1106 | 1.1587 | 1.205 | 1.2527 | 1.3015 | 1.349 | 1.3973 | 1.4453

## Slide 7: Overlapping Memory Access: DRE ops
Observation: M1, M2, M3, (M4, M5, E’) again have no significant difference
Chart: Random Access App. Fill Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.15226 | 0.30119 | 0.59834 | 1.955 | 2.3873 | 4.7748 | 9.5416 | 19.0795 | 38.1606 | 76.1869 | 152.3098 | 304.7398 | 609.6542 | 1219.0793 | 2441.405
M2 (ms) | 0.15206 | 0.3008 | 0.59755 | 1.9392 | 2.3841 | 4.7685 | 9.5289 | 19.0542 | 38.11 | 76.0857 | 152.1075 | 304.3351 | 608.8448 | 1217.4607 | 2438.167
M3 (ms) | 0.14832 | 0.29685 | 0.5932 | 1.1883 | 2.3747 | 4.745 | 9.5028 | 18.9907 | 37.9955 | 75.9464 | 151.8868 | 303.8764 | 607.8186 | 1215.2063 | 2430.8469
Chart: Random Access App. Drain Op. M1,2,3 (ms) vs. log(# Mem. Access)
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
M1 (ms) | 0.1486 | 0.29793 | 0.59473 | 1.1907 | 2.3817 | 4.7562 | 9.5399 | 19.0358 | 38.1075 | 76.1439 | 152.2908 | 304.761 | 609.4099 | 1219.5077 | 2440.3599
M2 (ms) | 0.14841 | 0.29754 | 0.59394 | 1.1892 | 2.3785 | 4.7498 | 9.5272 | 19.0104 | 38.0569 | 76.0426 | 152.0884 | 304.3563 | 608.6005 | 1217.8883 | 2437.1223
M3 (ms) | 0.14822 | 0.29714 | 0.59315 | 1.1876 | 2.3751 | 4.7434 | 9.502 | 18.9808 | 37.9742 | 75.9328 | 151.8523 | 303.8206 | 607.6246 | 1215.151 | 2430.2197
  For overlapping memory access, discrepancy between M1, M2, M3, (M4, M5, E’) is hidden by “pipeline effect”
  Thus, for overlapping memory access, we will use measurements at M3 in this presentation.

## Slide 8: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Experiment 1 – blocking memory access
      Experiment 2 – pipelined memory access
  Application exploration using HT
    Bloom filter examples
  Going forward
  HT Programming Basics

## Slide 9: Validation Experiments
  Validation of performance measurement on Merlin board
Experiments:
  Blocking memory access pattern
    Comparison of average latency of single memory access
  Pipelined memory access pattern
    Comparison of average latency of single memory access
    Comparison of total overlapping latency
Approach
Compare Merlin board measurement vs. Micron HMC SystemC simulator results
vs.

## Slide 10: Exp. 1: Average Latency, Blocking Access
Measurement on Merlin board
Simulation on HMC Simulator
1. Input (e.g. 100,000) blocking memory requests
2. Measure latency of each single memory access at M3
3. Calculate average (e.g. 100,000 accesses) latency & compare with avg. latency reported in SystemC Simulator

## Slide 11: Exp. 1: Average Latency, Blocking Access
Avg. Latency measured on Merlin board
Results from SystemC Simulator

## Slide 12: Exp. 1: Avg. Latency, Blocking Access
Merlin Board
HMC Simulator
freqfpga = 167MHz (6ns/clk)
freqhmc = 333MHz (3ns/clk)
freqsim = 625MHz (1.6ns/clk)
Clk freq.
Assume delay between M3 & M5 is n clkfpga
Average HMC latency on Merlin board:
(clock cycles)
Average HMC latency on HMC simulator:
(clock cycles)
=> n = 58
?
As long as delay between M3 and M5 is validated, the validation can be proved

## Slide 13: Exp. 1: Avg. Latency, Blocking Access
Merlin Board
HMC Simulator
freqfpga = 167MHz (6ns/clk)
freqhmc = 333MHz (3ns/clk)
freqsim = 625MHz (1.6ns/clk)
Clk freq.
Approach:
M3 – M4 delay:
  Setting up RTL simulation of Merlin infrastructure code
  Working on getting Synopsys VCS license
M4 – M5 delay:
  To contact Altera about measurement information of HMCC

## Slide 14: Exp. 2a: Average Latency, Blocking Access
Measurement on Merlin board
Simulation on HMC Simulator
1. Input (e.g. 100,000) pipelined memory requests
2. Measure latency of each single memory access at M3
3. Calculate average (e.g. 100,000 accesses) latency & compare with avg. latency reported in SystemC Simulator

## Slide 15: Exp. 2b: Total Latency, Pipelined
Measurement on Merlin board
Simulation on HMC Simulator
1. Input (e.g. 100,000) pipelined memory requests
Recall (Slide 7)
  In overlapping access
    M1 = M2 = M3 = (M4 = M5)
  For HMC
    M5 = C (from simulator)
D
L
T
Measure T (total latency) at M3 (Tmeasure) & C (Tsim), and compare Tmeasure and Tsim

## Slide 16: Exp. 2 Results – Average Latency
Merlin board
Chart: Memory Read: Total Latency (us) vs. # of memory requests
| 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000
M3 Total overlapping latency (us) | 48.63 | 96.858 | 145.266 | 193.242 | 241.818 | 289.632 | 337.968 | 386.148 | 434.874 | 483.228 | 531.804 | 579.078 | 627.258 | 675.438 | 723.51 | 771.978 | 821.646 | 869.118 | 917.778 | 964.836
Chart: Memory Read: Average Latency (ns) vs. # of memory requests
| 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000
M3 Average latency (ns) | 478.452 | 478.425 | 520.256 | 509.37 | 495.9756 | 509.625 | 497.3554 | 515.301 | 478.6393 | 496.2768 | 514.1809 | 521.3945 | 491.3349 | 479.3443 | 515.6004 | 509.4746 | 514.3193 | 509.082 | 484.3746 | 521.3028
Total Latency
Chart: Memory Read: Average Latency (ns) vs. # of memory requests
| 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000
Sim Average latency (ns) | 88.82 | 89.07 | 88.98 | 89.07 | 89.02 | 89.07 | 89.04 | 89.02 | 89.04 | 89.03 | 89.05 | 89.04 | 89.05 | 89.04 | 89.04 | 89.04 | 89.04 | 89.04 | 89.04 | 89.04
Chart: Memory Read: Total Latency (us) vs. # of memory requests
Sim Total latency (us) | 7.2784 | 14.4944 | 21.6784 | 28.8944 | 36.0784 | 43.2944 | 50.4784 | 57.6944 | 64.8784 | 72.0944 | 79.2784 | 86.4944 | 93.6784 | 100 | 100 | 100 | 100 | 100 | 100 | 100
HMC simulation
Results:
Both average latency keeps stable
Analysis:
FIFO size of HT (Merlin) infrastructure serializes memory request arriving at HMC pin

## Slide 17: Exp. 2 Results – Total Latency
Merlin board
Chart: Memory Read: Total Latency (us) vs. # of memory requests
| 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000
M3 Total overlapping latency (us) | 48.63 | 96.858 | 145.266 | 193.242 | 241.818 | 289.632 | 337.968 | 386.148 | 434.874 | 483.228 | 531.804 | 579.078 | 627.258 | 675.438 | 723.51 | 771.978 | 821.646 | 869.118 | 917.778 | 964.836
Chart: Memory Read: Total Latency (us) vs. # of memory requests
| 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000 | 15000 | 16000 | 17000 | 18000 | 19000 | 20000
Sim Total latency (us) | 7.2784 | 14.4944 | 21.6784 | 28.8944 | 36.0784 | 43.2944 | 50.4784 | 57.6944 | 64.8784 | 72.0944 | 79.2784 | 86.4944 | 93.6784 | 100 | 100 | 100 | 100 | 100 | 100 | 100
HMC simulation
Results:
Both average latency keeps stable
Analysis:
FIFO size of HT (Merlin) infrastructure serializes memory request arriving at HMC pin

## Slide 18: Outline
Brief review & overview
  Performance measurements on Merlin board
  Mapping notional CMC to Merlin board
  Validation of performance measurements on Merlin board
    Validation using HMC simulator
      Experiment 1
      Experiment 2
  Application exploration using HT
    Bloom filter examples
    Sorting examples
  Going forward
  HT Programming Basics
* DRE: Data rearrangement/reordering engine ** CMC Computational Memory Cube

## Slide 19: Bloom Filter HT Demos
Spell checker
  Input
    A dictionary
    Words to check
  Function
    A bloom filter was pre-set using the dictionary
    A new word was compared against bloom filter to check existence in the dictionary
  Output
    A wrong spelling is reported if the new word doesn’t exist in bloom filter
  HT utilization
    1 HT unit

## Slide 20: Bloom Filter HT Demos
Content-based deep packet inspection (longest string match)
  Input
    A group of different-length sensitive words
    Packet to inspect
  Function
    All same-length sensitive words are used to set the same bloom filter
    Multiple bloom filters are pre-set
    A new packet is compared against bloom filters to check existence of sensitive words
  Output
    Report the packet contains sensitive information, if matched
  HT utilization
    16 HT units

## Slide 21: Bucket Sort HT Demos
Sorting an array of numbers
  Input
    Array length (Maximum 1024)
  Function
    Array is initialized with random uniformly distributed integers between 0-256
    Numbers are distributed to the buckets
    Each bucket is sorted individually
    Sorted buckets are concatenated to obtain the sorted array
  Output
    Sorted array is reported
  HT utilization
    1 HT unit

## Slide 22: Going Forward
Platform development
Complete validation of CMC platform
Complete development & instrumentation of CMC platform
Develop library for customization of notional CMC architecture under study
  Create user-friendly CMC API
Explore CMC apps using HT
Case studies to explore
Notional CMC architectures
CMC apps, including:
  Data Reordering/Rearrangement Engine, sorting algorithms, bloom filter
Lessons learned, including:
  Characteristics of CMC-amenable apps
  How to re-factor algorithms to become CMC-amenable
F1
To be discussed