## Slide 1: Prototype Platform for CMC Studies DRE on Merlin Board

## Slide 2: DRE on Merlin Board
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
User app
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
DRE logic
…
Merlin Concepts
DRE logic
Prototype CMC
  Leverage LLNL’s DRE* work for initial prototyping
  Long term: evaluate CMC based on requirements of relevant apps
Tasks
  Study DRE with help of LLNL
  Port DRE to Merlin board using HT
setup
Fill
Drain
DRE commands
DRE: Data Reordering/Rearrangement Engine

## Slide 3: Interaction with LLNL
Porting DRE to Merlin board (discussion with LLNL)
  Approach 1: Reuse DRE’s HDL source code
    Altera counterparts for Xilinx IPs used in DRE need adaptation
    Creating DRE logic from scratch not cost-effective
  Approach 2: Implement DRE using Convey HT (HLL)
    DRE’s functionalities can be implemented using HT
    Discussed performance considerations regarding placement of DRE’s view buffer
DRE applications (available from LLNL)
  Demonstrate functionality of DRE with HMC device
  Obtained source code from LLNL
    Page Rank, Image Differencing, Random Access, SpMV
HLL: High-level language
DRE: Data Reordering/Rearrangement Engine

## Slide 4: Design Option #1
Create HT unit that contains
  One memory Read/Write module, one DRE module (setup, fill, drain logic), and one module for 1/16th of buffer memory
Replicate HT unit 16 times to use all memory ports
Host code
  Read/write to DRE’s view buffer through HT’s host data interfaces
  DRE’s view buffer is located in host memory
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W
Switch Logic
…
Merlin Concepts
DRE
…
…
1/16 Buffer
0
1
14
15
16
17
30
31
CPU
cache
one HT unit
Host Mem
…
View Buffer

## Slide 5: Design Option #2
Create one HT unit that contains
  16 memory Read/Write modules
  Multiple DRE modules
  Buffer shared by DRE modules and connected to the Stream I/F
  Stream I/F to DRE view buffer in host memory
Host code
  Read/Write to view buffer in host memory
CPU
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
0
1
14
15
Stream I/F
cache
Host Mem
…
View Buffer
one HT unit

## Slide 6: Design Option #3
Create an HT unit that contains
  One memory Read/Write module, one DRE module (setup, fill, drain logic)
Replicate HT unit 16 times to use all memory ports
Host code
  Allocate DRE’s view buffer in HMC
  Read/write to DRE’s view buffer through HIX directly or alternatively can use HIX’ data mover to move view buffer into host memory
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W
Switch Logic
…
Merlin Concepts
DRE
…
…
View Buffer
CPU
cache
Host Mem
one HT unit

## Slide 7: Pro-Con of Each Design Option
Option #1
  Pro: Less amount of HT code to write due to utilization of HT-unit replication support
  Con: Host data interfaces may be slow (investigation in progress)
Option #2
  Pro: HT streaming interface may be more performant than host data interface (investigation in progress)
  Cons
    More HT code to write since HT-unit replication cannot be used
    More prone to timing issues when compiling to hardware
Option #3
  Pros:
    Less HT code to write
    Beneficial to certain applications (e.g., reductive sum versus transpose)
  Con: Use extra space in HMC
Pick for better alignment with goal of CMC research

## Slide 8: Conclusions & Going Forward
Option 3 selected for rapid prototyping
  Target date for completion, ~4 weeks
Going forward
  After finishing Option 3 prototype
  Explore Option 4 and 5 (view buffer in FPGA fabric), see next slides

## Slide 9: Design Option #4
Put view buffer into FPGA
  Mapped to virtual addresses of application process
Pro: Clean architecture and potentially better performance
Con: Need modification to Convey’s driver code and FPGA infrastructure
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
View Buffer
0
1
14
15
16
17
30
31
CPU
cache
Host Mem
Translate Virtual Addr. into FPGA BRAM Addr.

## Slide 10: Design Option #5
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
View Buffer
0
1
14
15
16
17
30
31
CPU
cache
Host Mem
Put view buffer into FPGA
  Attach view buffer to switch logic to “hijack” certain direct HMC accesses from host
Pros
  Clean architecture and potentially better performance
  Leverage HIX’s virtual-to-physical address translation
Con: Need modification to FPGA infrastructure