## Slide 1: Potential Projects for HT on Merlin
DRE-related
  Any of the DRE applications:
    page rank, image differencing, random access, SpMV
  Matrix transpose
Other applications
  Smith-Waterman
  Improved bucket sort
  Bloom filter
  FFT
  Radix sort
  SHA1
OpenHT applications
  https://github.com/TonyBrewer/OpenHT/tree/master/apps

## Slide 2: Data Reordering Engine (DRE)*
Applications often show nearly random access patterns to memory
  Apps that manipulate complex, linked data structures
3D stack memory has logic base where processing in memory could be beneficial
  Utilize large in-package bandwidth and reduced latency
DRE
  Use hardware in logic base to traverse and reorder data structures
  Fill and drain operations to gather and scatter blocks of application data
  The goal is to accelerate data access so that CPU cores can compute on complex data efficiently packed into cache
*Maya Gokhale, Scott Lloyd, and Chris Hajas. 2015. Near memory data structure rearrangement. In Proceedings of the 2015 International Symposium on Memory Systems (MEMSYS '15). ACM, New York, NY, USA, 283-290. DOI=http://dx.doi.org/10.1145/2818950.2818986

## Slide 3: DRE Setup, Fill, & Drain Code Examples
inline void drainsp() {
for (size_t i = 0; i < scratchpad_len; i++) {
ref_base[idx_base[spix++]] = scratchpad[i];
if (spix >= idx_len) break;
}
}
void setup(value_pointer refp, size_t elem_sz, index_pointer indexp, int len, value_pointer sp, int sp_len)
{
ref_base = refp;
ref_elem_size = elem_sz;
idx_base = indexp;
idx_len = len;
scratchpad = sp;
scratchpad_len = sp_len;
}
inline void fillsp() {
index_type tmp_idx = spix = curr_idx;
for (size_t i = 0; i < scratchpad_len; i++) {
if (tmp_idx >= idx_len) break;
scratchpad[i] = ref_base[idx_base[tmp_idx++]];
}
}

## Slide 4: DRE on Merlin Board
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
User app
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
DRE logics
…
Merlin Concepts
DRE logics
Prototype CMC
  Leverage LLNL’s DRE* work for initial prototyping
  Long term: evaluate CMC based on requirements of relevant apps
Tasks
  Study DRE with help of LLNL
  Port DRE to Merlin board using HT
setup
Fill
Drain
DRE commands

## Slide 5: Discussion with LLNL
Porting DRE to Merlin board
  Approach: Implement DRE using Convey HT (HLL)
    DRE’s functionalities can be implemented using HT
    Discussed performance considerations regarding placement of DRE’s view buffer
  Also discussed: Reuse DRE’s HDL source code
    Altera counterparts for Xilinx IPs used in DRE not available
    Creating DRE logics from scratch using HDL too costly
DRE applications
  Demonstrate functionality of DRE with HMC device
  Obtained source code from LLNL
    Page rank, image differencing, Random access, SpMV
HLL: High-level language
DRE: Data Reordering/Rearrangement Engine

## Slide 6: Design Option #1
Create HT unit that contains
  One memory Read/Write module, one DRE module (setup, fill, drain logic), and one module for 1/16th of DRE’s view buffer
Replicate HT unit 16 times to use all memory ports
Host code
  Read/write to DRE’s view buffer through HT’s host data interfaces
  View buffer I/O can be unit-number independent for ease of testing
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W
Switch Logic
…
Merlin Concepts
DRE
…
…
1/16 Buffer
0
1
14
15
16
17
30
31
CPU
cache
Host Mem
one HT unit

## Slide 7: Design Option #2
Create one HT unit that contains
  16 memory Read/Write modules
  Multiple DRE modules
  Buffer shared by DRE modules and connected to the Stream I/F
  Stream I/F to DRE view buffer in host memory
Host code
  Read/Write to view buffer in host memory
CPU
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
0
1
14
15
Stream I/F
cache
Host Mem
…
View Buffer
one HT unit

## Slide 8: Design Option #3
Create an HT unit that contains
  One memory Read/Write module, one DRE module (setup, fill, drain logics)
Replicate HT unit 16 times to use all memory ports
Host code
  Allocate DRE’s view buffer in HMC
  Read/write to DRE’s view buffer through HIX’s data mover module
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W
Switch Logic
…
Merlin Concepts
DRE
…
…
View Buffer
CPU
cache
Host Mem
one HT unit

## Slide 9: Pro-Con of Each Design Option
Option #1
  Pro: Less amount of HT code to write due to utilization of HT-unit replication support
  Con: Host data interfaces may be slow (investigation in progress)
Option #2
  Pro: HT streaming interface may be more performant than host data interface (investigation in progress)
  Cons
    More HT code to write since HT-unit replication cannot be used
    More prone to timing issues when compiling to hardware
Option #3
  Pros:
    Less HT code to write
    Performant view-buffer accesses due to optimized HIX data mover
  Con: Use extra space in HMC