## Slide 1: Custom Memory Cube (CMC)
Gongyu Wang
Ph.D candidate

## Slide 2: Agenda
Introduction: Hybrid memory cube (HMC)
Motivation and goals for CMC
Approach to CMC
  Two phases
  FPGA/HMC board – Merlin
Programming Merlin
  Hybrid-threading toolset
Potential RC class course projects

## Slide 3: Introduction
Hybrid memory cube
  High-performance RAM interface for through-silicon vias (TSV)-based stacked DRAM memory
  Logic base (layer)
High bandwidth
  ~10% energy per bit of current DDR memories

## Slide 4: Custom Memory Cube (CMC)
Motivation
  Increasing need for fast and low-power parallel processing
  Memory accesses of data-intensive apps consumes considerable time and power
  HMC presents much higher memory bandwidth than current processors can consume
Goals
  HMC as high-bandwidth memory
    Exploit performance and power advantages
  CMC: Develop a customizable logic layer for HMC
  Offload processing tasks to CMC
    Concepts of C-RAM & PIM (e.g., SIMD, ARM64, & RISC-V in logic layer)
HMC: Hybrid-Memory Cube
C-RAM: Computational RAM
PIM: Processor in Memory
Notes: Hybrid Memory Cube
  Logic layer bound with TSV1 connected DRAM layers
  Improved performance over conventional DRAM
    10X Bandwidth, 1/3 energy consumption, lower latencies

## Slide 5: Approach to CMC
HMC apps
Prototype CMC system
  Use FPGA/HMC boards
Experiment with concepts of C-RAM, PIM, etc.
CMC Prototyping
HMC Studies
Study HMC device using FPGA/HMC boards
Measure and report performance of HMC accesses
HMC: Hybrid-Memory Cube
C-RAM: Computational RAM
PIM: Processor in Memory
2
CMC apps

## Slide 6: Phase 1
HMC studies
  Test and study HMC’s amenability in selected app. domains
    Amenability: bandwidth, latency, power, etc.
    App. Domains: sort, search, cryptography, FFT, etc.
Approach
  Develop test applications on FPGA/HMC board
  Measure report access time of HMC in FPGA and report results
System architecture
Convey Merlin

## Slide 7: Phase 1 with Merlin Board
Goal: test various user apps and report access time of HMC
  Wanted latency: Round-trip latency at inputs of HMCC
  Unwanted latencies: PCIe, HIX, switch logic
  Ability to set parameters of HMC access: packet size, etc.
Approaches to measuring route-trip latency of HMC access
  Direct measurement OR subtract unwanted
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
User app
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
Merlin Concepts
Req.
Res.

## Slide 8: Phase 2
Prototype CMC using FPGA/HMC boards
  Emulate processing capabilities of CMC on FPGA
Tasks
  Define CMC operations based on apps
  Explore processing capabilities
    Data processing: “wide” (many-core) and “shallow” (simple) processors; e.g., SIMD
    Control: e.g., Simplified RISC-V/ARM64
  Develop demo applications
X86 host
DRAM Layers
Logic Layer
CMC Prototype
FPGA fabric
Control processor
wide, shallow processing cores
2

## Slide 9: Phase 2 with Merlin Board
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
User app
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
DRE logic
…
Merlin Concepts
2
DRE logic
Prototype CMC
  Leverage LLNL’s DRE* work for initial prototyping
  Long term: evaluate CMC based on requirements of other relevant apps
Tasks
  Study, port, and modify DRE for our need
    Port to Arria 10 FPGA on Merlin board
  Prototype CMC architecture in FPGA
  Develop demo applications
*DRE: Data Reordering/Rearrangement Engine
setup
Fill
Drain
DRE commands

## Slide 10: Agenda
Introduction: Hybrid memory cube (HMC)
Motivation and goals for CMC
Approach to CMC
  Two phases
  FPGA/HMC board – Merlin
Programming Merlin
  Hybrid-threading toolset
Potential RC class course projects

## Slide 11: Convey HT Background
Convey computers
  Startup since 2006, based @ Texas
  Hybrid-core computing platforms
  Joined CHREC in 2013
    Via F3, focusing on bioinformatics app acceleration
Convey system philosophy – hybrid-core computing
Features | Gidel | Convey | SRC
Programming | C/Cpp + HDL | C/Cpp/ASM + HT + (HDL) | C/C++
Data Addressing | explicit, separate | explict, consistent | implicit
Host Connection | PCIe | FSB, QPI* | PCIe
* via PCIe
HT : Hybrid threading - Convey’s HLS-like programming tool

## Slide 12: Overview of HT Programming Model
Application “call-graph” structure
Personality

## Slide 13: HT Infrastructure
Host-coproc. strucutre
  Message/Data interfaces
HT unit
  Replication mechanism
HT module
  Essential functional blocks
  Memory hierarchy
  Can be replicated
  Messaging interfaces among modules
Instructions
  User-defined behaviors of modules

## Slide 14: User Programmable Parts
Hardware description files (.htd)
  Declare modules, variables, memory interfaces, etc.
Module instruction files (.cpp)
  Define behaviors of modules, including memory I/O, messaging interface, computation, etc.
CTL module example on next slide
  Responsible for:
    Accept calls from host
    Spawn threads onto other HT modules
    Return to host after all threads returned from other HT modules

## Slide 15: HT Code Example
HT
Personality with HT
A
Personality
Fn1
Fn2
Fn3
Fn4
HT tool flow
B
HT Example: Vector-add personality
Vadd Pers.
Control (CTL)
ADD
Ctl.htd
PersCtl_src.cpp
Host message
Variable declaration
Module I/O definition
Interface to other modules
Thread control
Call to ADD module
1 thread
C
Add.htd
PersAdd_src.cpp
128 threads
Memory interface
Memory Operations
Addition

## Slide 16: High-level Design Flow
HT bases on SystemC
  Cycle-accurate simulation
  Weed out inter-cycle bugs
OpenCL
  Behavioral emulation
  Tools handle timing issues

## Slide 17: Potential Course Project
Goals
  Learn HT programming and develop application for Merlin board using HMC device
  Get involved with CMC research
Tasks
  Start with simple code examples
    Hello world, Vadd, Bucket Sort, etc.
  Pick an application
    Smith-Waterman, Radix Sort, Improved bucket sort, DRE, etc.
    Or bring your own application
  Use SystemC simulation to validate design
Bonus task
  Code review with Gongyu Wang
  Compile to bit file and run application on Merlin board