## Slide 1: HMC System C Simulator
Yu Zou
Vinayak Deshpande
MS students
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida

## Slide 2: Agenda
CHREC overview
Notional CMC Architecture
Performance Measurement on Merlin Board
Mapping Notional CMC onto Merlin Board
Validation of Measurements
  HMC Configuration
  Collected Trace File – From Merlin Board
  Generated Trace File – For Simulator
  HMC SytemC Simulator - Architecture
  HMC SytemC Simulator - Results

## Slide 3: What is CHREC?
NSF Center for High-Performance Reconfigurable Computing
  Unique US national research center, operational since January 2007
  Leading ECE/CS research groups @ 3 (soon 4) major universities
    University of Florida (lead)
    Brigham Young University
    Virginia Tech
Under auspices of I/UCRC Program at NSF
  Industry/University Cooperative Research Center
    CHREC is supported by CISE Directorate @ NSF
  CHREC is both National Research Center and Consortium
    University groups serve as research base (faculty, students, staff)
    Industry & government organizations are research partners, sponsors, collaborators, advisory board, & technology-transfer recipients
  Cited by NSF as one of its top national R&D centers
    University of Pittsburgh (lead)
    Brigham Young University
    Virginia Tech
    University of Florida
2017

## Slide 4: CHREC Members
AFRL Sensors Directorate
AFRL Space Vehicles Directorate
Altera
BAE Systems
Boeing
Cisco Systems
Draper Laboratory
Emergent Space Tech
Fermilab
Gidel
Harris
Honeywell
IBM
Innoflight
Laboratory for Physical Sciences
Lockheed-Martin Space Systems
Los Alamos National Laboratory
MIT Lincoln Laboratory
NASA Ames Research Center
NASA Goddard Space Flight Center
NASA Johnson Space Center
NASA Kennedy Space Center
National Instruments
National Security Agency
Office of Naval Research
Raytheon
Rockwell Collins
Sandia National Laboratories
Space Micro
SSE/PlanetiQ
Walt Disney Animation Studios
Xilinx

## Slide 5: Notional CMC* Architecture
Based on Nair et al.** : an HMC with a user-programmable logic layer
A, B, C, D, and : performance-measurement points of interest
* CMC: Custom Memory Cube
** Nair, R., et al. "Active Memory Cube: A processing-in-memory architecture for exascale systems.“ IBM Journal of Res. & Development 59.2/3 (2015): 17-1.

## Slide 6: Performance Measurement on Merlin Board
CMC platform on Merlin board
*
Instrumented Merlin infrastructure with hardware performance monitors
  A’, B’, C’, D’, M1, M2, M3, M4, M5, and E’
Progress: Able to measure all listed parameters except:
  M4, M5: Exploring with help from Convey
  E’: Exploring with help with Micron under NDA
VB*: View Buffer

## Slide 7: Mapping Notional CMC onto Merlin Board
Simplifying assumption:
For this model, this part of CMC is assumed to have an HMC architecture
Merlin board
Case study: model of a notional CMC

## Slide 8: Agenda
CHREC overview
Notional CMC Architecture
Performance Measurement on Merlin Board
Mapping Notional CMC onto Merlin Board
Validation of Measurements
  HMC Configuration
  Collected Trace File – From Merlin Board
  Generated Trace File – For Simulator
  HMC SytemC Simulator - Architecture
  HMC SytemC Simulator - Results

## Slide 9: Validation of Measurement
overlapping memory request:
Measured on Merlin board: D’=M1=M2=M3
Collect memory trace at D’
Input memory trace to simulator’s host
Expect: M5 (= E’) = C = E (from HMC simulator)
Measurement on Merlin board
Simulation on HMC Simulator

## Slide 10: HMC Configuration
Config.def Parameters | Description | Supported Values | Current HMC Configuration On Merlin Bd.
REQUEST_BUFFER_SIZE | Dictates the size of the request buffer (in flits) in the HMC host controller module | Min: 9 Max : - Default:384 | 16 (Simulator does not allow values < 17)
TAGS_PER_LINK | Dictates the number of unique tags that each link has to attach to a particular request | Min:1 Max:512 Default:512 | 512
TOKENS_PER_LINK | Dictates the number of tokens each link has when sending to the cube | Min : 9 Default : 100 Max : 100 | 200 (Simulator accepts values > 100; are results valid?)

## Slide 11: HMC Configuration
Config.def Parameters | Description | Supported Values | Current HMC Configuration On Merlin Bd.
LINK_SPEED | Determines link clock rate | 10, 12.5, 15 Default : 15.0 | 10
LINK_WIDTH | Number of data lanes used on the request and response path of each link | 8 or 16 Default : 16 | 16
MAX_BLOCK_SIZE | Used in address mapping | 32, 64, 128 Default : 64 | 64
config.def

## Slide 12: Collected Trace File – From Merlin Board
memory_trace.log

## Slide 13: Generated Trace File – For Simulator
memory_trace_read.trc
Determines the number of idle link cycles before this request is issued.

## Slide 14: HMC SytemC Simulator - Architecture

## Slide 15: HMC SytemC Simulator - Results
HMCSim_Results

## Slide 16: HMC SytemC Simulator - Results