## Slide 1: CMC Research Platform with DRE as Initial Prototype
Gongyu Wang
PhD candidate
Yu Zou
Vinayak Deshpande
Suvrat Tedia
MS students
CMC: Custom memory Cube
DRE: Data rearrangement engine
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida
Dr. Alan George
Professor of ECE
University of Florida

## Slide 2: Agenda
Overview
  DRE on Merlin board
  Review design options 1-5
Summary of progress
  CHREC Mid-year Workshop 2016
  Current
CMC research platform
  Where are we now?
  Where are we heading?
Appendix
  Performance results of DRE apps so far

## Slide 3: DRE on Merlin Board
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
DRE logic
…
Merlin Concepts
DRE logic
Prototype CMC
  Leverage LLNL’s DRE* work for initial prototyping
  Long term: evaluate CMC based on requirements of relevant apps
Tasks
  Study DRE with help of LLNL
  Port DRE to Merlin board using HT
setup
Fill
Drain
DRE commands
DRE: Data Reordering/Rearrangement Engine
HMC DRAM layers

## Slide 4: Review Design Option #1
Create HT unit that contains
  One memory Read/Write module, one DRE module (setup, fill, drain logic), and one buffer module
Replicate HT unit 16 times to use all memory ports and have 16 DREs
Host code
  Read/write to DRE through HT’s host data interfaces
  DRE’s view buffer is located in host memory
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W
Switch Logic
…
Merlin Concepts
DRE
…
…
Buffer
CPU
cache
One DRE per HT unit
Host Mem
…
View Buffer

## Slide 5: Review Design Option #2
Create one HT unit that contains
  16 memory Read/Write modules
  Multiple DRE modules
  Buffer shared by DRE modules and connected to the stream I/F
  Stream I/F to DRE view buffer in host memory
Host code
  Read/Write to view buffer in host memory
CPU
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
0
1
14
15
Stream I/F
cache
Host Mem
…
View Buffer
one HT unit

## Slide 6: Review Design Option 3
Create an HT unit that contains
  Memory Read/Write module & DRE module (setup, fill, drain logic)
Replicate HT unit 16 times to use all memory ports and have 16 DREs
Host code
  Allocate DRE’s view buffer in HMC
  Read/write to DRE’s view buffer through HIX directly
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W
Switch Logic
…
Merlin Concepts
DRE
…
…
View Buffer
CPU
cache
Host Mem
One DRE per HT unit

## Slide 7: Review Design Option #4
Put view buffer into FPGA
  Mapped to virtual addresses of application process
Pro: Clean architecture and potentially better performance
Con: Need modification to Convey’s driver code and FPGA infrastructure
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
View Buffer
0
1
14
15
16
17
30
31
CPU
cache
Host Mem
Translate Virtual Addr. into FPGA BRAM Addr.

## Slide 8: Review Design Option #5
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
View Buffer
0
1
14
15
16
17
30
31
CPU
cache
Host Mem
Put view buffer into FPGA
  Attach view buffer to switch logic to “hijack” certain direct HMC accesses from host
Pros
  Clean architecture and potentially better performance
  Leverage HIX’s virtual-to-physical address translation
Con: Need modification to FPGA infrastructure

## Slide 9: Summary of Progress
DRE design option 1 | SystemC Simulation | Hardware Execution | Performance Measurement
Page rank |  |  | 
Random access |  |  | 
Image differencing |  |  | 
SpMV |  |  | 
DRE design option 3 | SystemC Simulation | Hardware Execution | Performance Measurement
Page rank |  |  | 
Random access |  |  | 
Image differencing |  |  | 
SpMV |  |  | 
CMW’16
Since CMW’16

## Slide 10: Agenda
Overview
  DRE on Merlin board
  Review design options 1-5
Summary of progress
  CHREC Mid-year Workshop 2016
  Current
CMC research platform
  Where are we now?
  Where are we heading?
Appendix
  Performance results of DRE apps so far

## Slide 11: Concept of CMC Platform (Review)
Motivation
  Explore designs of CMC architectures
  Early design & test of CMC apps
  Co-design of app & arch.
Host
DRAM layers
Envisioned CMC

## Slide 12: Envisioned CMC & Performance Points
A
B
D
E
A: CMC performance + data transfer performance
  A = B + data transfer
B: CMC performance
  B = C + D+ E
C: CMC-logic latency
D: HMC switch-VC latency
E: DRAM latency
2-link x16 4GB HMC
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
CMC logic
…
Host
C
Notes: Changed C

## Slide 13: Correspondent Performance Points
A: CMC performance + data transfer performance
  A = B + data transfer
B: CMC performance
  B = C + D + E
C: CMC-logic latency
D: HMC switch-VC latency
E: DRAM latency
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
Merlin* board MA100
CMC logic
A
B
D
E
2-link x16 4GB HMC
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
CMC logic
…
Host
C
C
Notes: Explain to me the F & G bullet in tomorrow’s morning meeting.

## Slide 14: Computation of Target Delays (Challenges)
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
Merlin* board MA100
CMC logic
A
B
F
G
D
E
Black dotted lines: available measurement pts.
  A, B: as defined before
  F, G: Provided perfmon logic: memory access latency from those points
Green dotted lines: additional target points
  E: DRAM delay
  D: More dynamic delay (queue, overflow)
  C: Somehow measure CMC logic latency
Challenges: How to measure, calculate, or integrate C, D, E?
2-link x16 4GB HMC
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
CMC logic
…
Host
C
C
Notes: Discuss (explain to me) the “Approach to target delays” bullet

## Slide 15: Computation of Target Delays (Discussion)
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
Merlin* board MA100
CMC logic
A
B
F
G
D
E
C
How to measure, calculate, or integrate C, D, E?
  Start with sequence HMC requests
    Measure C, Measure G, and subtract GD delay
    Challenge: derive GD delay
  Extend to concurrent HMC requests
    Challenge: overlapping compute and memory accesses makes it difficult to integrate C, D, & E delays
Notes: Discuss (explain to me) the “Approach to target delays” bullet

## Slide 16: Example with DRE Page Rank
Measurement points A, B, F, and G available on our CMC platform
Measurement results of DRE page rank shown above
  Design option 3, graph scale 2^24
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
Merlin* board MA100
CMC logic
CMC buffer
A
B
F
G
D
E
A | B | F | G | D | E
666.5sec | 3136510131 cycles | 280568847867 cycles | 280568847867 cycles | TBD | TBD
C
Notes: Discuss in morning meeting

## Slide 17: Additional Issues (For Future Discussion)
CMC buffer of CMC platform is in HMC
  Measured delays can be used for estimating buffer access times directly
CMC buffer in FPGA
  May need additional measurement points
  Need to enable such buffer first (work in progress)
PCIe emulating serial links of CMC/HMC?
Alternatively, subtract PCIe delay and add serial link delay (calculated/simulated)
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
Merlin* board MA100
CMC logic
CMC buf.
…
CMC buf.
…
CMC buffer
A
B
F
G
D
E
2-link x16 4GB HMC
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
CMC logic
…
Host
CMC buf.
…
CMC buffer
C

## Slide 18: Conclusions
Functioning initial CMC prototype
  Exploring alternative DRE designs (functions/apps)
  Exploring alternative CMC architectures (e.g., buffer placement)
  Has basic performance measuring capabilities
From lessons learned thus, re-focusing CMC research
  Relate components of CMC research platform to conceptual CMC device
  Identified target measurement points
  Laid foundation for computing target points using CMC research platform
Notes: Modified conclusions slide

## Slide 19: Moving Forward (Based on Today’s Discussion)
Continue investigating design option 5 & 4
  Reading Convey infrastructure HDL code to find out how to enable design option 5 and then 4
  Glen offered Q&A session with Merlin-board engineers of Micron/Convey
R&D into computing target delays
  Using available measurement methods
  Can add more measurement points if needed
Continue using DRE as initial CMC prototype
Notes: Modified title

## Slide 20: Appendix

## Slide 21: Summary of Progress
DRE design option 1 | SystemC Simulation | Hardware Execution | Performance Measurement
Page rank |  |  | 
Random access |  |  | 
Image differencing |  |  | 
SpMV |  |  | 
DRE design option 3 | SystemC Simulation | Hardware Execution | Performance Measurement
Page rank |  |  | 
Random access |  |  | 
Image differencing |  |  | 
SpMV |  |  | 
CMW’16
Since CMW’16

## Slide 22: Interaction with LLNL
Previous telecon
  Presented page-rank app working on Merlin board
    Design option 1 and 3
  Two execution modes: baseline & CMC
  Discussion
    Unfair comparison between exe. modes for design option 1
    No cache is bad idea for DRE in general
HLL: High-level language
DRE: Data Reordering/Rearrangement Engine

## Slide 23: Page Rank Results
Graph Scale |  | 2^12 | 2^13 | 2^14 | 2^15 | 2^16 | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23 | 2^24
Direct access (no DRE) | t_oper | 0.34 | 0.76 | 1.44 | 2.99 | 5.94 | 11.97 | 24.03 | 48 | 95.98 | 195.6 | 387.94 | 766.43 | 1631.63
 | t_btMINEDGE | 0.24 | 0.41 | 0.81 | 2.05 | 3.91 | 7.8 | 18.05 | 33.08 | 72.62 | 148.6 | 280.2 | 617.04 | 1274.39
 | t_rest | 0.1 | 0.35 | 0.63 | 0.94 | 2.03 | 4.17 | 5.98 | 14.92 | 23.36 | 47 | 107.74 | 149.39 | 357.24
Design Option3 with 1 DRE | t_oper | 0.23 | 0.55 | 1.09 | 2.04 | 4.1 | 8.39 | 16.24 | 34.97 | 66.53 | 127.15 | 268.78 | 514.31 | 1020.14
 | t_btMINEDGE | 0.17 | 0.2 | 0.42 | 1.15 | 2.11 | 4.36 | 10.41 | 19.14 | 41.57 | 81.84 | 156.32 | 357.4 | 666.5
 | t_rest | 0.06 | 0.35 | 0.67 | 0.89 | 1.99 | 4.03 | 5.83 | 15.83 | 24.96 | 45.31 | 112.46 | 156.91 | 353.64
 | t_setup | 0 | 0 | 0.02 | 0 | 0 | 0.02 | 0.07 | 0.14 | 0.2 | 0.6 | 0.45 | 1.83 | 2.67
 | t_fill | 0.01 | 0.02 | 0.03 | 0.09 | 0.08 | 0.25 | 0.86 | 1.22 | 2.66 | 5.9 | 6.78 | 22.01 | 30.51
Design Option2 with 1 DRE | t_oper |  |  |  |  |  |  |  |  |  |  |  |  | 
 | t_btMINEDGE |  |  |  |  |  |  |  |  |  |  |  |  | 
 | t_rest |  |  |  |  |  |  |  |  |  |  |  |  | 
 | t_setup |  |  |  |  |  |  |  |  |  |  |  |  | 
 | t_fill |  |  |  |  |  |  |  |  |  |  |  |  | 
Design Option1 with 1 DRE | t_oper | 0.14 | 0.33 | 0.71 | 1.01 | 2.28 | 4.56 | 7.39 | 16.73 | 27.8 | 54.74 | 129.39 | 192.01 | 415.6
 | t_btMINEDGE | 0.02 | 0.02 | 0.05 | 0.16 | 0.19 | 0.4 | 1.1 | 2.09 | 4.28 | 8.2 | 15.73 | 36.29 | 70.21
 | t_rest | 0.12 | 0.31 | 0.66 | 0.85 | 2.09 | 4.16 | 6.29 | 14.64 | 23.52 | 46.54 | 113.66 | 155.72 | 345.39
 | t_setup | 0 | 0 | 0 | 0 | 0 | 0 | 0.02 | 0.02 | 0.01 | 0.05 | 0.01 | 0.24 | 0.15
 | t_fill | 0.01 | 0.02 | 0.04 | 0.16 | 0.18 | 0.37 | 1.04 | 1.98 | 4.07 | 7.64 | 14.81 | 34.05 | 65.81
64-bit memory loads (will try 64-B loads in future)
Option 1 runs faster than option 3 but takes longer to fill view buffer

## Slide 24: Random Access
Table Size |  | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23 | 2^24 | 2^25 | 2^26 | 2^27 | 2^28 | 2^29 | 2^30 | 2^31
Direct access (no DRE) | t_oper | 0.01 | 0 | 0.01 | 0.03 | 0.02 | 0.08 | 0.17 | 0.29 | 0.53 | 1.12 | 2.12 | 4.28 | 8.68 | 17.04 | 33.41
 | t_ran | 0 | 0 | 0.01 | 0 | 0 | 0.02 | 0.02 | 0.03 | 0.08 | 0.17 | 0.35 | 0.57 | 1.35 | 2.76 | 4.93
 | t_compute | 0.01 | 0 | 0 | 0.03 | 0.02 | 0.06 | 0.15 | 0.26 | 0.45 | 0.95 | 1.77 | 3.71 | 7.33 | 14.28 | 28.48
Design Option3 with 1 DRE | t_oper | 0 | 0 | 0.02 | 0.03 | 0.02 | 0.09 | 0.19 | 0.34 | 0.68 | 1.26 | 2.52 | 4.96 | 10.12 | 19.19 | 38.93
 | t_setup | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | t_fill | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.02 | 0 | 0.2 | 0.01 | 0.05 | 0.16 | 0.31 | 0.53
 | t_drain | 0 | 0 | 0 | 0.01 | 0 | 0 | 0 | 0 | 0 | 0.3 | 0.04 | 0.11 | 0.16 | 0.44 | 0.74
 | t_ran | 0 | 0 | 0 | 0.02 | 0 | 0.02 | 0.03 | 0.05 | 0.08 | 0.19 | 0.47 | 1.03 | 1.79 | 3.19 | 6.7
 | t_compute | 0 | 0 | 0.02 | 0.01 | 0.02 | 0.07 | 0.16 | 0.29 | 0.6 | 1.07 | 2.05 | 3.93 | 8.33 | 16 | 32.23
Design Option2 with 1 DRE | t_oper |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | t_setup |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | t_fill |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | t_drain |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design Option1 with 1 DRE | t_oper | 0 | 0 | 0 | 0 | 0.02 | 0.01 | 0.03 | 0.07 | 0.15 | 0.31 | 0.59 | 1.15 | 2.2 | 4.64 | 9.17
 | t_setup | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | t_fill | 0 | 0 | 0 | 0 | 0 | 0.01 | 0.01 | 0.01 | 0.05 | 0.11 | 0.21 | 0.38 | 0.78 | 1.44 | 3.07
 | t_drain | 0 | 0 | 0 | 0 | 0.02 | 0 | 0 | 0.06 | 0.06 | 0.19 | 0.22 | 0.55 | 0.95 | 2.17 | 4.33
t_oper | operation time |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
t_setup | DRE setup time |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
t_fill | DRE fill time |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
t_drain | DRE drain time |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
t_compute | t_oper-t_ran |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
t_ran | random generation time |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
64-bit memory loads, random-number generation on host
Investigating why DRE has shown worse performance than direct access
  Will try 64-B memory access with DRE

## Slide 25: Image Differencing
Image Width (or Height) |  | 2^9 | 2^10 | 2^11 | 2^12 | 2^13 | 2^14
Direct access (no DRE) | t_oper | 0.14 | 0.55 | 2.21 | 9.01 | 35.82 | 144.78
Design Option3 with 1 DRE | t_oper | 0.14 | 0.57 | 2.26 | 8.98 | 36.54 | 146.18
 | t_setup | 0 | 0 | 0 | 0 | 0 | 0
 | t_fill | 0 | 0.02 | 0.02 | 0.09 | 0.47 | 1.62
 | t_drain |  |  |  |  |  | 
Image Width |  | 2^9 | 2^10 | 2^11 | 2^12 | 2^13 | 2^14
Direct access (no DRE) | t_oper | 0.07 | 0.28 | 1.13 | 4.47 | 17.79 | 72.46
Design Option3 with 1 DRE | t_oper | 0.07 | 0.28 | 1.11 | 4.44 | 18.48 | 71.79
 | t_setup | 0 | 0 | 0 | 0 | 0 | 0
 | t_fill | 0 | 0 | 0 | 0.01 | 0 | 0.02
 | t_drain |  |  |  |  |  | 
Image Width |  | 2^9 | 2^10 | 2^11 | 2^12 | 2^13 | 2^14
Direct access (no DRE) | t_oper | 0.08 | 0.28 | 1.11 | 4.44 | 17.89 | 72.45
Design Option3 with 1 DRE | t_oper | 0.01 | 0.04 | 0.2 | 0.76 | 3 | 11.95
 | t_setup | 0 | 0 | 0 | 0 | 0 | 0
 | t_fill | 0 | 0 | 0 | 0 | 0.01 | 0.02
 | t_drain |  |  |  |  |  | 
2 images
8-bit memory loads
1 images
8-bit memory loads
1 images
64-bit memory loads
In future: 32-bit memory loads in direct-access mode; 64-B memory loads with DRE

## Slide 26: SpMV
Matrix Scale |  | 2^16 | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23 | 2^24
Direct access (no DRE) | t_oper | 3.38 | 6.74 | 13.46 | 26.77 | 53.25 | 113.15 | 225.56 | 450.93 | 902.42
 | t_btMinCol | 3.31 | 6.57 | 13.07 | 25.88 | 51.74 | 109.95 | 219.35 | 437.66 | 876.62
 | t_rest | 0.07 | 0.17 | 0.39 | 0.89 | 1.51 | 3.2 | 6.21 | 13.27 | 25.8
Design Option3 with 1 DRE | t_oper | 3.26 | 6.55 | 12.88 | 26.03 | 51.75 | 110.23 | 218.69 | 410.1 | 865.18
 | t_btMinCol | 3.25 | 6.55 | 12.88 | 26.02 | 51.74 | 110.18 | 218.65 | 409.99 | 865.02
 | t_rest | 0.01 | 0 | 0 | 0.01 | 0.01 | 0.05 | 0.04 | 0.11 | 0.16
 | t_setup | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | t_fill | 0.03 | 0.05 | 0.06 | 0.26 | 0.61 | 1.1 | 2.05 | 3.88 | 4.94
Design Option2 with 1 DRE | t_oper |  |  |  |  |  |  |  |  | 
 | t_setup |  |  |  |  |  |  |  |  | 
 | t_fill |  |  |  |  |  |  |  |  | 
 | t_drain |  |  |  |  |  |  |  |  | 
Design Option1 with 1 DRE | t_oper |  |  |  |  |  |  |  |  | 
 | t_setup |  |  |  |  |  |  |  |  | 
 | t_fill |  |  |  |  |  |  |  |  | 
 | t_drain |  |  |  |  |  |  |  |  | 
In future: 64-bit memory loads in direct-access mode; 64-B memory loads with DRE

## Slide 27: DRE Setup, Fill, & Drain Examples w/ Page Rank
void dre::setup(value_pointer refp, size_t elem_sz, index_pointer indexp, int len, value_pointer sp, int sp_len)
{
//Send register data to coprocessor
pHtHif->SendAllHostMsg(REF_ADDR, (uint64_t)ref_base);
pHtHif->SendAllHostMsg(IDX_ADDR, (uint64_t)idx_base);
pHtHif->SendAllHostMsg(SP_ADDR, (uint64_t)scratchpad);
pHtHif->SendAllHostMsg(IDX_LEN, (uint64_t)idx_len);
pHtHif->SendAllHostMsg(SP_LEN, (uint64_t)scratchpad_len);
}
inline void dre::fillsp() {
index_type tmp_idx = spix = curr_idx;
for (int unit = 0; unit < unitCnt; unit++)
pAuUnits[unit]->SendCall_htmain(FILL, tmp_idx, unit /*offset*/, unitCnt /*stride*/);
for (int unit = 0; unit < unitCnt; unit++) {
while (!pAuUnits[unit]->RecvReturn_htmain())
usleep(1000);
}
}
for (gsize_t i = 0; i < num_vertices; ++i) {
// Loop over adjacency list
for (gsize_t j = 0; j < edges; ++j) {
tmp += cur_pr[edge_i[j]];
}
tmp = jump_prob + (d_factor * tmp);
next_pr[i] = tmp;
}
for (gsize_t i = 0; i < num_vertices; ++i) {
dre.setup((value_pointer)cur_pr, sizeof(double), (index_pointer) edge_i, edges,
scratchpad, block_sz);
// Loop over adjacency list
dre.init_loop(); // calls dre.fillsp() within
for (int i = 0; i < dre.ialen(); i++)
tmp += dre.get(); // calls dre.fillsp() within and read view buffer on HMC
// …
Same DRE APIs

## Slide 28: DRE Setup, Fill, & Drain Examples w/ Page Rank
inline void drainsp() {
for (size_t i = 0; i < scratchpad_len; i++) {
ref_base[idx_base[spix++]] = scratchpad[i];
if (spix >= idx_len) break;
}
}
void setup(value_pointer refp, size_t elem_sz, index_pointer indexp, int len, value_pointer sp, int sp_len)
{
ref_base = refp;
ref_elem_size = elem_sz;
idx_base = indexp;
idx_len = len;
scratchpad = sp;
scratchpad_len = sp_len;
}
inline void fillsp() {
index_type tmp_idx = spix = curr_idx;
for (size_t i = 0; i < scratchpad_len; i++) {
if (tmp_idx >= idx_len) break;
scratchpad[i] = ref_base[idx_base[tmp_idx++]];
}
}
for (gsize_t i = 0; i < num_vertices; ++i) {
// Loop over adjacency list
for (gsize_t j = 0; j < edges; ++j) {
tmp += cur_pr[edge_i[j]];
}
tmp = jump_prob + (d_factor * tmp);
next_pr[i] = tmp;
}
for (gsize_t i = 0; i < num_vertices; ++i) {
dre.setup((value_pointer)cur_pr, sizeof(double), (index_pointer) edge_i, edges, scratchpad, block_sz);
// Loop over adjacency list
dre.fill();
for (int i = 0; i < prIA.ialen(); i++) {
tmp += dre.get();
}
}

## Slide 29: Performance Measurements
Performance measurements for HMC accesses
  Two measurement methods of latency/bandwidth
    CPU measurement from view of host application
    FPGA measurement using PERFMON logic of Convey PDK
  Two running modes
    Host only
      CPU code directly accessing HMC
    CMC
      CMC computation on FPGA accessing HMC in highly parallel fashion
Support of measurement methods
  Both measurement methods work with CMC mode
  PERFMON does not work with host-only mode

## Slide 30: PERMON Concept Diagram
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
…
Merlin Concepts
DREs
…
CPU
cache
Host Mem
Virtual MCs
Switch logic
xb_rs
Crossbar
…
…
…
…
PERFMON logic is located in core logic
  Not measuring direct HMC accesses that originated from host (through the blue lines)
Custom PERFMON logic need to be built to support
  FPGA measurement in host-only mode
  Closer-to-HMCC measurement for either mode
xb_rq
Pers_PERFMON
MC_PERFMON

## Slide 31: GUPS Performance
PERFMON output average latencies
Results consistent with GUPS results
Log(GUPS) on FPGA shows orders of magnitude perf. gain
CMC shows speedup if host-only is baseline

## Slide 32: STREAM Performance
PERFMON outputs average latencies
Results show nearly constant difference between Pers & MC PERFMON measurements
It is possible to separate clock counts for each STREAM kernel
HT performance number seems low
Order of magnitude perf. gain of HT over host-only

## Slide 33: PERFMON Results Need Validation
**MC Interface**
Interface Load Cycles Stores Cycles Stall RQ Stall RS Read Trans Write Trans Atomic Trans
---------- --------------- --------------- --------------- --------------- --------------- --------------- ---------------
port00 508213 337144 0 0 507065 337144 0
port01 508761 337144 0 0 507613 337144 0
port02 10094 288 0 0 8946 288 0
port03 10377 288 0 0 9229 288 0
port04 6908 288 0 0 6908 288 0
port05 7226 288 0 0 7226 288 0
port06 505597 337144 0 0 505597 337144 0
port07 505904 337144 0 0 505904 337144 0
port08 508306 336972 0 0 508306 336972 0
port09 509058 336972 0 0 509058 336972 0
port10 10155 280 0 0 10155 280 0
port11 10162 280 0 0 10162 280 0
port12 5996 244 0 0 5996 244 0
port13 6912 244 0 0 6912 244 0
port14 505568 336936 0 0 505568 336936 0
port15 505403 336936 0 0 505403 336936 0
========== =============== =============== =============== =============== =============== TOTAL 4124640 2698592 0 0 4120048 2698592 0
STREAM with Array Size = 2^16
Imbalanced load/store distribution among ports

## Slide 34: GUPS Perf. Results
Size | 2^16 | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23 | 2^24 | 2^25 | 2^26 | 2^27 | 2^28 | 2^29
HT GUPs | 0.080215 | 0.095881 | 0.12068 | 0.130711 | 0.13948 | 0.148305 | 0.152353 | 0.155882 | 0.159712 | 0.162431 | 0.163855 | 0.164173 | 0.16412 | 0.163775
MC perf_mon |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Avg. LD latency | 1059.6 | 968.7 | 884.2 | 877.5 | 868.4 | 866.2 | 866.4 | 865.8 | 865.9 | 866.3 | 867.2 | 867.6 | 870.3 | 873.5
Avg. ST Latency | 1099.3 | 995.6 | 901.9 | 889.0 | 877.9 | 872.6 | 870.7 | 869.4 | 868.4 | 868.3 | 868.2 | 868.4 | 870.8 | 874
Pers perf_mon |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Avg. LD Latency | 1164.1 | 1081.4 | 1004.5 | 1005.9 | 1002.7 | 1004.4 | 1006.8 | 1008 | 1009.5 | 1010.5 | 1012.1 | 1012.7 | 1015.7 | 1019.1
Avg. ST Latency | 1201.5 | 1105.8 | 1019.5 | 1014 | 1008.7 | 1007 | 1007.3 | 1007.6 | 1008 | 1008.4 | 1009.2 | 1009.5 | 1012.1 | 1015.5
Host-only GUPS (24 OMP threads) | 0.00425 | 0.004537 | 0.004731 | 0.004839 | 0.004879 | 0.004898 | 0.004905 | 0.004915 | 0.004924 | 0.004945 | 0.00494 | 0.004917 | 0.004945 | 0.004934

## Slide 35: STREAM Perf. Results
Size | 2^16 | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23 | 2^24 | 2^25 | 2^26 | 2^27
HT Bandwidth (GB/s) |  |  |  |  |  |  |  |  |  |  |  | 
Copy | 0.9645 | 0.9492 | 1.2801 | 1.2691 | 1.2852 | 1.3169 | 1.3149 | 1.321 | 1.3236 | 1.3238 | 1.3239 | 1.3243
Scale | 0.9576 | 0.9596 | 1.2801 | 1.267 | 1.2832 | 1.3182 | 1.3142 | 1.3208 | 1.3246 | 1.3237 | 1.3244 | 1.3244
Add | 0.7175 | 0.9501 | 1.1566 | 1.267 | 1.3209 | 1.2999 | 1.3205 | 1.3229 | 1.3236 | 1.3228 | 1.3227 | 1.3231
Triad | 0.7178 | 0.9524 | 1.1559 | 1.2697 | 1.2818 | 1.3177 | 1.3172 | 1.3226 | 1.3234 | 1.3225 | 1.3232 | 1.3229
MC perf_mon |  |  |  |  |  |  |  |  |  |  |  | 
Avg. LD latency | 1434.1 | 1476.4 | 1511.1 | 1529.9 | 1543.8 | 1551 | 1553.2 | 1560.1 | 1555.5 | 1560.1 | 1577 | 1593.5
Avg. ST Latency | 1478.3 | 1521.6 | 1556.1 | 1577.1 | 1594.7 | 1603 | 1606.4 | 1616.7 | 1609.8 | 1615.2 | 1641 | 1666
Pers perf_mon |  |  |  |  |  |  |  |  |  |  |  | 
Avg. LD Latency | 1756.5 | 1793.1 | 1823.3 | 1840.8 | 1849.6 | 1854.7 | 1855.7 | 1859.7 | 1856.9 | 1860.3 | 1871.2 | 1879.5
Avg. ST Latency | 1793.4 | 1824.5 | 1849.4 | 1867.4 | 1877.1 | 1881.6 | 1883.3 | 1889.3 | 1885.1 | 1888.7 | 1905.6 | 1918.9
HostOnly (OMP 24 threads) Bandwidth (GB/s) |  |  |  |  |  |  |  |  |  |  |  | 
Copy | 0.0829 | 0.0831 | 0.0845 | 0.0848 | 0.0838 | 0.0833 | 0.0824 | 0.0817 | 0.0807 | 0.0801 | 0.08 | 0.0797
Scale | 0.0837 | 0.084 | 0.0837 | 0.0836 | 0.0841 | 0.0832 | 0.0826 | 0.0817 | 0.081 | 0.0801 | 0.0798 | 0.0797
Add | 0.0758 | 0.0764 | 0.0767 | 0.077 | 0.0765 | 0.0765 | 0.076 | 0.0752 | 0.0762 | 0.0755 | 0.0757 | 0.0755
Triad | 0.076 | 0.0765 | 0.0778 | 0.0776 | 0.0765 | 0.0761 | 0.0762 | 0.0755 | 0.0759 | 0.0758 | 0.0756 | 0.0755