## Slide 1: HT Programming
Yu Zou
Graduate Student
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida

## Slide 2: Outline
HT programming basics
CHREC framework
  Merlin infrastructure
  PERFMON code
  User-friendly host API
DRE app. PageRank example

## Slide 3: Outline
HT programming basics
CHREC framework
  Merlin infrastructure
  PERFMON code
  User-friendly host API
DRE app. PageRank example

## Slide 4: Convey HT Background
Convey computers
  Startup since 2006, based @ Texas
  Hybrid-core computing platforms
  Joined CHREC in 2013
    Via F3, focusing on bioinformatics app acceleration
Convey system philosophy – hybrid-core computing
Features | Convey
Programming | C/Cpp/ASM + HT + (HDL)
Data Addressing | explict, consistent
Host Connection | PCIe 2.0/3.0
HT : Hybrid threading - Convey’s HLS-like programming tool

## Slide 5: Overview of HT Programming Model
Application “call-graph” structure

## Slide 6: HT Infrastructure
Host-coproc. strucutre
  Message/Data interfaces
HT unit
  Replication mechanism
HT module
  Essential functional blocks
  Memory hierarchy
  Can be replicated
  Messaging interfaces among modules
Instructions
  User-defined behaviors of modules

## Slide 7: HT Toolset
Supported variable type
  Private variable
  Shared variable
  Global variable
Supported data type
  uint64_t, uint32_t
  ht_uint1_t, ht_uint2_t, …, ht_uint64_t
  ht_int1_t, ht_int2_t, … , ht_int64_t

## Slide 8: User Programmable Parts
Host source files
  Define program behaviors on the host, including data transmission, control flow, user interface, etc.
Hardware description files (.htd)
  Declare modules, variables, memory interfaces, etc.
Module instruction files (.cpp)
  Define behaviors of modules, including memory I/O, messaging interface, computation, etc.

## Slide 9: High-level Design Flow

## Slide 10: HT Code Example
HT
Personality with HT
A
Personality
Fn1
Fn2
Fn3
Fn4
HT tool flow
B
HT Example: Vector-add personality
Vadd Pers.
Control (CTL)
ADD
Ctl.htd
PersCtl_src.cpp
Host message
Variable declaration
Module I/O definition
Interface to other modules
Thread control
Call to ADD module
1 thread
C
Add.htd
PersAdd_src.cpp
128 threads
Memory interface
Memory Operations
Addition

## Slide 11: Outline
HT programming basics
CHREC framework
  Merlin infrastructure
  PERFMON code
  User-friendly host API
DRE app. PageRank example

## Slide 12: Merlin Infrastructure
By reverse-engineering Verilog code
167 MHz (6ns/clk)
334 MHz (3ns/clk)

## Slide 13: Key Components
HIX – host-FPGA interface
HIX_TLB
  Translate virtual address from host to physical address
  For host directly access HMC
CMC – HT logic

## Slide 14: Key Components
Crossbar
  Up to 16 HT units can be used
  Route memory request from different units to corresponding memory controller
MC – there are 4 memory controllers

## Slide 15: Key Components
MC_TLB
  Translate virtual address from HT logic to phys. addr.
HMC_IF
  Reformat memory request, e.g. adding tags
  Group access to each vault and schedule priority

## Slide 16: CHREC Framework v0.1 - HW
Achievements:
Added three clock counters: PERS_PERFMON, MC_PERFMON, HMC_IF_PERFMON
Modified based on PERFMON code provided by Convey/Micron
  Memory access for board configuration were also counted
  Filtered out irrelevant memory access, isolated memory access from HT logic

## Slide 17: CHREC Framework v0.1 - HW
Achievements:
PERS_PERFMON
  Roundtrip latency of HT logic memory request
MC_PERFMON
  Roundtrip latency of access to memory controller
HMC_IF_PERFMON
  The closest point to HMC that we can currently measure

## Slide 18: CHREC Framework v0.1 - HW
Limitations
  Only one memory controller and one HMCC are used
    Inefficient use of HMC
  Size of some FIFO is decreased to isolate memory access from HT logic
    Not fully utilize HMC bandwidth
Ongoing work
  Changing FIFO size to increase utilization of HMC bandwidth
  To refine PERFMON code to enable all MCs and HMCCs in the future

## Slide 19: CHREC Framework v0.1 - SW
User-friendly API – CHREC_MON
  Easy to read PERFMON data from FPGA
After completion of HT logic
Create a CHREC_MON object
Call CHREC_MON_READ() function
PERFMON data will be read and stored into corresponding arrays
Display

## Slide 20: CHREC Framework v0.1 - SW
Original PERFMON host code provided by Convey/Micron

## Slide 21: Outline
HT programming basics
CHREC framework
  Merlin infrastructure
  PERFMON code
  User-friendly host API
DRE App. PageRank Example

## Slide 22: DRE* setup, fill, drain
void setup(value_pointer refp, index_pointer indexp, value_pointer sp)
{
ref_base = refp;
idx_base = indexp;
scratchpad = sp;
}
void fill() {
for (size_t i = 0; i < scratchpad.length(); i++) {
scratchpad[i] = ref_base[idx_base[i]];
}
}
void drain() {
for (size_t i = 0; i < scratchpad.length(); i++) {
ref_base[idx_base[i]] = scratchpad[i];
}
}
*Data Reordering/Rearrangement Engine by Lawrence Livermore National Lab

## Slide 23: DRE PageRank Example
./app –s 15 –p 54067
Host is using TCP/IP to access PERFMON data, port number is required

## Slide 24: Appendix

## Slide 25: Introduction
Hybrid memory cube
  High-performance RAM interface for through-silicon vias (TSV)-based stacked DRAM memory
  Logic base (layer)
High bandwidth
  ~10% energy per bit of current DDR memories

## Slide 26: Advantage of HMC
High bandwidth comes from internal parallelism
  Vaults can be accessed in parallel
  Banks can be accessed in pipeline
But not enough ! ! !
  Pins constrain max. bandwidth
  Bottleneck for data-intensive
  apps
    Big data, e.g. PageRank
    Gnome research, e.g. DNA
    sequencing

## Slide 27: High Bandwidth of CMC
HMC configuration
  16 HMCs are chained together
  Size – 8 GB
  64 bit vertical interface each DRAM partition
  32 vaults per cube
  TSV signaling rate 2 Gb/s
  8 high-speed external serial links
Available external bandwidth – 320 GB/s
Available internal bandwidth – 8 TB/s
25x

## Slide 28: Bloom Filter HT Demos
Spell checker
  Input
    A dictionary
    Words to check
  Function
    A bloom filter was pre-set using the dictionary
    A new word was compared against bloom filter to check existence in the dictionary
  Output
    A wrong spelling is reported if the new word doesn’t exist in bloom filter
  HT utilization
    1 HT unit

## Slide 29: Bloom Filter HT Demos
Content-based deep packet inspection (longest string match)
  Input
    A group of different-length sensitive words
    Packet to inspect
  Function
    All same-length sensitive words are used to set the same bloom filter
    Multiple bloom filters are pre-set
    A new packet is compared against bloom filters to check existence of sensitive words
  Output
    Report the packet contains sensitive information, if matched
  HT utilization
    16 HT units