## Slide 1: Prototype Platform for CMC Studies — DRE on Merlin Board
Gongyu Wang
PhD candidate
Shefali Gundecha
Riju John Xavier
Yu Zou
MS students
CMC: Custom memory Cube
DRE: Data reording engine
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida
Dr. Alan George
Professor of ECE
University of Florida

## Slide 2: Agenda
DRE on Merlin board
  Design Option 3 implemented
  Functionality validated via page rank application
Performance monitoring (PERFMON) logic
  GUPS and STREAM results
Conclusions and moving forward

## Slide 3: DRE on Merlin Board
Host
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
User app
Switch Logic
…
…
VC #0
Switch
VC #N
…
…
…
Link#0
Link#1
DRE logic
…
Merlin Concepts
DRE logic
Prototype CMC
  Leverage LLNL’s DRE* work for initial prototyping
  Long term: evaluate CMC based on requirements of relevant apps
Tasks
  Study DRE with help of LLNL
  Port DRE to Merlin board using HT
setup
Fill
Drain
DRE commands
DRE: Data Reordering/Rearrangement Engine

## Slide 4: Interaction with LLNL
Porting DRE to Merlin board (discussion with LLNL)
  Approach 1: Reuse DRE’s HDL source code
    Altera counterparts for Xilinx IPs used in DRE need adaptation
    Creating DRE logic from scratch not cost-effective
  Approach 2: Implement DRE using Convey HT (HLL)
    DRE’s functionalities can be implemented using HT
    Discussed performance considerations regarding placement of DRE’s view buffer
DRE applications (available from LLNL)
  Demonstrate functionality of DRE with HMC device
  Obtained source code from LLNL
    Page Rank, Image Differencing, Random Access, SpMV
HLL: High-level language
DRE: Data Reordering/Rearrangement Engine

## Slide 5: DRE Setup, Fill, & Drain Examples w/ Page Rank
inline void drainsp() {
for (size_t i = 0; i < scratchpad_len; i++) {
ref_base[idx_base[spix++]] = scratchpad[i];
if (spix >= idx_len) break;
}
}
void setup(value_pointer refp, size_t elem_sz, index_pointer indexp, int len, value_pointer sp, int sp_len)
{
ref_base = refp;
ref_elem_size = elem_sz;
idx_base = indexp;
idx_len = len;
scratchpad = sp;
scratchpad_len = sp_len;
}
inline void fillsp() {
index_type tmp_idx = spix = curr_idx;
for (size_t i = 0; i < scratchpad_len; i++) {
if (tmp_idx >= idx_len) break;
scratchpad[i] = ref_base[idx_base[tmp_idx++]];
}
}
for (gsize_t i = 0; i < num_vertices; ++i) {
// Loop over adjacency list
for (gsize_t j = 0; j < edges; ++j) {
tmp += cur_pr[edge_i[j]];
}
tmp = jump_prob + (d_factor * tmp);
next_pr[i] = tmp;
}
for (gsize_t i = 0; i < num_vertices; ++i) {
dre.setup((value_pointer)cur_pr, sizeof(double), (index_pointer) edge_i, edges, scratchpad, block_sz);
// Loop over adjacency list
dre.fill();
for (int i = 0; i < prIA.ialen(); i++) {
tmp += dre.get();
}
}

## Slide 6: Design Option 3
Create an HT unit that contains
  Memory Read/Write module & DRE module (setup, fill, drain logic)
Replicate HT unit 16 times to use all memory ports
Host code
  Allocate DRE’s view buffer in HMC
  Read/write to DRE’s view buffer through HIX directly
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W
Switch Logic
…
Merlin Concepts
DRE
…
…
View Buffer
CPU
cache
Host Mem
one HT unit

## Slide 7: Progress of Design Option 3
Implemented DRE using HT
  Maintained same API signatures of DRE commands
    Setup, fill, and drain
  DRE view buffer is allocated on HMC
Validated via page rank application
  Modifications
    Move page rank vector, adjacency lists of each vertex to HMC
    Change setup() and fillsp() of DRE to use HT APIs
      Code snippets on next slide
      Can use multiple HT units (each contains one DRE) to fill
  Our modified page rank runs and results check out
    Results in subsequent slides
rmat scale: 23
view_size: 4096
min_edges: 128
RMAT generation, vertices:8388608
RMAT generation, edges:134217728
RMAT generation, bytes:1140850688
RMAT generation, time:935.21 sec, EPS:143516
PageRank Vectors, bytes:134217728
num_edges = 134217728, edgeCnt = 268435456 (should be 2x num_edges)
sig_hex:0xfde8001000108000 sig_ctime:0x57048832
wrt sig_hex:0xfde8001000108000 sig_ctime:0x0
TotalUnitCnt = 16, #AUs = 1
page rank time:512.08 sec
Setup time: 0 sec
Reorg time: 0 sec
Oper. time: 512.08 sec
Cache time: 0 sec
Convey time: 14.9 sec
errors:0

## Slide 8: DRE Setup, Fill, & Drain Examples w/ Page Rank
void dre::setup(value_pointer refp, size_t elem_sz, index_pointer indexp, int len, value_pointer sp, int sp_len)
{
//Send register data to coprocessor
pHtHif->SendAllHostMsg(REF_ADDR, (uint64_t)ref_base);
pHtHif->SendAllHostMsg(IDX_ADDR, (uint64_t)idx_base);
pHtHif->SendAllHostMsg(SP_ADDR, (uint64_t)scratchpad);
pHtHif->SendAllHostMsg(IDX_LEN, (uint64_t)idx_len);
pHtHif->SendAllHostMsg(SP_LEN, (uint64_t)scratchpad_len);
}
inline void dre::fillsp() {
index_type tmp_idx = spix = curr_idx;
for (int unit = 0; unit < unitCnt; unit++)
pAuUnits[unit]->SendCall_htmain(FILL, tmp_idx, unit /*offset*/, unitCnt /*stride*/);
for (int unit = 0; unit < unitCnt; unit++) {
while (!pAuUnits[unit]->RecvReturn_htmain())
usleep(1000);
}
}
for (gsize_t i = 0; i < num_vertices; ++i) {
// Loop over adjacency list
for (gsize_t j = 0; j < edges; ++j) {
tmp += cur_pr[edge_i[j]];
}
tmp = jump_prob + (d_factor * tmp);
next_pr[i] = tmp;
}
for (gsize_t i = 0; i < num_vertices; ++i) {
dre.setup((value_pointer)cur_pr, sizeof(double), (index_pointer) edge_i, edges,
scratchpad, block_sz);
// Loop over adjacency list
dre.init_loop(); // calls dre.fillsp() within
for (int i = 0; i < dre.ialen(); i++)
tmp += dre.get(); // calls dre.fillsp() within and read view buffer on HMC
// …
Same DRE APIs

## Slide 9: Page Rank Results (1 & 16 DREs)
16 DRE
  FPGA runtime longer than 1 DRE
    Due to 16 * DRE dispatch delay
Low perf. problem?
  1 or 16 DREs
1 DRE
  FPGA runtime shorter than non-FPGA
  Non-FPGA runtime dominated by reading view buffer (on HMC)

## Slide 10: Page Rank Results (Cont.)
Good news: perf. with DRE better than without
  Characteristic of CMC research platform
16 DRE is bad “optimization”
  Due to dominating view-buffer access time
  More computation-centric optimization can considerably improve perf.
    E.g., moving accumulation of page rank to FPGA

## Slide 11: Agenda
DRE on Merlin board
  Design Option 3 implemented
  Functionality validated via page rank application
Performance measurement
  Status of measurement methods
  GUPS and STREAM results
Conclusions and moving forward

## Slide 12: Performance Measurements
Performance measurements for HMC accesses
  Two measurement methods of latency/bandwidth
    CPU measurement from view of host application
    FPGA measurement using PERFMON logic of Convey PDK
  Two running modes
    Host only
      CPU code directly accessing HMC
    CMC
      CMC computation on FPGA accessing HMC in highly parallel fashion
Support of measurement methods
  Both measurement methods work with CMC mode
  PERFMON does not work with host-only mode

## Slide 13: PERMON Concept Diagram
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
…
Merlin Concepts
DREs
…
CPU
cache
Host Mem
Virtual MCs
Switch logic
xb_rs
Crossbar
…
…
…
…
PERFMON logic is located in core logic
  Not measuring direct HMC accesses that originated from host (through the blue lines)
Custom PERFMON logic need to be built to support
  FPGA measurement in host-only mode
  Closer-to-HMCC measurement for either mode
xb_rq
Pers_PERFMON
MC_PERFMON

## Slide 14: GUPS Performance
PERFMON output average latencies
Results consistent with GUPS results
Log(GUPS) on FPGA shows orders of magnitude perf. gain
CMC shows speedup if host-only is baseline

## Slide 15: STREAM Performance
PERFMON outputs average latencies
Results show nearly constant difference between Pers & MC PERFMON measurements
It is possible to separate clock counts for each STREAM kernel
HT performance number seems low
Order of magnitude perf. gain of HT over host-only

## Slide 16: PERFMON Results Need Validation
**MC Interface**
Interface Load Cycles Stores Cycles Stall RQ Stall RS Read Trans Write Trans Atomic Trans
---------- --------------- --------------- --------------- --------------- --------------- --------------- ---------------
port00 508213 337144 0 0 507065 337144 0
port01 508761 337144 0 0 507613 337144 0
port02 10094 288 0 0 8946 288 0
port03 10377 288 0 0 9229 288 0
port04 6908 288 0 0 6908 288 0
port05 7226 288 0 0 7226 288 0
port06 505597 337144 0 0 505597 337144 0
port07 505904 337144 0 0 505904 337144 0
port08 508306 336972 0 0 508306 336972 0
port09 509058 336972 0 0 509058 336972 0
port10 10155 280 0 0 10155 280 0
port11 10162 280 0 0 10162 280 0
port12 5996 244 0 0 5996 244 0
port13 6912 244 0 0 6912 244 0
port14 505568 336936 0 0 505568 336936 0
port15 505403 336936 0 0 505403 336936 0
========== =============== =============== =============== =============== =============== TOTAL 4124640 2698592 0 0 4120048 2698592 0
STREAM with Array Size = 2^16
Imbalanced load/store distribution among ports

## Slide 17: Agenda
DRE on Merlin board
  Design Option 3 implemented
  Functionality validated via page rank application
Performance monitoring (PERFMON) logic
  GUPS and STREAM results
Conclusions and moving forward

## Slide 18: Conclusions
Host-only mode can serve as baseline of CMC
DRE is implemented on Merlin board using HT
  Design option 3 shows low raw performance
  Speedup when compared to baseline (host-only)
Two performance measurement methods
  CPU and FPGA measurements
  Both works for CMC mode
  Only CPU measurement works for host-only mode

## Slide 19: Moving Forward
Investigating design option 5 & 4
  Reading Convey infrastructure HDL code to find out how to enable design option 5 and then 4
  Glen confirm that both options should be possible but may require much effort
Validation of STREAM results & PERFMON logic
  In progress with help from Glen
Enable PERFMON with DRE design
  In progress

## Slide 20: Discussion
Any comments on current PERFMON logic?
Evaluate options for custom PERFMON logic
  Closer-to-HMCC
    Granularity? HT memory access data unit OR HMC packet
  Support for host-only mode
    Can be included in above option
    Granularity? CPU memory access width OR
DRE
  More DRE applications
    Should at least test DRE’s drain command w/ another DRE app.
  Optimization of DRE applications
    Unroll loop in host code to better utilize multiple DREs
    Move computation to FPGA
Move onto CMC application suggested by LPS
  E.g., Bloom filter

## Slide 21: Appendix
Two slides of concept diagrams of DRE design option 5 & 4
Two slides of complete data tables of performance measurements for GUPS and STREAM

## Slide 22: Design Option #5
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
View Buffer
0
1
14
15
16
17
30
31
CPU
cache
Host Mem
Put view buffer into FPGA
  Attach view buffer to switch logic to “hijack” certain direct HMC accesses from host
Pros
  Clean architecture and potentially better performance
  Leverage HIX’s virtual-to-physical address translation
Con: Need modification to FPGA infrastructure

## Slide 23: Design Option #4
Put view buffer into FPGA
  Mapped to virtual addresses of application process
Pro: Clean architecture and potentially better performance
Con: Need modification to Convey’s driver code and FPGA infrastructure
PCIe Gen3 X8
Arria 10 GX1150
2-link x16 4GB HMC
HIX
HMCC
HMCC
…
Mem. R/W’s
Switch Logic
…
Merlin Concepts
DREs
…
…
View Buffer
0
1
14
15
16
17
30
31
CPU
cache
Host Mem
Translate Virtual Addr. into FPGA BRAM Addr.

## Slide 24: GUPS Perf. Results
Size | 2^16 | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23 | 2^24 | 2^25 | 2^26 | 2^27 | 2^28 | 2^29
HT GUPs | 0.080215 | 0.095881 | 0.12068 | 0.130711 | 0.13948 | 0.148305 | 0.152353 | 0.155882 | 0.159712 | 0.162431 | 0.163855 | 0.164173 | 0.16412 | 0.163775
MC perf_mon |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Avg. LD latency | 1059.6 | 968.7 | 884.2 | 877.5 | 868.4 | 866.2 | 866.4 | 865.8 | 865.9 | 866.3 | 867.2 | 867.6 | 870.3 | 873.5
Avg. ST Latency | 1099.3 | 995.6 | 901.9 | 889.0 | 877.9 | 872.6 | 870.7 | 869.4 | 868.4 | 868.3 | 868.2 | 868.4 | 870.8 | 874
Pers perf_mon |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Avg. LD Latency | 1164.1 | 1081.4 | 1004.5 | 1005.9 | 1002.7 | 1004.4 | 1006.8 | 1008 | 1009.5 | 1010.5 | 1012.1 | 1012.7 | 1015.7 | 1019.1
Avg. ST Latency | 1201.5 | 1105.8 | 1019.5 | 1014 | 1008.7 | 1007 | 1007.3 | 1007.6 | 1008 | 1008.4 | 1009.2 | 1009.5 | 1012.1 | 1015.5
Host-only GUPS (24 OMP threads) | 0.00425 | 0.004537 | 0.004731 | 0.004839 | 0.004879 | 0.004898 | 0.004905 | 0.004915 | 0.004924 | 0.004945 | 0.00494 | 0.004917 | 0.004945 | 0.004934

## Slide 25: STREAM Perf. Results
Size | 2^16 | 2^17 | 2^18 | 2^19 | 2^20 | 2^21 | 2^22 | 2^23 | 2^24 | 2^25 | 2^26 | 2^27
HT Bandwidth (GB/s) |  |  |  |  |  |  |  |  |  |  |  | 
Copy | 0.9645 | 0.9492 | 1.2801 | 1.2691 | 1.2852 | 1.3169 | 1.3149 | 1.321 | 1.3236 | 1.3238 | 1.3239 | 1.3243
Scale | 0.9576 | 0.9596 | 1.2801 | 1.267 | 1.2832 | 1.3182 | 1.3142 | 1.3208 | 1.3246 | 1.3237 | 1.3244 | 1.3244
Add | 0.7175 | 0.9501 | 1.1566 | 1.267 | 1.3209 | 1.2999 | 1.3205 | 1.3229 | 1.3236 | 1.3228 | 1.3227 | 1.3231
Triad | 0.7178 | 0.9524 | 1.1559 | 1.2697 | 1.2818 | 1.3177 | 1.3172 | 1.3226 | 1.3234 | 1.3225 | 1.3232 | 1.3229
MC perf_mon |  |  |  |  |  |  |  |  |  |  |  | 
Avg. LD latency | 1434.1 | 1476.4 | 1511.1 | 1529.9 | 1543.8 | 1551 | 1553.2 | 1560.1 | 1555.5 | 1560.1 | 1577 | 1593.5
Avg. ST Latency | 1478.3 | 1521.6 | 1556.1 | 1577.1 | 1594.7 | 1603 | 1606.4 | 1616.7 | 1609.8 | 1615.2 | 1641 | 1666
Pers perf_mon |  |  |  |  |  |  |  |  |  |  |  | 
Avg. LD Latency | 1756.5 | 1793.1 | 1823.3 | 1840.8 | 1849.6 | 1854.7 | 1855.7 | 1859.7 | 1856.9 | 1860.3 | 1871.2 | 1879.5
Avg. ST Latency | 1793.4 | 1824.5 | 1849.4 | 1867.4 | 1877.1 | 1881.6 | 1883.3 | 1889.3 | 1885.1 | 1888.7 | 1905.6 | 1918.9
HostOnly (OMP 24 threads) Bandwidth (GB/s) |  |  |  |  |  |  |  |  |  |  |  | 
Copy | 0.0829 | 0.0831 | 0.0845 | 0.0848 | 0.0838 | 0.0833 | 0.0824 | 0.0817 | 0.0807 | 0.0801 | 0.08 | 0.0797
Scale | 0.0837 | 0.084 | 0.0837 | 0.0836 | 0.0841 | 0.0832 | 0.0826 | 0.0817 | 0.081 | 0.0801 | 0.0798 | 0.0797
Add | 0.0758 | 0.0764 | 0.0767 | 0.077 | 0.0765 | 0.0765 | 0.076 | 0.0752 | 0.0762 | 0.0755 | 0.0757 | 0.0755
Triad | 0.076 | 0.0765 | 0.0778 | 0.0776 | 0.0765 | 0.0761 | 0.0762 | 0.0755 | 0.0759 | 0.0758 | 0.0756 | 0.0755