## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Vinayak Deshpande
Suvrat Tedia
MS students
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida
Dr. Gongyu Wang
Dr. Alan George
Professor of ECE
University of Florida

## Slide 2: Review & Overview
DRE* on Merlin board
  Notional CMC** architecture
  Explored design options (design options 1 – 5)
  Implemented DRE prototypes on Merlin-board CMC platform
    Design options 1, 2, & 3
    SpMV app (using HT) with design options 1 and 3
    Image differencing app (using HT) with design option 3
Performance measurement on Merlin board for CMC
  Performance measurement on notional CMC architecture
  Performance modeling of CMC arch. on Merlin board
    Performance measurement
    Challenges & solutions
    Where are we now?
    Where are we heading (CAW16)?
* DRE: Data rearrangement/reorder engine ** CMC Custom Memory Cube
Notes: When we first started working on the Merlin board, we concentrated on the design and implementation of the data rearrangement engine (DRE) on the Merlin board. Implementation of DRE prototypes is interesting, but unless we can make useful performance measurement, the usefulness of the CMC platform is limited.

## Slide 3: Notional CMC Architecture
Simplified view: an HMC with a user-programmable logic layer

## Slide 4: DRE Prototype on CMC Architecture
View buffer (VB) can be set up inside the HMC (design option 3) or inside CMC logic (design option 4)
VB4
VB3

## Slide 5: Review & Overview
DRE* on Merlin board
  Notional CMC** architecture
  Explore design options (design options 1 – 5)
  DRE prototypes on Merlin-board CMC platform
    Design options 1, 2, & 3
    SpMV app (using HT) with design options 1 and 3
    Image processing app (using HT) with design option 3
Performance measurement on Merlin board for CMC
  Performance measurement on notional CMC architecture
  Performance modeling of CMC arch. on Merlin board
    Performance measurement
    Challenges & solutions
    Where are we now?
    Where are we heading (CAW16)?
* DRE: Data rearrangement/reorder engine ** CMC Custom Memory Cube

## Slide 6: Performance Measurement
Desired observation points
A: Host latency
B: CMC latency
C: CMC component delay
D: Latency of HMC internal data access
  Local-vault and non-local-vault accesses cause different latencies
E: Latency of DRAM layer access
  Inside vault, row buffer hit & row buffer miss will cause different latencies
T: Transfer delay
  Depends on design option (where the view buffer is stored)
  Notional CMC architecture
* Latency: delay from input into a point in the system to desired outcome
T

## Slide 7: Mapping of Observation Points to Merlin Platform
latency A = latency B + delay T
latency B = latency B’ – delay F’minusD’
delay C = delay C’
latency D = latency D’
latency E = latency E’
delay T = some function of T’ (depends on design option)
F’minusD’
T’
T
Notes: T is command + result data transfer back to host; depends on design options and where results are stored (HMC, DDR, FPGA fabric, etc)

## Slide 8: Performance Measurement on Merlin Board
A’ is measured in host code
B’, C’, F’ are measured in HT code (CMC logic)
T’ to be determined
Delay F’minusD’ = latency F’ – latency D’
If we cannot obtain D’ and E’ from Micron (or while waiting for NDA)
latency D’ = latency G’ – latency G’_D’ = latency G’ – (VirtualMC module latency + HMCC module latency + HMC link latency)
latency E’ cannot be measured; but may be determined using simulation tools
latency A = latency A’
latency B = latency B’ – delay F’minusD’
delay C = delay C’
latency D = latency D’
latency E = latency E’
delay T = some function of T’ (depends on design option)
F’minusD’
T’

## Slide 9: Approach for Challenge D’
latency D’ = latency G’ – delay F’minusD’ = latency G’ – (VirtualMC module latency + HMCC module latency + HMC link latency)
Latency G’ (round-trip)
  Collaborating with Convey to debug PERFMON code
VirtualMC module latency
  Implemented as TLB (Translation Look-aside Buffer) in code
  Non-deterministic
  Will collaborate with Convey
HMCC module latency
  Collaborating with Altera
F’minusD’
T’

## Slide 10: Approach for Challenge G’
PERFMON
  PERFMON view of Merlin platform
  Hardware monitor designed by Convey
Notes: Pers_PERFMON and MC_PERFMON are verilog module names

## Slide 11: Approach for Challenge G’ (Contd.)
Roadblock
  Total LD latency measured in PERFMON code (189,232 cycles) inconsistent with latency measured in app HT code (742 cycles)
  Consulted with Convey: PERFMON code collects other memory accesses (including host, infrastructure) in addition to memory accesses from app (HT code)
Notes: Results measured by PERFMON code not what we needed (not incorrect)

## Slide 12: Approach for Challenge G’ (Contd.)
Solution
  Found method to isolate memory accesses (modified PERFMON code)
  Validated modification by comparing measured F’ (from PERFMON) against F’ measured in application HT code
  Similarly, we can apply modification to measure G’
measured in modified PERFMON
measured in app (HT)
Notes: Figures shows F’ measured in PERFMON is consistent with F’ measured in HT code
Now we have determined F’, in a similar manner, we can determine G’.

## Slide 13: VirtualMC module latency
  Will collaborate with Convey
  How we currently understand problem (from analyzing infrastructure code):
    TLB translates virtual memory addresses to physical addresses
    Delay is not consistent (e.g., long delay can be caused by TLB miss)
    Possible solutions:
      Statistical model?
      Increase page-table size to minimize TLB misses?
Notes: TLB Translation Lookaside Buffer – a memory cache to translate virtual address to physical address

## Slide 14: Benchmarking to Determine A, B, C, and F
A’ is measured in host code
B’, C’, F’ are measured in HT code (CMC logic)
latency D’ = latency G’ – latency G’_D’ = latency G’ – (VirtualMC module latency + HMCC module latency + HMC link latency)
latency E’ cannot be measured; but may be determined using simulation tools
F’minusD’
T’
Notes: These are the observation points that we can currently measure.

## Slide 15: Benchmarking Results: Single Mem. Rd/Wr
Operations | A’ (ns) | B’ (cycles) | C’ (cycles) | F’ (cycles)
Single memory read | 1058559 | 168.4414 | 4 | 164.4414
Single memory write | 1057302 | 175.6587 | 4 | 171.6587
A’ measured inside host application using timers
B’, C’ and F’ are measured inside the HT code (CMC logic) using counters
T’

## Slide 16: Measure B’
B’ is measured in HT code
  Starting point of CMC
  Ending point of CMC
starting time of B’
ending time of B’
latency B’
Operations | A’ (ns) | B’ (cycles) | C’ (cycles) | F’ (cycles)
Single memory read | 1058559 | 168.4414 | 4 | 164.4414
Single memory write | 1057302 | 175.6587 | 4 | 171.6587
T’

## Slide 17: Measure C’
starting time of B’ & C’
latency C’
ending time of C’
C’ is measured in HT code
  Starting point of CMC logic
  Ending point of CMC logic
Operations | A’ (ns) | B’ (cycles) | C’ (cycles) | F’ (cycles)
Single memory read | 1058559 | 168.4414 | 4 | 164.4414
Single memory write | 1057302 | 175.6587 | 4 | 171.6587
T’

## Slide 18: Measure F’
ending time of C’;
starting time of F’
ending time of B’
latency F’
F’ is measured in HT code
  Point of issuing memory request
  Point of receiving memory response
Operations | A’ (ns) | B’ (cycles) | C’ (cycles) | F’ (cycles)
Single memory read | 1058559 | 168.4414 | 4 | 164.4414
Single memory write | 1057302 | 175.6587 | 4 | 171.6587
T’

## Slide 19: Going Forward (CAW16)
Complete performance measurement on Merlin board for single-memory operation
  Finish measurement of latency HMCC, latency G’, latency F’_D’, latency VirtualMC
Map results to model of envisioned CMC architecture
Apply lessons learned to conduct experiments to measure DRE operations