## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Vinayak Deshpande
Suvrat Tedia
MS students
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida
Dr. Gongyu Wang
Dr. Alan George
Professor of ECE
University of Florida

## Slide 2: Review & Overview
DRE* on Merlin board
  Notional CMC** architecture
  Explored design options (design options 1 – 5)
  Implemented DRE prototypes on Merlin-board CMC platform
    Design options 1, 2, & 3
    SpMV app (using HT) with design options 1 and 3
    Image differencing app (using HT) with design option 3
Performance measurement on Merlin board for CMC
  Performance measurement on notional CMC architecture
  Performance modeling of CMC arch on Merlin board
    Performance measurement
    Challenges
    Where are we now?
    Where are we heading (CAW16)?
* DRE: Data rearrangement engine ** CMC Computational Memory Cube
Notes: When we first started working on the Merlin board, we concentrated on the design and implementation of the data rearrangement engine (DRE) on the Merlin board. Implementation of DRE prototypes is interesting, but unless we can make useful performance measurement, the usefulness of the CMC platform is limited.

## Slide 3: Notional CMC Architecture

## Slide 4: DRE Prototype on CMC Arch.
View buffer can be set up inside the HMC or inside the CMC logic

## Slide 5: Review & Overview
DRE* on Merlin board
  Notional CMC** architecture
  Explore design options (design options 1 – 5)
  DRE prototypes on Merlin-board CMC platform
    Design options 1, 2, & 3
    SpMV app (using HT) with design options 1 and 3
    Image processing app (using HT) with design option 3
Performance measurement on Merlin board for CMC
  Performance measurement on notional CMC architecture
  Performance modeling of CMC arch on Merlin board
    Performance measurement
    Challenges
    Where are we now?
    Where are we heading (CAW16)?
* DRE: Data rearrangement engine ** CMC Computational Memory Cube
Notes: When we first started working on the Merlin board, we concentrated on the design and implementation of the data rearrangement engine (DRE) on the Merlin board. Implementation of DRE prototypes is interesting, but unless we can make useful performance measurement, the usefulness of the CMC platform is limited.

## Slide 6: Performance Measurement
A: Host latency
B: CMC latency
C: CMC component delay
D: Latency of HMC internal data access
  Local-vault and non-local-vault accesses cause different latencies
E: Latency of DRAM layer access
  Inside vault, row buffer hit & row buffer miss will cause different latencies
  Notional CMC architecture
* Latency: delay from input into a point in the system to desired outcome

## Slide 7: Performance Modeling of CMC Arch. Option 3
latency A = latency A’
latency B = latency B’ – delay F’minusD’
delay C = delay C’
latency D = latency D’
latency E = latency E’
F’minusD’

## Slide 8: Performance Modeling of CMC Arch. Option 4
latency A = latency A’
Transfer delay X =
latency B = latency B’ – delay F’minusD’
delay C = delay C’
latency D = latency D’
latency E = latency E’
F’minusD’
Notes: X is command + result data transfer back to host; depends on design options and where results are stored (HMC, DDR, FPGA fabric, etc)

## Slide 9: Review & Overview
DRE* on Merlin board
  Notional CMC** architecture
  Explore design options (design options 1 – 5)
  DRE prototypes on Merlin-board CMC platform
    Design options 1, 2, & 3
    SpMV app (using HT) with design options 1 and 3
    Image processing app (using HT) with design option 3
Performance measurement on Merlin board for CMC
  Performance measurement on notional CMC architecture
  Performance modeling of CMC arch on Merlin board
    Performance measurement
    Challenges
    Where are we now?
    Where are we heading (CAW16)?
* DRE: Data rearrangement engine ** CMC Computational Memory Cube
Notes: When we first started working on the Merlin board, we concentrated on the design and implementation of the data rearrangement engine (DRE) on the Merlin board. Implementation of DRE prototypes is interesting, but unless we can make useful performance measurement, the usefulness of the CMC platform is limited.

## Slide 10: Performance Measurement on Merlin Board
A’ is measured in host code
B’, C’, F’ are measured in HT code
Delay F’minusD’ = latency F’ – latency D’
latency D’ = latency G’ – latency G’_D’ = latency G’ – (VirtualMC module latency + HMCC module latency + HMC link latency)
latency E’ cannot be measured; but may be determined using simulation tools
latency A = latency A’
latency B = latency B’ – delay F’minusD’
delay C = delay C’
latency D = latency D’
latency E = latency E’
This is only if we cannot get D’ from Micron. Is that correct?
F’minusD’

## Slide 11: Approach for Challenge D’
latency D’ = latency G’ – delay F’minusD’ = latency G’ – (VirtualMC module latency + HMCC module latency + HMC link latency)
Latency G’ (round-trip)
  Collaborating with Convey to debug PERFMON code
VirtualMC module latency
  Implemented as TLB (Translation Look-aside Buffer) in code
  Non-deterministic
  Will collaborate with Convey
HMCC module latency
  Collaborating with Altera
F’minusD’

## Slide 12: Approach for Challenge G’
PERFMON
  PERFMON view of Merlin platform
  Hardware monitor designed by Convey
Notes: Pers_PERFMON an MC_PERFMON are verilog module names

## Slide 13: Approach for Challenge G’ (Contd.)
Roadblock
  Total LD latency measured in PERFMON code (189,232 cycles) inconsistent with latency measured in app HT code (742 cycles)
  Consulted with Convey: PERFMON code collects other memory accesses (including host, infrastructure) in addition to memory accesses from app (HT code)
Notes: Results measured by PERFMON code not what we needed (not incorrect)
Figures shows F’ measured in PERFMON is consistent with F’ measured in HT code
Now we have determined F’, in a similar manner, we can determine G’.

## Slide 14: Approach for Challenge G’ (Contd.)
Solution
  Found method to isolate memory accesses (modified PERFMON code)
  Validated modification by comparing measured F’ (from PERFMON) against F’ measured in application HT code
  Similarly, we can apply modification to measure G’
measured in modified PERFMON
measured in app (HT)
Notes: Results measured by PERFMON code not what we needed (not incorrect)
Figures shows F’ measured in PERFMON is consistent with F’ measured in HT code
Now we have determined F’, in a similar manner, we can determine G’.

## Slide 15: VirtualMC module latency
  Will collaborate with Convey
  How we understand the problem (from analyzing infrastructure code):
    TLB translate virtual memory addresses to physical addresses
    Delay is not consistent (e.g., long delay can be caused by TLB miss)
    Possible solutions:
      Statistical model?
      Increase page-table size to minimize TLB misses?
Notes: TLB Translation Lookaside Buffer – a memory cache to translate virtual address to physical address

## Slide 16: Benchmarking for A, B, C, and F
A’ is measured in host code
B’, C’, F’ are measured in HT code
latency D’ = latency G’ – latency G’_D’ = latency G’ – (VirtualMC module latency + HMCC module latency + HMC link latency)
latency E’ cannot be measured; but may be determined using simulation tools
F’minusD’

## Slide 17: Benchmarking Results: Single Mem. Rd/Wr
Operations | A’ (ns) | B’ (cycles) | C’ (cycles) | F’ (cycles)
Single memory read | 1058559 | 168.4414 | 4 | 164.4414
Single memory write | 1057302 | 175.6587 | 4 | 171.6587
A’ is measured inside the host application using timers
B’, C’ and F’ are measured inside the HT code.

## Slide 18: Measure B’
B’ is measured in HT code
  Starting point of CMC
  Ending point of CMC
starting time of B’
ending time of B’
latency B’
Operations | A’ (ns) | B’ (cycles) | C’ (cycles) | F’ (cycles)
Single memory read | 1058559 | 168.4414 | 4 | 164.4414
Single memory write | 1057302 | 175.6587 | 4 | 171.6587

## Slide 19: Measure C’
starting time of B’ & C’
latency C’
ending time of C’;’
C’ is measured in HT code
  Starting point of CMC logic
  Ending point of CMC logic
Operations | A’ (ns) | B’ (cycles) | C’ (cycles) | F’ (cycles)
Single memory read | 1058559 | 168.4414 | 4 | 164.4414
Single memory write | 1057302 | 175.6587 | 4 | 171.6587

## Slide 20: Measure F’
ending time of C’;
starting time of F’
ending time of B’
latency F’
F’ is measured in HT code
  Point of issuing memory request
  Point of receiving memory response
Operations | A’ (ns) | B’ (cycles) | C’ (cycles) | F’ (cycles)
Single memory read | 1058559 | 168.4414 | 4 | 164.4414
Single memory write | 1057302 | 175.6587 | 4 | 171.6587

## Slide 21: Going Forward (CAW16)
Complete performance measurement on Merlin board for single-memory operation
  Finish measurement of latency HMCC, latency G’, latency F’_D’, latency VirtualMC
Map results to model of envisioned CMC architecture
Apply lessons learned to conduct experiments to measure DRE apps
Let’s discuss