## Slide 1: Research Platform for Custom Memory Cube
Yu Zou
Graduate Student (Research Assistant)
Dr. Herman Lam
Assoc. Professor of ECE
University of Florida

## Slide 2: Outline
Introduction: Hybrid Memory Cube (HMC)
Motivation and goals for CMC research platform
HT Programming
  Hybrid-threading toolset
    Architecture
    Data structures
    Data access patterns
  HT code example
    Vector add
HT Demo
  Bloom filter

## Slide 3: Outline
Introduction: Hybrid Memory Cube (HMC)
Motivation and goals for CMC research platform
HT Programming
  Hybrid-threading toolset
    Architecture
    Data structures
    Data access patterns
  HT code example
    Vector add
HT Demo
  Bloom filter

## Slide 4: Introduction
Hybrid memory cube
  High-performance RAM interface for through-silicon vias (TSV)-based stacked DRAM memory
  Logic base (layer)
High bandwidth
  ~10% energy per bit of current DDR memories

## Slide 5: Advantage of HMC
High bandwidth comes from internal parallelism
  Vaults can be accessed in parallel
  Banks can be accessed in pipeline
But not enough ! ! !
  Pins constrain max. bandwidth
  Bottleneck for data-intensive
  apps
    Big data, e.g. PageRank
    Gnome research, e.g. DNA
    sequencing

## Slide 6: Custom Memory Cube (CMC)
Motivation
  Increasing need for fast high-performance parallel processing
  Memory accesses of data-intensive apps consumes considerable time
  Near memory processing or in-memory processing
DRAM Layers
Logic Layer
CPU
CMC
Data Processing

## Slide 7: High Bandwidth of CMC
HMC configuration
  16 HMCs are chained together
  Size – 8 GB
  64 bit vertical interface each DRAM partition
  32 vaults per cube
  TSV signaling rate 2 Gb/s
  8 high-speed external serial links
Available external bandwidth – 320 GB/s
Available internal bandwidth – 8 TB/s
25x

## Slide 8: CMC Research Platform
Create initial prototype of CMC arch using FPGA+HMC
Explore perf. measurement methods for CMC platform
Research perf. modelling for notional CMC architecture
Initial case study CMC app
Create research platform for design-space exploration CMC apps & arch (C-RAM* & PIM**)
Goal
*C-RAM: Computational RAM
**PIM: Processor In Memory
Motivation
Memory-intensive apps: memory bottleneck & high energy consumption
HMC: higher B/W & lower power than current memories
Potential for C-RAM* & PIM** processing (CMC)
Approach

## Slide 9: Notional CMC Architecture*
Based on Nair et al.* : an HMC with a user-programmable logic layer
A, B, C, D, and E: performance-measurement points of interest
* Nair, R., et al. "Active Memory Cube: A processing-in-memory architecture for exascale systems.“ IBM Journal of Res. & Development 59.2/3 (2015): 17-1.

## Slide 10: Performance Measurement on Merlin Board
CMC platform on Merlin board
*
Instrumented Merlin infrastructure with hardware performance monitors
  A’, B’, C’, D’, M1, M2, M3, M4, M5, and E’
VB*: View Buffer

## Slide 11: Mapping Notional CMC onto Merlin Board
Simplifying assumption:
For this model, this part of CMC is assumed to have an HMC architecture
Merlin board
Case study: model of a notional CMC

## Slide 12: Model of CMC-to-Merlin Mapping
      Latency A = ctrl signal transfer time B + latency C + result transfer time B
      Ctrl signal transfer time B : time to transfer control signals between host and CMC
      Data transfer time B: time for host access to obtain result (e.g., transfer from view buffer)
      Latency C = delay TSV* + latency C’ – delay D’minusE’
      Delay D’minusE’ = latency D’ – latency E’
      * delay TSV= between DRE core and switch, time to transfer a request +
      time to transfer response of that request
Model of notional CMC
Latency: round-trip delay from input into a point in the system to desired outcome
CMC platform on Merlin board

## Slide 13: Advantage of Platform
Fast prototyping
Short emulation time
  PageRank
  2^20 vertices, floating data
  SystemC simulation: 10~15 minutes
    Easy to change
    Slow validation
    Not accurate performance prediction
  CMC platform emulation: less than 1 minutes
    4+ hours to generate bitfile
    Quick validation
    Accurate performance prediction

## Slide 14: Outline
Introduction: Hybrid Memory Cube (HMC)
Motivation and goals for CMC research platform
HT Programming
  Hybrid-threading toolset
    Programming Model
    Data structures
    Data access patterns
  HT code example
    Vector add
HT Demo
  Bloom filter

## Slide 15: Convey HT Background
Convey computers
  Startup since 2006, based @ Texas
  Hybrid-core computing platforms
  Joined CHREC in 2013
    Via F3, focusing on bioinformatics app acceleration
Convey system philosophy – hybrid-core computing
Features | Convey
Programming | C/Cpp/ASM + HT + (HDL)
Data Addressing | explict, consistent
Host Connection | PCIe 2.0/3.0
HT : Hybrid threading - Convey’s HLS-like programming tool

## Slide 16: Overview of HT Programming Model
Application “call-graph” structure

## Slide 17: HT Infrastructure
Host-coproc. strucutre
  Message/Data interfaces
HT unit
  Replication mechanism
HT module
  Essential functional blocks
  Memory hierarchy
  Can be replicated
  Messaging interfaces among modules
Instructions
  User-defined behaviors of modules

## Slide 18: HT Toolset
Supported variable type
  Private variable
  Shared variable
  Global variable
Supported data type
  uint64_t, uint32_t
  ht_uint1_t, ht_uint2_t, …, ht_uint64_t
  ht_int1_t, ht_int2_t, … , ht_int64_t

## Slide 19: User Programmable Parts
Host source files
  Define program behaviors on the host, including data transmission, control flow, user interface, etc.
Hardware description files (.htd)
  Declare modules, variables, memory interfaces, etc.
Module instruction files (.cpp)
  Define behaviors of modules, including memory I/O, messaging interface, computation, etc.

## Slide 20: High-level Design Flow

## Slide 21: HT Code Example
HT
Personality with HT
A
Personality
Fn1
Fn2
Fn3
Fn4
HT tool flow
B
HT Example: Vector-add personality
Vadd Pers.
Control (CTL)
ADD
Ctl.htd
PersCtl_src.cpp
Host message
Variable declaration
Module I/O definition
Interface to other modules
Thread control
Call to ADD module
1 thread
C
Add.htd
PersAdd_src.cpp
128 threads
Memory interface
Memory Operations
Addition

## Slide 22: HT Demo – Spell Checker
Algorithm: Bloom filter
  Function: to train a filter, which can report whether an item was seen before or not
Use case: spell checker
  Use a dictionary to train a filter
  Use the trained filter to check a input word
    If it was seen before (i.e. it exists in the dictionary), it is reported as a correct spelling
    If not (i.e. it doesn’t exist in the dictionary), it is reported as a wrong spelling