## Slide 1: Reconfigurable Supercomputing @CHREC
Herman Lam
Associate Director, CHREC
University of Florida

## Slide 2: Outline
Elevator Overview (30 – 40 secs. each)
RSC* Research on Novo-G
  Real-Time, Feature-based Object Recognition
  Behavioral Emulation for Future-Gen Systems
  Sparse-Matrix Processor for Graph Apps
  Reconfigurable Interconnects, Novo-G#
HLS** Studies
  OpenCL vs. VHDL: Performance & Productivity Comparison
  CMS+ Endcap L-1 Muon Trigger: Making a Case for HLS
HMC+ Studies
  CMC: Custom Memory Cube
*Reconfigurable Supercomputing
**High-level Synthesis
+Hybrid Memory Cube
SC15 Booth 207 (www.chrec.org)

## Slide 3: Real-Time, Feature-based Object Recognition
Feature match
Feature Extraction
& Segmentation
Feature
Description
Feature Matching
& Classification
Goal: Develop power-efficient hardware architecture for onboard image processing
Motivation: Unsupervised decision making essential to many domains (safety, cost)
Mean-Shift unsupervised image segmentation algorithm
    SURF feature extraction; Canny & Sobel edge detection
    SURF feature-based object classification (future work)
  Object recognition: organize labeled features using a balanced kd-tree
  Extracts scale-invariant features @ 280fps (Altera Stratix-V FPGA)
  Describes scale- & rotation-invariant features @ 140fps (Stratix-IV)

## Slide 4: Behavioral Emulation for Future-Gen Systems
  Analytical studies
  Software simulation
  Behavioral Emulation
  Cycle-accurate emulation
  Prototype device
  Prototype system
How to study future notional devices, nodes, & systems, up to Exascale without an existing Exascale system
Goal & Motivation
Approach
Manage Exascale complexity via Behavioral Emulation (BE)
Coarse-grained, multi-scale simulation approach to balance accuracy, speed, & scalability
BE Process
BE Platforms
SST*based BE platform
Experimental testbed to support algorithm DSE+ on future-gen archs
NGEE** BE platform
BE acceleration via FPGAs
*SST: Structural Simulation Toolkit, Sandia National Lab
**NGEE: Novo-G Exascale Emulation +DSE: Design-Space Exploration

## Slide 5: Sparse-Matrix Processor for Graph Apps
Goal: Develop scalable architectures
for accelerating graph processing in
the language of linear algebra
Motivation: Traditional architectures are poorly suited for the sparsity of graph datasets
Approach
  Develop custom architectures for distributed SpGEMM
  Scale to multiple FPGAs leveraging Novo-G# interconnect
SpGEMM – Sparse Generalized Matrix/Matrix Multiplication
Adjacency Matrix Representation
FPGA-accelerated Operations
Accelerated Graph Algorithms
Outcomes
  Developed optimized storage format and data-distribution techniques
  Developed single-processor FPGA architecture for accelerated SpGEMM

## Slide 6: Reconfigurable Interconnects for Novo-G#
Goal: Enable large-scale app acceleration with a reconfigurable 3D-torus network
Motivation: Large-scale RSC apps are communication-bound
  Turn communication-bound problems into computation-bound problems
Approach
  Novo-G# network design to support multi-FPGA apps efficiently
    40 Gbps link support, <10% FPGA util.
  Modeling & simulation of novel topologies, architectures & protocols
    Scalable, accurate VisualSim model avail.
  OpenCL support for productive multi-FPGA development
    BSP* with inter-FPGA channel support avail.
Novo-G#
64 Gidel ProceV (Stratix V D8)
3D torus or 6D hypercube
6 Rx-Tx links per FPGA
4x 10 Gbps per link
ProceV board
3D torus network stack
*BSP: Board-support package

## Slide 7: Outline
Elevator Overview (30 – 40 secs. each)
RSC* Research on Novo-G
  Real-Time, Feature-based Object Recognition
  Behavioral Emulation for Future-Gen Systems
  Sparse-Matrix Processor for Graph Apps
  Reconfigurable Interconnects, Novo-G#
HLS** Studies
  OpenCL vs. VHDL: Performance & Productivity Comparison
  CMS+ Endcap L-1 Muon Trigger: Making a Case for HLS
HMC+ Studies
  CMC: Custom Memory Cube
*Reconfigurable Supercomputing
**High-level Synthesis
+Hybrid Memory Cube

## Slide 8
Experimental Setup
VHDL design flow
  Gidel ProceV-D8
OpenCL design flow
  Gidel ProceV-D8, Nallatech P385-D5, Bittware S5-PHQ-D8, Altera OpenCL 14.0
OpenCL* vs. VHDL
Performance & Productivity Comparison
HDL Design Flow
Low-level HDL at RTL level
Design verification (cycle-accurate simulation using HDL testbenches)
Place & route: hours+
Limited number of turns-per-day
OpenCL Design Flow
C-like syntax for FPGAs
Functional verification of project
Synthesis and PAR performed after kernel code is finalized
Increase number of turns-per-day
Conclusions - OpenCL:
Offers more productive design flow
Generates comparable clock frequencies
Uses more resources
Code portable across different platforms
*Altera OpenCL
Design
Productivity
Kernel design time
  VHDL: 6 months
  OpenCL: 1 month

## Slide 9: CMS* Endcap L-1 Muon Trigger Making a Case for HLS
*CMS (Compact Muon Solenoid) experiment
at The Large Hadron Collider, CERN
  Peta-bytes of data on every bunch crossing @40MHz (every 25 ns)
  FPGA-based design to reduce event rate to ~100KHz
Challenges
  Current version in Verilog (HDL)
  Took several years
  > 4000 lines
  Development & maintenance
  Complexity rapidly increasing
  Verification for scientists
  Manually converted to C++
  Increasingly difficult & inconsistent
Goal
  Explore use of HLS languages & tools for next-gen CMS code
Outcomes
  Very promising thus far
  Vivado HLS C/C++ entry improved productivity
  Hardware optimization via HLS a challenge
  Verification: C++ code can be compiled using g++ compiler
  No need for manual conversion from HDL
  Design tool: Vivado HLS
  Xilinx Virtex-7 XC7VX690T

## Slide 10: Custom Memory Cube (CMC)
Goal: Explore potential of customizable logic layer for HMC
    Concepts of C-RAM* & PIM** (e.g., SIMD, ARM64, & RISC-V in logic layer)
Approach: Prototype CMC using FPGA/HMC boards
FPGA/HMC boards
    Convey Merlin (MA-100)
    PICO EX500 w/ AC510 modules
Software simulators
    Gem5
    Goblin core64
    SST+
Testbeds for CMC Research:
Processor testbeds
    JUNO ARM64 development platform
    RISC-V: Rocket Core on Zedboard
*C-RAM: Computational Memory **PIM: Processor in Memory
+SST: Structural Simulation Toolkit, Sandia National Lab

## Slide 11: Conclusions
Much going on !!
In reconfigurable supercomputing
@ CHREC
Come see us!!
SC15 Booth 207 (www.chrec.org)
Novo-G#